## Slide 1: D0.2 Active Scanning comments discussion
Date: 2013-01-16
Authors:

## Slide 2: Abstract
The presentation discusses on the D0.2 active scanning related technical comments resolutions.
All the comments are briefly described and some topics of the comments are discussed in details.

## Slide 3: Comments classicification
Controversial comments: (discussed in the presentation)
  10.1.4.2 Active scanning procedure of the scanning STA
    MLME_SCAN.confirm reporting with SUCCESS CID254, CID263
    FILS capable and legacy STA operations are not clear with steps e) and f) CID274, CID275
  Clarification on criteria to response with Beacon CID 281
  Transmission of the Probe Request to individual address CID 262
Non-controversial issues (not discussed in this presentation)
  RX Power usage in response criteria, CID272
  Incomplete IF condition, not referencing to any value CID283
  INTERMEDIATE_SCAN_RESULTS reporting CID276
  Broadcasted Probe Response transmission to only FILS capable devices, CID267, CID282
  Duplicate text, CID122, CID279
  Including BSSID to probe request with AP Configuration Count CID284
  10.1.4.2 Referencing to FILS specific operation CID273

## Slide 4: 10.1.4.2 Active scanning procedure of the scanning STA
Reporting with SUCCESS CID254, CID263
  Why is ResultCode set to SCAN_SUCCESS without any "conditions“
  are there any cases where the ResultCode is not "Success“
  Cannot find any reasons to mandate MLME-SCAN.confirm primitive with "Resultcode set to SCAN_SUCCESS". On the other hand, if it is always set to Success, then the ResultCode is no longer needed.

## Slide 5: 10.1.4.2 Active scanning procedure of the scanning STA
Reporting with SUCCESS CID254, CID263
Discussion:
  The ResultCode is always present in the current MLME primitive
  Some value needs to be specified for the ResultCode. Leaving result code unspecified would be only done in scanning operation
  The SME knows if it has commanded SCAN-STOP, no need to propose other value
  The comments do not propose other solution to set the ResultCode
Recommended resolution:
  Continue to set ResultCode to Success

## Slide 6: 10.1.4.2 Active scanning procedure of the scanning STA
Issues with steps e) and f) CID274, 275
  If the first "If" condition in step e) is met, then a STA may execute “set NAV to 0 and scan the next channel” twice (once in step e then in step f again)
  The added text is out of order and only applies to STAs with dot11FILSActivated is true.
Slide 6

## Slide 7: 10.1.4.2 Active scanning procedure of the scanning STA CID 274
Discussion CID 274 The duplicate reference to the SET NAV 0 may be avoided by setting the STA to go to step f)
    Also the repetition of the reporting option description is avoided.
  The proposed resolution to CID274 is very long and hard to read:
  Change step e) to the following: "If PHY-CCA.indication (busy) primitive has not been detected before the Probe Timer reahces MinChannelTime, then set NAV to 0 and scan the next channel, else process any received probe responses, and any received beasons if dot11FILSActivated is true in the STA, until ProbeTimer reaches MaxChannelTime. If ReportingOption is IMMEDIATE and new AP or new information of the AP is detected, issue MLME-SCAN.confirm primitive with the ResultCode equal to IMMEDIATE_SCAN_RESULT and the BSSDescriptionSet containing information of the detected AP. wWhen ProbeTimer reaches MaxChannelTime, process all received probe responsesif dot11FILSActivated is true in the STA and if the ReportOption is Channel_Specific, issue an MLME-SCAN.confirm primitive with the ResultCode either equal to SUCCESS if the scanned channel is the last channel, or equal to INTERMEDIATE_SCAN_RESULT otherwise, and with the BSSDescriptionSet containing information of all APs that have been discovered from the scanned channel but have not been reported yet."

## Slide 8: 10.1.4.2 Active scanning procedure of the scanning STA
Issues with steps e) and f) CID275
  The added text is out of order and only applies to STAs with dot11FILSActivated is true.
Discussion:
  It is true that reporting option MLME-INTERMEDIATE_SCAN_RESULT is new and only applicable to FILS capable STAs
  The MLME-INTERMEDIATE_SCAN_RESULT is used in other places of hte standard as well
    Where to put definition that only FILS Capable STAs may use this reporting option?
      MLME is not typically describing capabilities
      Active Scanning procedure just specifies the operation for MLME commands, no capabilities are defined in these clauses
      PICS are typically indicating capabilities, but we do not have them yet and they should not be the only source for capability
Resolution: Submission needed to describe the non-FILS and FILS capable STAs operation

## Slide 9: 10.1.4.2 Active scanning procedure of the scanning STA
Issues with steps e) and f) CID276
Discussion:
  It is true that reporting option MLME-INTERMEDIATE_SCAN_RESULT is new and only applicable to FILS capable STAs
  The MLME-INTERMEDIATE_SCAN_RESULT is used in other places of hte standard as well
    Where to put definition that only FILS Capable STAs may use this reporting option?
      MLME is not typically describing capabilities
      Active Scanning procedure just specifies the operation for MLME commands, no capabilities are defined in these clauses
      PICS are typically indicating capabilities, but we do not have them yet and they should not be the only source for capability

## Slide 10: Clarification on criteria to response with Beacon CID 281
Text in standard:
STAs with dot11FILSActivated equal to true should respond to one or more Probe Request frames addressed to broadcast address with a Beacon frame if the criteria below are met:
  — The responding STA that is about to transmit a probe response receives an acknowledged Probe Response addressed to the requesting STA containing information of the BSS of the responding STA.
  — The next TBTT of the responding STA is within dot11BeaconResponseDuration and is no later than any deadline of Probe Response Reception Time, if the Probe Response Reception Time element is present in any Probe Request frame.
Comment:
  There are two criteria. It is not clear whether the condition is all criteria must are met or any criteria is met. Not sure why the first criteria?

## Slide 11: Clarification on criteria to response with Beacon CID 281
Discussion:
  The first condition is avoiding repetition on the parameter values transmission to the scanning STA
  The second condition is needed to be able to response with Beacon instead of Probe Response when TBTT is soon after the received probe response
  Both conditions avoid unncessary Probe Response frames transmission
  The first criteria could be more precise and define the information that is given from the AP
Resolution:
  Submission needed to specify the first condition in more details i.e. Specify the required information in details

## Slide 12: Transmission of the Probe Request to individual address CID 262
Comment:
  The Figure 10-3c describes the case where the Probe Request is sent to an individual address of an AP. However, this case is actually not a valid case in the current active scanning procedure, as the probe request is always sent to the broadcase destination address
Discussion:
  It is true that individual address usage for the legacy STAs is not specified (in details)
  Usage of the individual address in probe request is desireable
    Reduces the number of probe response frames

## Slide 13: Transmission of the Probe Request to individual address CID 262
Resolution alternatives:
  Deny the use of individually addressed probe request from non-FILS STAs
  or continue with the text currently present and allow individually addressed Probe Request transmission for all STAs

## Slide 14: References