## Slide 1: Text for active scanning procedure of the scanning STA
Date: 2013-01-18
Authors:

## Slide 2: Comments:
The presentation provides resolution text for CIDs 274, 275 and 276.
Issues with steps e) and f) CID274, 275 and 276
  If the first "If" condition in step e) is met, then a STA may execute “set NAV to 0 and scan the next channel” twice (once in step e then in step f again)
  The added text is out of order and only applies to STAs with dot11FILSActivated is true.

## Slide 3: Text to be changed:

## Slide 4: New text
e) If PHY-CCA.indication (busy) primitive has not been detected before the Probe Timer reaches MinChannelTime, then go to step f), else while the Probe Timer is less than the MaxChannelTime:
1. process any received probe responses;
2. process any received beacons if dot11FILSActivated is true in the STA; and
3. If dot11FILSActivated is true in the STA, ReportingOption is IMMEDIATE, and new AP or new information of the AP is detected, issue MLME-SCAN.confirm primitive with the ResultCode equal to IMMEDIATE_SCAN_RESULT and the BSSDescriptionSet containing information of the detected AP.
If dot11FILSActivated is true and the ReportingOption is CHANNEL_SPECIFIC, issue at the time when the Probe Timer reaches the MaxChannelTime an MLME-SCAN.confirm primitive, with the ResultCode equal to SUCCESS and the BSSDescriptionSet containing information of all APs that have been discovered from the scanned channel.
f) set NAV to 0 and scan the next channel.