## Slide 1: FILS Handling of Large Objects, FILS Piggy-Backing
Date: 2013-05-13 (WORKING DRAFT ONLY!!!)
Authors:
Name | Company | Address | Phone | email
René Struik | Struik Security Consultancy | Toronto ON, Canada | USA: +1 (415) 690-7363 Toronto: +1 (647) 867-5658 Skype: rstruik | rstruik.ext@gmail.com

## Slide 2: FILS Key Establishment
STA
AP
Association Request
Beacon/Probe Resp.
Authentication Request
Authentication Response
Association Request
Key
Establishment
Key
Confirmation
TTP
online/offline assistance
with authentication
FILS key establishment protocol options provided:
FILS Authentication with TTP, based on ERP
(two flavors: with or without “PFS” (ERP+ECDH, resp. ERP)  see next slides)
Authentication without online TTP, based on ECDH and ECDSA certificate
Slide source: 13/324r0

## Slide 3: Adding “piggy-backed info” to protocol flows …
STA
AP
Association Request
Beacon/Probe Resp.
Authentication Request
Authentication Response
Association Request
Key
Establishment
Key
Confirmation
TTP
Services
+ piggy-backed info response
+ piggy-backed info request
Authentication help
Configuration help
IP address assignment
Authorization
Subscription
credentials
Piggy-backing info along FILS authentication protocol:
Higher-layer set-up, including IP address assignment
Authorization functionality, subscription credentials, etc.
See details elsewhere in presentation
Slide source: 13/324r0

## Slide 4: FILS Security Status
Current Status:
Three FILS authentication protocol options specified:
  FILS Authentication with Trusted Third Party
  FILS Authentication with Trusted Third Party and “PFS”
  FILS Authentication without Trusted Third Party
Main differences:
  Different trust assumptions
  Different assumption on “pre-existing” system set-up
  Different assumptions on online availability of the “backbone network”
Common elements:
  All have only four protocol flows
  All implemented via Authentication/Association Request/Response frames
  All allow piggy-backing of other info along Association frames
  (e.g., IP address assignment)
Current Work in Progress:
How to deal with large objects (e.g., certificates, higher-layer data objects)
How to specify main piggy-backing details (e.g., on IP address assignment)
Slide source: 13/324r0

## Slide 5
Questions
1. How to deal with large objects (e.g., certificates, higher-layer data objects)?
Intra-frame fragmentation.
How to handle large objects that fit within a single frame
Inter-frame fragmentation.
How to fragment FILS frames, if these become too long due to large objects
2. How to specify main piggy-backing details (e.g., on IP address assignment)?
Flexibility re AEAD authenticated encryption mode.
Authentication and potential encryption of piggy-backed information

## Slide 6
Frame Fragmentation (802.11-2012)
Conceptual Channel
802.11 Channel w/Fragmentation
Notes:
Header contains Sequence Control Field that indicates fragment# (4-bits) and sequence # (12-bits)
Originator (A) partitions frame body and sends individual segments in separate frames, in order
Recipient (B) reconstructs original (conceptual) frame from received segments, in order
When secure channel used, each segment is individually secured (by originator) or unsecured (by recipient)
Duplicate segments and segments received after time-out are acknowledged
802.11-2012 allows fragmentation/defragmentation with individually addressed MSDUs and MMPDUs
HDR
Body
FCS
A
B
HDR1
Body1
FCS1
A
B
Body3
FCS3
Body2
FCS2
A
A
B
B
HDR2
HDR3

## Slide 7
Use of Existing 802.11-2012 Frame Fragmentation with FILS
Indeed possible, FILS protocol does not use 802.11-2012 frame protection
Doesn’t this cause Denial-of-Service Attacks?
With TTP:
AP needs to keep state on Auth Request received from STA till moment it receives verdict back from TTP;
AP may need to keep state longer, till it received and processed Assoc Request from STA (prior to key confirmation, there is no evidence that STA was indeed alive)
Without TTP:
AP may need to keep state till it received and processed Assoc Request from STA (prior to key confirmation, there is no evidence that STA was indeed alive)
Conclusion:
With either FILS scheme, AP needs to keep state till it received and processed message flow #3 (Assoc Request aka key confirmation) from STA.
Without TTP, time window during which AP needs to keep state may be shorter than if back-end TTP communication required, depending on implementation details.

## Slide 8
Doesn’t this cause Denial-of-Service Attacks? (cont’d #1)
Effect of fragmentation
FILS initiated by single STA sending fragmented Auth Request with 3 fragments:
AP: keep 1 record; correspond with up to 1 TTP; perform 1 computation
FILS initiated by 3 STAs sending short, non-fragmented Auth Request only:
AP: keep 3 records; correspond with up to 3 TTPs; perform 3 computations
Conclusion:
In terms of resource consumption, Denial-of-Service attack scales at most linearly with
number of STAs or with maximum # of fragments in Auth frame.

## Slide 9
Doesn’t this cause Denial-of-Service Attacks? (cont’d, #2)
Effect of authorization
AP may need to maintain state longer, if ultimate verdict on access based on both
Authentication of STA;
Authorization of STA.
Time window to reach authorization decision determines DoS attack time window.
Hence, beneficial to
get early-on insight into credential validity (e.g., certificate verification so as to know who STA is)  communicate certificates early-on (in Auth Req/Resp) helps
get early-on insight into authorization decisions (e.g., by third party)  “aggressive mode” piggy-backing (w/ some stuff in Auth Req/Resp.) helps as well
Conclusion:
In real life, there are limits to time-bounded local resource allocation to handle n STA
join request. Having modest (say, at most three) # fragments does not impact this a lot.

## Slide 10
Frame Fragmentation – Straw Poll #1
Use existing frame fragmentation mechanism (802.11-2012) to handle frames that
would otherwise not “fit”.
Yes
No
“Don’t Care”
Need more information
Result:

## Slide 11
Intra-Frame Fragmentation with FILS (1)
Conceptual Object
802.11 Representation as Sequence of Information Elements
Conversion mechanism:
Represent single object/multiple objects within single frame
Allows recovering of original object from representation
Works also if object spread over multiple frames
Allows reconstruction as soon as segments all received
Note: This allows full flexibility on how one could carry objects within a single and across multiple frames
Body
255
Body1
Body3
Body2
255
77
176
176
176
IE1
IE2
IE3
1
1
255
255
77
587
Foreign object:
may live outside 802.11
syntax/semantics unknown
to 802.11
e.g., DHCP, Higher Layer, IP
Large object:
may not fit within single IE
e.g., Certificate chain
Represent as ordered
sequence of IEs
“piggy-backing” possible
“squeezing” large objects
into frame possible
“spreading” large objects
over several frames too…
Requires one new IE

## Slide 12
Intra-Frame Fragmentation with FILS (2)
Conceptual Object
802.11 Representation as Sequence of Information Elements
How to recover objects?
Within single frame: separator symbol (‘’) allows unique recovery of multiple objects
Object spread over multiple frames: parse till ‘’-symbol found (assuming only one object to spread across)
Note:
Up to implementation to partition to one’s needs
Representation with multiple ‘’-symbols in the end possible (“padding”)
Body
255
Body1
Body3
Body2
255
77
176
176
176
IE1
IE2
IE3
1
1
250
255
77
587
0
176
IE4
end-of-object indicator (‘’,  EOF, etc.)
object “segments” (in order)

## Slide 13
Intra-Frame Fragmentation with FILS (3)
Applications:
Foreign object:
may live outside 802.11
syntax/semantics unknown to 802.11
e.g., DHCP, Higher Layer, IP (cf. D0.5, Section 8.4.2.186)
Large object:
may not fit within single IE
e.g., Certificate, certificate chain (“super-sized” public key IE, D0.5, 8.4.2.183)
Construct allows more than one foreign object/large object in single frame
Lots of flexibility in reducing likelihood of frame fragmentation (i.e., keeping FILS authentication to just 4 exchanges frames, even with certificates and piggy-backed info)
How to recover objects?
Within single frame: separator symbol (‘’) allows unique recovery of multiple objects
Object spread over multiple frames: parse till ‘’-symbol found (assuming only one object to spread across)
Note:
Up to implementation to partition to one’s needs
Representation with multiple ‘’-symbols in the end possible (“padding”)

## Slide 14
Intra-Frame Fragmentation – Straw Poll #2
Represent “conceptual objects” as described in 13/311r1:
Introduce new Information Element (IE) for “conceptual object” type
Have conversion routine for Object as sequence of IEs (and for sequence of Objects)
Yes
No
“Don’t Care”
Need more information
Result:

## Slide 15
Authenticated Encryption (1)
General mechanism
After AEAD protection
Now with Information elements:
or...
or...
or...
Main problem: How to pinpoint the portions that are encrypted? (only problem for recipient)
Header
Payload
Header
Secured Payload
Authentication of entire frame
0
7
1
3
4
6
5
8
9
A
0
7
1
3
4
6
5
8
9
A
0
7
1
3
4
6
5
8
9
A
0
7
1
3
4
6
5
8
9
A
Encrypted segments starts here

## Slide 16
Authenticated Encryption (2)
How to pinpoint the portions that are encrypted? (only problem for recipient)
Recipient can easily find this “L”-symbol: simply parse received message (and remove this “L”-symbol)
Does this also work for other “encryption ON/OFF” combinations?
0
7
1
3
4
6
5
8
9
A
0
7
1
3
4
6
5
8
9
A
0
7
1
3
4
6
5
8
9
A
L
0
7
1
3
4
6
5
8
9
A
“L”
1
1
2
2
L
“L”
2

Encryption length indicator IE
(4 octets)

## Slide 17
Authenticated Encryption (3)
Does this also work for other “encryption ON/OFF” combinations?
YES! Exploit structure in IEs: encryption/decryption is essentially on “unordered” set of IEs.
Step 1 @sender: massage in right form (split frame into “to be encrypted elements” and “other data”)
Step 2 @sender: encrypt and put “L”-symbol (encryption indicator IE) in place
0
7
1
3
4
6
5
8
9
A
0
7
1
3
4
6
5
8
9
A
0
1
3
6
8
9
7
4
5
A
Other
data
To be encrypted data
0
A
1
3
4
7
5
6
8
9
“L”

## Slide 18
Authenticated Encryption (4)
Step 1 @recipient: find encryption indicator, length of encrypted segment, decrypt and verify authenticity, and remove “L”-symbol
(NOTE: encryption indicator is always “on the left”)
Step 2 @recipient: massage “decrypted data” and “other data”, so that IEs will be in ascending order.
0
1
3
6
8
9
7
4
5
A
Other
data
Decrypted data
0
A
1
3
4
7
5
6
8
9
“L”
0
A
1
3
4
7
5
6
8
9
“L”
0
7
1
3
4
6
5
8
9
A

## Slide 19
Authenticated Encryption (5)
What about complexity?
Step 1 @sender: massage in right form (split frame into “to be encrypted elements” and “other data”)
Scan data from left to right and partition string according to “Encryption ON/OFF” indication
Step 2 @recipient: massage “decrypted data” and “other data”, so that IEs will be in ascending order.
Scan leftmost elements of two substrings and build combined string according to order IE Identifiers.
Step 2 @sender: encrypt and authenticate and put “L”-symbol (encryption length indicator IE) in place
Step 1 @recipient: find encryption indicator, length of encrypted segment, decrypt and verify authenticity, and remove “L”-symbol
0
7
1
3
4
6
5
8
9
A
0
1
3
6
8
9
7
4
5
A
Other
data
To be encrypted data
0
A
1
3
4
7
5
6
8
9
“L”
0
A
1
3
4
7
5
6
8
9
“L”

## Slide 20
Authenticated Encryption (6)
Summary:
Flexible authenticated encryption scheme:
Sender has full control over which portions to encrypt
(e.g., encryption of vendor-specific info, specific higher-layer objects)
Recipient can always decrypt-and-verify, irrespective of sender’s security policy
Limited incremental cost:
Requires new 4-octet information element (“encryption indicator element”)
This allows recipient to always easily find “encrypted data” and “other data”
Requires single left-to-right scan of string on sender’s and recipient’s side
Implementation cost scan operation insignificant:
*Scan on recipient’s side only after decrypt-and-verify, so no schedule impact
*Scan on sender’s side may be trivial and can be anticipated by sender
Notes:
AEAD scheme described has minimal complexity, in the following sense:
Any AEAD scheme where one cannot statically determine size and/or location of “encrypted data” from frame itself requires introduction of “encryption indicator IE”
Any scheme where one wishes to have “encrypted data” together, so that AEAD crypto inputs can be easily determined ,requires some type of “scan” operation

## Slide 21
Authenticated Encryption (7)
Summary:
Flexible authenticated encryption scheme:
Sender has full control over which portions to encrypt
(e.g., encryption of vendor-specific info, specific higher-layer objects)
Recipient can always decrypt-and-verify, irrespective of sender’s security policy
Implementation choices:
Any implementer who does not care about flexibility (i.e., its security policy is to always encrypts the entire frame), does not need to implement “scan” on sender’s
side. In that case, encrypt-and-authenticate coincides with usual CCM mode.
Any implementer whose incoming frame processing considers IEs as a set, i.e., unordered, does not need to implement “scan” on recipient’s side. In that case, decrypt-and-verify coincides with usual CCM mode.
Result: (“Best of both worlds”)
Implementers who do not like flexibility/generality can go their way
Implementation of “encryption indicator element” allows others who do like flexibility to go their way as well (“peaceful coexistence”)

## Slide 22
Authenticated Encryption (8)
Options:
1. No flexibility. Always encrypt FILS Association Request/Response “body”
2. Some flexibility. Allow only encryption of “first chunk”…
No re-ordering of IEs at all.
3. Full flexibility. Allow encryption of any chunks, as set by senders policy…
Potential re-ordering of IEs “under the hood”. Put “right” as part of AEAD routine.
Details in 13/311r1.
Header
Secured Payload
Header
Secured Payload
Visible Chunk
“L”
Header
Secured Payload
Visible Chunk
“L”

## Slide 23
Authenticated Encryption – Straw Poll #3
  Implement flexible encryption scheme as specified in 13/311r1:
  Introduce new Information Element (IE) as “security indicator element” (4-octets), so as to indicate length of encryption segment following
  Facilitate Option #2 of previous Slide (#22).
  For clarity: This only applies to FILS Association frames
Yes
No
“Don’t Care”
Need more information
Result: