## Slide 1: FILS Handling of Large Objects
Date: 2013-05-14
Authors:

## Slide 2: Abstract
A technique to fragment data that is too large to fit into one IE is presented
Technique also allows representation of higher-layer
encapsulation element

## Slide 3: IE Size Limitation
Section 8.4.2.1 of IEEE Std 802.11-2012 gives base format for an IE:
The Length field defines the length of the Information field
One octet Length means Information cannot be greater than 255 octets!
Some IEs have fixed components after the Length that further reduce the size of the Information field
Element ID
Length
Information
Octets: 1 1 variable

## Slide 4: Public Key Definition in P802.11ai D0.5
With a Key Type component (indicates certificate or 2 kinds of raw public key), the public key is limited to 254 octets!
  This may be acceptable for certain raw ECC public keys
  Too small for acceptable FFC public keys
  Too small for certificates (even those with ECC public keys)
Need some way to convey data > 255 octets using IEs that limit data to 255 octets!
Element ID
Length
Key Type
Octets: 1 1 1 variable
FILS Public Key

## Slide 5: Jumbo-IE
Stretches existing IEs by allowing larger length:
The Length field defines the length of the Information field
Size of Length field may depend on Element ID (i.e., no a-priori length limitation).
Jumbo-IE encoded, so as to avoid interpreting as existing IEs
Jumbo-IE encoded in backward-compatible way
Length of Jumbo-IE uniquely recovered during re-assembly
Multiple Jumbo-IEs uniquely recovered during re-assembly
Element ID
Length
Information
Octets: 1  0 variable

## Slide 6: Fragmenting Jumbo-IE into Separate IEs
Use a new Fragment IE
Jumbo-IE is represented by 1 or more Fragment IEs
  Re-assembly does not depend on details of Jumbo-IE
  Re-assembly of multiple Jumbo-IEs uniquely defined
Existing IEs not impacted
Fragment ID
Length
Fragmented Data
Octets: 1 1 variable

## Slide 7: Fragmenting Jumbo-IE into Separate IEs
3 FR IEs fragment Jumbo-IE (discarding length info)
All fragments except last one have length of 255 octets
(if necessary, add empty fragment)
Receipt of FR IE indicates start fragmentation
Reassembly Jumbo-IE stops with receipt length<255 FR IE
Reassembly does not depend on details Jumbo-IE
586 octets
FR
255
ID
Len
ID
FR
255
FR
77
FR
0
FR
0
Only add if all
fragments o.w. of
length 255 octets

## Slide 8: Fragmenting Jumbo-PK IE into Separate IEs
585 octets
FR
255
PK
KT
KT
Len
PK
FR
255
FR
77
3 FR IEs fragment Jumbo-IE (discarding length info)
All fragments except last one have length of 255 octets
(if necessary, add empty fragment)
Receipt of FR IE indicates start fragmentation
Reassembly Jumbo-IE stops with receipt length<255 FR IE
Reassembly does not depend on details Jumbo-IE

## Slide 9: Backwards Compatibility
IEEE 802.11-2012 says in section 8.3.3.1
  IEs have a fixed order in a frame
  IEs that are not understood are skipped over
Implications of IE ordering
  Cannot rearrange order of existing IEs
  New IEs can be defined to go in any order without affecting existing implementations
Fragment IE is special
  FR IE used as vehicle to transport Jumbo-IE only
  Re-assembly based on FR IEs only: no need to inspect Jumbo-IE details
Other
  No change of semantics of existing IEs
  FR IE can be used without impacting fixed order in a frame

## Slide 10: References
11-13-0311-02ai-Proposed-Resolutions-for-Assigned-Security-CIDs
Acknowledgement
Thanks to Paul Lambert who suggested the “trick” on
Slide 7 (that allows shaving off 2 octets of
representation in most cases)

## Slide 11
Intra-Frame Fragmentation – Straw Poll
Represent “conceptual objects” as described in 13/311r2:
Introduce new Information Element (IE) for “Fragment” type
Have conversion routine for “Jumbo IE” as sequence of Fragment IEs (and for sequence of such Jumbo IEs)
Yes
No
“Don’t Care”
Need more information
Result:

## Slide 12
Intra-Frame Fragmentation – Motion
Instruct the editor to incorporate changes to D0.5, as indicated in 13/311r2
Yes
No
Abstain
Result: Y/N/A