## Slide 1: CID 266 & CID 281
Date: 2013-03-08
Authors:

## Slide 2: Abstract
CID266 resolution is done erroneously. The resolution to the comment CID266 will cause a bloat of the Probe Response frames.
There is another comment CID281, that is not solved. CID281 proposes alternative resolution.

## Slide 3: Text related to CIDs
STAs with dot11FILSActivated equal to true should respond to one or more Probe Request frames addressed to broadcast address with a Beacon frame if the criteria below are met:
— The responding STA that is about to transmit a probe response receives an acknowledged Probe Response addressed to the requesting STA containing the BSS of the responding STA.
— The next TBTT of the responding STA is within dot11BeaconResponseDuration and is no later than any deadline of Probe Response Reception Time, if the Probe Response Reception Time element is present in any Probe Request frame.

## Slide 4: CID 266
Comment:
Following description is the condition of the Probe Request omission.
"The responding STA that is about to transmit a probe response receives an acknowledged Probe Response addressed to the requesting STA containing information of the BSS of the responding STA.“
The comment does not specify any reason, or justification for the change. It just points the place of the standard.

## Slide 5: CID 266
Proposed change:
”... with a Beacon frame if the criteria below are is met:
The responding STA that is about to transmit a probe response receives an acknowledged Probe Response addressed to the requesting STA containing information of the BSS of the responding STA. The next TBTT of the responding STA is within dot11BeaconResponseDuration and is no later than any deadline of Probe Response Reception Time, if the Probe Response Reception Time element is present in any Probe Request frame.”

## Slide 6: CID 266
Resolution code: ACCEPTED (EDITOR: 2013-01-16 21:43:51Z) Need to check results. In D0.3, this was a hyphenated list (a change from D0.2), this modification results in only a single item which does not justify a list format. In pondering the options, made it a continuation of the paragraph ending in "criteria below is met:" Please comment if there is a better way of doing this.
The comment is deleting a technical operation. The motivation and reasoning is to improve readability.
The readability improvement is not a justification for technical change.

## Slide 7: CID 281
Comment: “There are two critria below. It is not clear whether the condition is all criteria must are met or any criteria is met. Not sure why the first criteria?”
No proposed resolution.

## Slide 8: Why the first condition
— The responding STA that is about to transmit a probe response receives an acknowledged Probe Response addressed to the requesting STA containing the BSS of the responding STA.
Traditionally the same frame (Beacon or Probe Response) has been provided the link quality assessment as well as the information of the BSS. This information may be collected separately:
The devices may obtain the link performance information from any omni-directionally transmitted frame. When the congestion in the network increases, typically there are plenty of frames available for link assessment. For instance all ACK frames transmitted by the AP are suitable for link assessment.
The devices may obtain information of the BSS through a frame that is transmitted by other STA.

## Slide 9: Why the first condition
— The responding STA that is about to transmit a probe response receives an acknowledged Probe Response addressed to the requesting STA containing the BSS of the responding STA.
The condition enables a single response form the network to be transmitted to the scanning STA. This reduces the number of scanning frames transmission especially in the congested situations.
The scanning STA desires to discover the network, i.e. BSS having the same SSID. Typically these BSS use the same authentication mechanism. To initiate a link setup, it is important for a STA to discover that the network exists.
The condition defines a minimum response level is defined.

## Slide 10: Proposed text to
STAs with dot11FILSActivated equal to true should respond to one or more Probe Request frames addressed to broadcast address with a Beacon frame if either of the criteria below are is met:
— The responding STA that is about to transmit a probe response receives an acknowledged Probe Response addressed to the requesting STA containing information of the BSS SSID of the responding STA.
— The next TBTT of the responding STA is within dot11BeaconResponseDuration and is no later than any deadline of Probe Response Reception Time, if the Probe Response Reception Time element is present in any Probe Request frame.
The change is described in the document 13-210r1.
The resolution improves readability, the reduces the number of probe responses and clarifies the first response condition.