## Slide 1: Response Frame Indication
Date: 2013-3-18
Authors:

## Slide 2
Authors:

## Slide 3
Authors:

## Slide 4: Background
The concept of early ACK indication was proposed and accepted [1].
  Add two-bit Ack Indication in SIG field to indicate whether an immediate response is requested right after the PPDU, and also the type of the response (e.g. 00: Ack; 01: BA; 10: No Ack; 11: reserved)
  If a STA decodes the SIG correctly, but 1) decides to skip the remaining fields after SIG for power saving, or 2) is not able to decode /verify the MAC header, it can determine whether to defer medium access for Ack protection based on the Ack Indication in SIG
SIG
MH
Data
Ack
Ack Indication

## Slide 5: Background
Also, indication in SIG field further includes another frame type “Not ACK, CTS or BA” to further allow speed frame exchange [2]:
Response Frame (2-Bit) |  | Frame Types
0 | 0 | ACK
0 | 1 | BA
1 | 0 | No Response
1 | 1 | Not ACK, CTS or BA

## Slide 6: Issue
However, as IEEE 802.11 TGah allows multiple types of Ack frames, these classification may not work properly.
  There are normal ACK frame and also short ACK frame.
  There are normal Block ACK frame and also short Block ACK frame.
When a response frame indication is set to “00”, 3rd party STAs don’t know if normal ACK will follow or short ACK will follow.
Similar case will happen for Block ACK.
Therefore, 3rd party STAs cannot know exactly when to initiate channel access, and thus the benefit of using early Ack indication diminishes.

## Slide 7: Issue
To resolve this issue, the ACK indication may need to include the information on the duration of the response frame.
However, to enable this feature a transmitter needs to know which response frame a recipient will use in response to current transmission.
  Normal ACK/NDP ACK
  Normal BA/NDP BA
  Normal CTS/NDP CTS
  Etc

## Slide 8: Proposal
Non-AP STAs shall support NDP MAC control frames that can be used as a response frame (ACK, CTS, BA).
  A transmitter doesn’t need to figure out if a recipient can support those NDP MAC control frames or not.

## Slide 9: Proposal
An AP and associated STAs shall know preferred frame format of ACK, CTS, BA (normal vs. NDP) of each other by defining a mandatory rule in the spec. to use NDP frame unless other frame is needed.
  In case normal response frame is needed, both transmitter and recipient can figure out normal frame is used for the response frame without explicit information exchange.
  E.g.: Normal ACK shall be used in response to a frame with MRQ subfield in HT Control field is set to 1.

## Slide 10: Conclusions
Proposed a mechanism that a transmitter of a frame can figure out the type of response frame (NDP or normal) a recipient shall use.
Next step is to figure out how to redefine/set Ack Indication bits such that 3rd party STAs can defer the channel access properly.

## Slide 11: Straw Polls
SP1: Do you support that the following NDP MAC control frames are mandatory for Non-AP STAs?
  ACK, CTS, BA
SP2: Do you support that an AP and associated STAs shall know preferred frame format for ACK, CTS, and BA (normal vs. NDP) of each other by defining a mandatory rule in the spec. “to use NDP unless other frame is needed”.

## Slide 12: References
[1] IEEE 802.11-12/0119r0, Early Ack Indication
[2] IEEE 802.11-12/0834r0, Speed Frame Exchange