## Slide 1: PRAW Follow Up
Date: 2013-3-18
Authors:

## Slide 2
Authors:

## Slide 3
Authors:

## Slide 4: Sectorized Beam Operation for Spatial Re-Use
SFD R13 sectorized beam operation allows BSS AP-STA to Spatial re-use the medium with OBSS STAs and APs.
Significant network capacity enhancement in the moderately to highly overlapped BSS situation
AP1
STA1
Omni-Beam Duration
NAV
NAV
TXOP
Sectorized-Beam Transmit and Receiver Duration
AP1
STA1
SO OBSS STA2
SO OBSS AP2
OBSS STA3
Spatial Re-use by out-of-range OBSS STAs and APs
Note: SO (Spatially Orthogonal) OBSS STA/AP is defined as the OBSS STA/AP which can receive the omni transmission but not the sectorized transmission from AP1 and not the transmission from STA1

## Slide 5: Agenda – Open Issues
NDP for sector training is still TBD
Scheduling of periodic sector training within a beacon interval for Type 1 sectorization
Sector ID Feedback format is still TBD

## Slide 6: Proposed Sector Training NDP
Candidate short NDPs
Propose to use CTS NDP with Address Indicator set to 0 and RA set to partial BSSID for the sector training. The CTS NDPs with the Address Indicator set to 0 and RA set to partial BSSID will be transmitted through the Sectorized Beams (with assending Sector ID starting with Sector ID=0) during the sector training.
Note: STAs receiving the NDPs can identify the Sector ID via value in the Duration (relative to that of the NDPA)
Value | Meaning
0 | NDP CTS (control frame)
1 | NDP PS-Poll (control frame)
2 | NDP ACK (control frame)
3 | NDP Block ACK (control frame)
4 | NDP Beamforming Report Poll (control frame)
5 | NDP Probe Request (management frame)
6 | NDP Paging (management frame)
7 | Reserved
S. ID 0
NDP
NDP
NDP
NDPA
S. ID 1
S. ID N
+HTC

## Slide 7: Scheduling of Periodic Sector Training within a Beacon Interval
Sector Operation I.E. (Type 1) indicates which beacon intervals a periodic sector training occurs.
Further specification is needed to indicate the timing of sector training within a beacon interval.
AP
STA
… …
Beacon
Beacon
NDP
NDP
NDP
(P)RAW
NDPA
NDP
NDP
NDP
(P)RAW
NDPA
+HTC
+HTC

## Slide 8: Sounding RAW
During that Sounding RAW (to all AIDs or to some restricted AIDs), a non-AP STA having the corresponding AID, is prohibited to transmit anywhere (for reliable sounding), but may wake-up and hear the entire sounding
Due to this new behavior of STAs, which is not defined in the current RAW element, we need one bit indication (Sounding or not)

## Slide 9: Sounding RAW
Feature | Value | Interpretation
Page ID | 2 bits | Indicates the page index for hierarchical AID (based on hierarchical AID) of the allocated group
Block Offset | 5 bits | Assuming 32 blocks per page, these bits indicate the starting block index of the allocated group
Block Range | variable bits | Indicates the number of blocks (starting from the block offset) for the allocated group
RAW Start Time | 8 bits | Duration in TU from end of beacon transmission to RAW Start time
RAW Duration | variable bits | Duration of RAW in TU
Access restricted to paged STA only | 2 bits | Bit 1: Set to 1 if only STA with their TIM bit set to 1 are allowed to perform UL transmissions Bit 2: Set to 1 if RAW is reserved for frames with duration smaller than slot duration, such as PS-Polls / trigger frames (ignored if Bit 1 is not set)
Group/Resource allocation frame indication | 1 bit | Set to 1 to indicate if STAs need to wake up at the beginning of the RAW to receive group addressed frames such as resource allocation (format of the resource allocation frame TBD)
Sounding RAW | 1 bit | Set to 1 to indicate if non-AP STAs are prohibited to transmit but are allowed to listen the entire RAW Set to 0 otherwise
Slot definition | variable bits | Include Slot duration signaling Slot assignment to STA Cross boundary transmissions allowed/not allowed Format is TBD
RAW Parameter Set element

## Slide 10: Sector ID Feedback Format
In SFD (Spec Framework Document) 4.6.C 9, the Sector ID Feedback uses VHT Action frame with Sector ID Index still remained TBD
Order | Information
1 | Category
2 | VHT Action
3 | Sector ID Index (format TBD- see next chart)

## Slide 11: Proposed Sector ID Feedback Format
The proposed Sector ID Index format
  Preferred Sector ID: the sector that the STA receives highest quality AP signal
  SNR: received SNR at the preferred Sector, 0 to 31 represents SNR values -3 to 27 dB respectively. When the SNR value is greater than 27db, set to 30. If the SNR value is less than -3dB, set to 0. 31 indicates no feedback.
  Receive Sector Bit Map: 0 indicates that the station does not receive the AP signal in a specific Sector. The position of the bit map (0 to 7) corresponding to the sector ID. This allows the AP to know which sectors the STA are in.
Preferred Sector ID (3 bits)
Rcvr Sector Bit Map (8 bits = 8 sectors)
SNR (5 bits)
I
I
I
I
I
I
I
I
0
1
2
3
4
5
6
7
I=0/1, STA receives/does not receives signal (<-98 dBm) in the corresponding sector
Sector ID
AP
STA I=1,
Preferred Sector
I=0
I=0
I=0
I=0
I=0

## Slide 12: Straw Poll 1
Do you support to use CTS NDP with Address Indicator set to 0 and RA set to Partial BSSID for sector training. The CTS NDPs with the Address Indicator set to 0 and RA set to Partial BSSID will be transmitted through the Sectorized Beams (with assending Sector ID starting with Sector ID=0) during the sector training.

## Slide 13: Straw Poll 2
  Do you support to schedule a Sounding RAW using the sounding RAW indicator as indicated in Slide 7?

## Slide 14: Straw Poll 3
Do you support to use the Sector ID Index format as proposed in Slide 9 for the Sector ID Feedback

## Slide 15: Motion 1
Move to accept using CTS NDP with Address Indicator set to 0 and RA set to Partial BSSID for sector training in SFD. The CTS NDPs with the Address Indicator set to 0 and RA set to Partial BSSID will be transmitted through the Sectorized Beams (with assending Sector ID starting with Sector ID=0) during the sector training.

## Slide 16: Motion 2
  Move to include in SFD the Sounding RAW indicator for sector training as described in Slide 7?

## Slide 17: Motion 3
Move to include the Sector ID Index format in SFD as proposed in Slide 9 for the Sector ID Feedback