## Slide 1: Active Scanning for 11ah Follow Up
Date: 2013-03-18
Authors:
Name | Affiliations | Address | Phone | Email
Jae Seung Lee | ETRI | 161 Gajeong-dong, Yuseong-Gu, Daejoen, Korea | +82 42 860 1326 | jasonlee@etri.re.kr
Minho Cheong | ETRI |  | +82 42 860 5635 | minho@etri.re.kr
Hyoungjin Kwon | ETRI |  | +82 42 860 1698 | kwonjin@etri.re.kr
Jaewoo Park | ETRI |  | +82 42 860 5723 | parkjw@etri.re.kr
Sok-kyu Lee | ETRI |  | +82 42 860 5919 | sk-lee@etri.re.kr
Huai-Rong Shao | Samsung |  |  | hr.shao@samsung.com
Chiu Ngo | Samsung |  |  | chiu.ngo@samsung.com
Eric Wong | Broadcom | 190 Mathilda Place, Sunnyvale, CA | +1 408 922 6672 | ewong@broadcom.com
Matthew Fischer | Broadcom |  |  | mfischer@broadcom.com
Yong Liu | Broadcom |  |  | yongliu@broadcom.com
Minyoung Park | Intel | Hillsboro, OR | +1 503 712 4705 | minyoung.park@intel.com
Tom Tetzlaff | Intel |  |  | thomas.a.tetzlaff@intel.com
Emily Qi | Intel |  |  | emily.h.qi@intel.com
Yongho Seok | LG Electronics | LG R&D Complex Anyang-Shi, Kyungki-Do, Korea | +82-31-450-1947 | yongho.seok@lge.com
Jinsoo Choi | LG Electronics |  |  | 
Jeongki Kim | LG Electronics |  |  | 
HanGyu Cho | LG Electronics |  |  | 

## Slide 2: Authors:
Jae Seung Lee, ETRI
Name | Affiliations | Address | Phone | Email
Su Khiong Yong | Marvell |  |  | skyong@marvell.com
Hongyuan Zhang | Marvell |  |  | Hongyuan@marvell.com
Sudhir Srinivasa | Marvell |  |  | sudhirs@marvell.com
Simone Merlin | Qualcomm | 5775 Morehouse Dr, San Diego, CA | +1 858 845 1243 | smerlin@qualcomm.com
Santosh Abraham | Qualcomm |  |  | 
Menzo Wentink | Qualcomm |  |  | 
Alfred Asterjadhi | Qualcomm |  |  | 
Amin Jafarian | Qualcomm |  |  | 
Hemanth Sampath | Qualcomm |  |  | 
VK Jones | Qualcomm |  |  | 
Chittabrata Ghosh | Nokia | Berkeley, CA | +1 650 200 7566 | chittabrata.ghosh@nokia.com
Klaus Doppler | Nokia |  |  | 
Sayantan Choudhury | Nokia |  |  | 
Esa Tuomaala | Nokia |  |  | 
Osama Aboul-Magd | Huawei |  |  | Osama.AboulMagd@huawei.com
George Calcev | Huawei | Rolling Meadows,IL |  | George.Calcev@huawei.com
Young Hoon Kwon | Huawei |  |  | Younghoon.kwon@huawei.com
Betty Zhao | Huawei |  |  | Betty.Zhao@huawei.com
David Yangxun | Huawei |  |  | David.Yangxun@huawei.com
Bin Zhen | Huawei |  |  | ZhenBin@huawei.com
Sun, Bo | ZTE |  |  | sun.bo1@zte.com.cn
Lv, Kaiying | ZTE |  |  | lv.kaiying@zte.com.cn

## Slide 3: Authors:
Jae Seung Lee, ETRI
Name | Affiliations | Address | Phone | Email
Ken Mori | Panasonic |  |  | Mori.ken1@jp.panasonic.com
Rojan Chitrakar | Panasonic |  |  | Rojan.Chitrakar@sg.panasonic.com
Haiguang Wang | I2R | 1 Fusionopolis Way, #21-01 Connexis Tower, Singapore 138632 | +65-6408 2000 | hwang@i2r.a-star.edu.sg
Shoukang Zheng | I2R |  |  | skzheng@i2r.a-star.edu.sg
Wai Leong Yeow | I2R |  |  | wlyeow@i2r.a-star.edu.sg
Zander Lei | I2R |  |  | leizd@i2r.a-star.edu.sg
Yuan Zhou | I2R |  |  | yzhou@i2r.a-star.edu.sg
ChaoChun Wang | MediaTek |  |  | chaochun.wang@mediatek.com
James Wang | MediaTek |  |  | james.wang@mediatek.com
Jianhan Liu | MediaTek |  |  | jianhan.liu@mediatek.com
Vish Ponnampalam | MediaTek |  |  | vish.ponnamplam@mediatek.com
James Yee | MediaTek |  |  | james.yee@mediatek.com
Thomas Pare | MediaTek |  |  | thomas.pare@mediatek.com
Kiran Uln | MediaTek |  |  | kiran.uln@mediatek.com
Anna Pantelidou | Renesas Mobile |  |  | 
Juho Pirskanen | Renesas Mobile |  |  | 
Timo Koskela | Renesas Mobile |  |  | 
Liwen Chu | STMicroelectronics |  |  | 
George Vlantis | STMicroelectronics |  |  | 

## Slide 4: Introduction
Short Probe Response frame has been included in 11ah Spec Framework Document
  11ah STA may use short Probe Response frame for active scanning which is a shortened version of Probe Response frame
  Short Probe Response frame contains Timestamp, either Compressed SSID or full SSID, optional Duration to Next Full Beacon, other TBD optional fields and optional IEs
  STA may indicate in the Probe Request which optional information to be included in the short Probe Response frame in optimized way
This contribution proposes following:
  How to indicate optional information to be included in the short Probe Response
Jae Seung Lee, ETRI

## Slide 5: Indicating Optional Information
Probe Response Option IE is included in the Probe Request frame
  Requesting STA indicates which optional information to be included in the short Probe Response frame using Probe Response Option IE in the Probe Request frame
    STA requests minimum information that is required for association to the AP
  Using Request element in current 802.11 spec can increase the size of Probe Request too much
    Request element includes Element IDs of all the requested elements, and each Element ID of the requested element in the Request element consumes 1 octet
    Suggest to use bitmaps indicating what information should be included in the Probe Response
Jae Seung Lee, ETRI
Slide 5
Notes: 삭제

## Slide 6: Probe Response Option IE
Probe Response Option IE Format
  Included in the Probe Request
  Information to be included in the short Probe Response is categorized into 8 bitmaps (Detailed information included in the bitmap is TBD)
    Request full SSID: If it is set to 1, Full SSID is included in the Short Probe Response frame. Otherwise, compressed SSID is included
    If each bit in the bitmap is set to 1, the corresponding information should be included in the Probe Response frame
    Only bitmaps with at least one 1 are included in the Probe Response Option IE.
    Probe Response Group bitmap indicates which Probe Response Option bitmap is included in the Probe Response Option IE
  Define bitmap 0 as a default bitmap that contains frequently used options
    If only bitmap 0 is chosen to be included in the Probe Response Option IE, Probe Response Group bitmap may be omitted.
Jae Seung Lee, ETRI
Slide 6
Element ID | Length | Probe Response Group bitmap | Probe Response Option bitmap 0 | ……. | Probe Response Option bitmap n
Octets: 1 1 1 1 1

## Slide 7: Probe Response Option Bitmaps
Example of Probe Response Option Bitmap Definition
  Bitmap 0 (Default Bitmap): contains Request full SSID, Request Duration to Next Full Beacon, Request Access Network Options, Request Capability Information, Request Supported Rates, Request RSN element, Request EDCA Parameter, etc.
  Bitmap 1 (11u related information + other information): Request Interworking element, Request Roaming consortium element, Request Emergency alert Identifier, etc…
  Bitmap 2 (11k related information): Request BSS Average Access Delay, Request BSS Available Admission Capacity, Request BSS AC Access Delay, Request TPC Report element, etc…
  There are many Information Elements that are not necessary to 11ah, so 8 * 8 bit bitmap is enough to signal the information that should be included in the Probe Request
    For example, FH Parameter Set, DSSS Parameter Set, 20/40 BSS Coexistence, etc…. are not necessary for 11ah
  We can choose to include only widely used parameters in the bitmap definition
  Detailed information to be included in the bitmap is TBD
Jae Seung Lee, ETRI
Slide 7

## Slide 8: Probe Response Option – Examples (1/2)
Example of using Probe Response Option Bitmap #1
  The STA requests
    Full SSID, Duration to Next Full Beacon, Access Network Option, Request Capability Information, Request supported rates (that are defined in bitmap 0)
    Request Interworking element and Request Roaming consortium element (that are defined in bitmap 1)
    to be included in the short probe response
  Probe Response option IE example:
Jae Seung Lee, ETRI
Slide 8
Element ID | Length (= 3) | Probe Response Group bitmap (11000000) | Probe Response Option bitmap 0 (11111000) | Probe Response Option bitmap 1 (11000000)

## Slide 9: Probe Response Option – Examples (2/2)
Example of using Probe Response Option Bitmap #2 (using default bitmap)
  The STA requests
    Full SSID, Duration to Next Full Beacon, Access Network Option, Request Capability Information, Request supported rates (in bitmap 0 which is defined to be a default bitmap )
    to be included in the short probe response
    Only bitmap 0 (default bitmap) is included -- Probe Response Group bitmap can be omitted
  Probe Response option IE example:
Jae Seung Lee, ETRI
Slide 9
Element ID | Length (= 1) | Probe Response Option bitmap 0 (11111000)

## Slide 10: Summary
We proposed how to indicate optional information to be included in the short Probe Response
  Requesting STA indicates which optional information to be included in the short Probe Response frame using Probe Response Option IE in the Probe Request frame
  Bitmap structure is used for the indication
  Consumes less octet than using Request element in the baseline spec
STA can request minimum information that is required for association to the AP
  STA can associate immediately after it receives Short Probe Response
Jae Seung Lee, ETRI

## Slide 11: Straw Poll
Do you support to include the concept of Probe Response Option as described in slide 6 in the Spec Framework document under R.4.4.1.4.C?
Yes:
No:
Abstain:
Jae Seung Lee, ETRI

## Slide 12: Motion
Move to include the definition of Probe Response Option IE as described in slide 6 in the Spec Framework document under R.4.4.1.4.C?
Yes:
No:
Abstain:
Jae Seung Lee, ETRI

## Slide 13: References
[1] IEEE 802.11-12/0869r0 Active Scanning for 11ah
[2] IEEE 802.11-11/1137r13 Proposed Specification Framework for TGah
Jae Seung Lee, ETRI