## Slide 1: P802.1Qbz + P802.11ak Proposed Division of Work
Date: 2013-04-08
Authors:

## Slide 2: Abstract
A proposal on how to divide the work between P802.1Qbz and P802.11ak for wired/wireless bridging.
Content of this presentation same as content of:
http://www.ieee802.org/1/files/public/docs2013/bz-nfinn-division-of-work-0413-v01.pdf

## Slide 3: The Portal, today
What 802.11 presents to the bridge/router is a Portal, which offers a single generic IEEE 802 MAC service to the Bridge (or Router).
  This prevents the bridge/router from using the individual links optimally (for accurate forwarding), because the bridge cannot access individual links.
  The Portal does not reflect transmitted frames back to the bridge. This is good, because otherwise, bridges cannot learn source addresses.
Each non-AP station presents each of its multiple wireless associations as an independent generic instance of the MAC service.
  That’s just what we want, but the station also reflects back any multicasts or broadcasts to the upper layers, which breaks source address learning.
AP1
AP2
B/R
AP-AP link
Portal

## Slide 4: What P802.11ak can provide
New: 802.11 presents to the bridge/router a bundle of MAC service instances, allow the bridge to send a frame to any combination of ports.
  As is true today, the MACs do not reflect transmitted frames.
  (Actually, a controlled and an uncontrolled port are provided for each.)
As is true today, each non-AP station presents each of its multiple wireless associations as an independent instance of the MAC service.
  New: he non-AP station does not reflect any frames back to the upper layers.
AP1
AP2
B/R
AP-AP link
Single frames come up the stack.
Going down, bridge presents a single frame and a vector of ports to send it on.

## Slide 5: Summary of P802.1Qbz and P802.11ak changes
11ak: Make a wired/wireless connection at a non-AP station legal.
11ak: Do not reflect frames back to a non-AP station’s upper layers (bridge, router, or host).
11ak: Present a bundle of point-to-point interfaces to the upper layers (bridge, router, or host). Upper layers can offer a single frame with a port vector. AP optimizes multicast transmission or not, at its pleasure.
1Qbz and 11ak: When adding a tag to an LLC MSDU, change the MSDU to a Type/Length encoding, and then add the LLC-formatted tag. Similarly, expand things back out when removing tags.
11ak or 1Qbz: Define how to pick the “cost” of a point-to-point wireless link that is really not fixed, or even well-defined.
11ak or 1Qbz: Define basic model for heuristics to decide whether a (potentially flaky) wireless link is or is not visible in the network.

## Slide 6: What does this mean for implementers?
The use cases for an AP not at the edge of the network, though very real, are not yet common.
The use cases for a VLAN-aware or bridging non-AP station are more numerous. This is a common case, today, but there are several, non-interoperable ways to build it.
The cost of implementing 802.11ak in an AP core or a non-AP station NIC. which enables them to support a bridge or router more efficiently, is small compared to the cost of the bridging or routing function, itself.
So, I would expect 802.11ak to be widely implemented, even if a combined bridge/AP is an extra-cost feature.
But, we will now have the opportunity to apply every bit of IEEE, IETF, ITU-T, and other Ethernet networking technology to the Wi-Fi world, as well as the wired world.