## Slide 1: P802.1Qbz + P802.11ak Proposed Division of Work
Date: 2013-05-09
Authors:

## Slide 2: Abstract
A proposal on how to divide the work between P802.1Qbz and P802.11ak for wired/wireless bridging.
Content of this presentation same as content of:
http://www.ieee802.org/1/files/public/docs2013/bz-nfinn-division-of-work-0413-v04.pdf
For background, see:
https://mentor.ieee.org/802.11/dcn/13/11-13-0253-00-00ak-changes-to-802-1q-required-by-802-1qbz.pptx

## Slide 3: The AP-DS interface
The interface between the Access Point (AP) and Distribution System (DS) is defined in Annex R of IEEE Std 802.11™-2011.
R.2.2.2.4, in particular, states that the DS reflects every multicast or broadcast back to the source station; this is exactly what must not happen in the case of a station that is attached to a Bridge. Although Annex R is informative, not normative, a change seems necessary.
In general, Annex R assumes that the 3-address format is used, not the 4-address format. As discussed in earlier presentations, the 4-address format is likely necessary for .11ak.
B/R
Portal
AP1
AP2
Distribution System (DS)

## Slide 4: Revised AP-DS interface
The earlier “802.1Q changes necessary” contribution (bz-nfinn-802-1Q-changes-0313-v01.pdf, or 11-13/253) outlined a “bundle of point-to-point interfaces aka a vector” idea that the present document will expand upon.
The difference between this bundle of point-to-point links, an extension of the current definitions in 802.11, and the current definitions in 802.1, is a matter of plotting a function in polar vs. rectilinear vs. log-log coordinates. The substance of specifications, like the function being plotted, is the same.
Our suggestion is that 802.11ak consider altering Annex R (informative) to this bundle-aka-a-vector model, and that 802.1Qbz add a similar informative annex to map the 802.1Q bridge port model to the same bundle-aka-a-vector model.

## Slide 5: The DS, today
What 802.11 presents to the bridge/router is a Portal, which offers a single generic IEEE 802 MAC service to the Bridge (or Router).
  This prevents the bridge/router from using the individual links optimally (for accurate forwarding), because the bridge cannot access individual links.
  Wireless (or wired) AP-AP links are the province of the DS; they are not visible above the Portal.
  The method to be used by the DS to interconnect APs that are not physically co-located is not specified, nor is the method by which it accesses the wired network (the Portal is not always suitable).
B/R
Portal
AP1
AP2
Distribution System (DS)

## Slide 6: DS after P802.11ak
New: 802.11 AP presents to the bridge/router a bundle of MAC service instances, which allows it to send an MSDU to any combination of ports.
  The bridges or routers are the DS and prevent reflection – no need for a Portal.
  Broadcast distribution/reflection is what bridges/routers do for a living.
  Each instance within the bundle carries only Destination Address (DA) and Source Address (SA) – not Transmitter Address (TA) nor Receiver Address (RA).
The bundle is equivalent to presenting an MSDU, DA, SA and a vector that identifies the combination of port(s)
    MSDU passed from non-AP to AP MSDU to DS: RA is always the AP MAC and is discarded by AP. AP identifies the TA to the DS by setting one bit in the vector (where the bit position is associated with the non-AP STA)
    MSDU passed from DS to AP to non-AP(s): AP sets TA as its own MAC address and the RA is selected at the AP’s discretion to cover the bits set in the vector, as described in the next slide.
  AP-to-AP links are available to the DS, as they now, but on exactly the same basis as wired links.
B/R
B/R
AP1
AP2
Distribution System (DS)
B/R
B/R

## Slide 7: Selecting the Receiver Address
When transmitting, the Bridge (or router) supplies a MSDU that has only Destination and Source addresses, and a vector indicating on which “point-to-point links” (i.e., to which stations) the MSDU is to be transmitted.
For 3-address format, of course, RA == DA, and the vector can have only all bits set (individual key) or one bit set (shared key).
For 4 addresses, AP uses the full vector to pick the RA and key:
  If vector has only 1 bit set, then clearly, the AP uses the unicast address of that station as the RA, and uses that station’s key to secure the frame.
  If there are multiple bits set, then the AP has a free choice:
    It can transmit the MSDU multiple times using different unicast RAs and keys.
    If all bits are set, it can transmit the MSDU once, using the broadcast RA and key.
    The AP can establish and distribute a set of multicast RAs and use the broadcast key to distribute the MSDU to a subset of stations.

## Slide 8: Existing Distribution Systems
The bridge (or router) attached to the AP via this bundle of point-to-point links (aka a vector) is a perfectly valid implementation of the data transfer portion of the Distribution System (DS).
  A DS is not required to have a portal. And now no portal is needed, in this case.
  This does not eliminate or obsolete existing implementations of the DS. Rather, the DS is provided with a new anti-reflection capability.
  The presence of this data transfer technique does not inhibit the DS from performing any of its other functions.
Note that this bundle-of-links-aka-vector model can pretty much eliminate the difference between the 3-address format and the 4-address format across the AP-DS interface.

## Slide 9: Summary of P802.1Qbz and P802.11ak changes suggested by this document
11ak: Modify the informative 802.11 Annex R to describe the bundle-of-links-and-a-vector model.
1Qbz: Provide an informative annex specifying how to map the bundle-of-links-and-a-vector model to the current Bridge Port model.