## Slide 1: Extended Block Ack
Date: 2013-03-27
Authors:

## Slide 2: Abstract
Propose to extend the maximum BA window from 64 to 256 to support greater efficiency of operation at high PHY rates – see LB193 CID 278:
  The highest indicated modulation and stream combinations for some PHYs result in PHY rates that will reduce throughput efficiency to exceedingly low levels if the maximum Block Ack window size is not allowed to increase beyond the existing 64.
  Increase the maximum allowed MPDUs in the Block Ack frame to 256 by creating a new form of Block Ack that supports a longer BA window and a longer BA bitmap

## Slide 3: Existing Limitations
AMPDU, max window = 64 MPDU
AMSDU, max size = 11454 B

## Slide 4: AMSDU has higher PER at same SNR
E.g. Assume BER = 9e-6:
MPDU, No AMSDU:
  UDP payload = 1460 B => MPDU payload = 1508 B
  PPDU payload = 1566 B
  PER = 1-(1-9e-6)^(1566*8) = 10.7% PER
MPDU, With AMSDU = 4xMSDU:
  UDP payload = 1460 B MPDU payload = 6088 B
  PPDU payload = 6146 B
  PER = 1-(1-9e-6)^(6146*8) = 35.8% PER

## Slide 5: But AMSDU has fewer MPDUs per PPDU
Which term dominates?
Increasing PER vs Decreasing MPDU count

## Slide 6: RAW PHY Rate Comparison
 | SNR |  |  |  |  |  |  | 
 | NSS | 2 |  |  |  |  |  | 
 | SGI | 0 |  |  |  |  |  | 
MCS: | 9 | 8 | 9 |  |  |  | MCS9 | 
 | MAX | MAX | MAX |  |  |  | MCS8 | 
20 MHz |  | 156.0 | 173.3 |  |  |  | 111.1% | 
40 MHz |  | 324.0 | 360.0 |  |  |  | 111.1% | 
80 MHz |  | 702.0 | 780.0 |  |  |  | 111.1% | 
160 MHz |  | 1404.0 | 1560.0 |  |  |  | 111.1% | 
BER |  |  |  |  |  |  |  | 
PER |  |  |  |  |  |  |  | 

## Slide 7: UDP Throughput (1.0 dB/dec AWGN)
 | SNR | 26 |  |  |  |  |  | 
UDP | NSS | 2 |  |  |  |  |  | 
 | SGI | 0 |  |  |  |  |  | 
MCS: | 9 | 8 | 9 | MCS9_64x4 | 9 | MCS9_256 | MCS9_256 | MCS9_256
 | MAX | 64x4 | 64x4 | MAX9 | 256x0 | MAX9 | MCS8_64x4 | MCS9_64x4
20 MHz | 173.3 | 141.0 | 113.5 | 65.5% | 145.0 | 83.7% | 102.9% | 127.8%
40 MHz | 360.0 | 288.3 | 231.6 | 64.3% | 296.0 | 82.2% | 102.7% | 127.8%
80 MHz | 780.0 | 603.0 | 483.0 | 61.9% | 617.7 | 79.2% | 102.4% | 127.9%
160 MHz | 1560.0 | 1134.6 | 902.5 | 57.9% | 1156.5 | 74.1% | 101.9% | 128.1%
BER |  | 7.049E-07 | 7.235E-06 |  | 7.235E-06 |  |  | 
PER |  | 3.4% | 29.9% |  | 8.7% |  |  | 

## Slide 8: UDP Throughput (1.0 dB/dec AWGN)
 | SNR | 26.1 |  |  |  |  |  | 
UDP | NSS | 2 |  |  |  |  |  | 
 | SGI | 0 |  |  |  |  |  | 
MCS: | 9 | 8 | 9 | MCS9_64x4 | 9 | MCS9_256 | MCS9_256 | MCS9_256
 | MAX | 64x4 | 64x4 | MAX9 | 256x0 | MAX9 | MCS8_64x4 | MCS9_64x4
20 MHz | 173.3 | 142.0 | 122.3 | 70.5% | 147.8 | 85.3% | 104.1% | 120.9%
40 MHz | 360.0 | 290.4 | 249.6 | 69.3% | 301.7 | 83.8% | 103.9% | 120.9%
80 MHz | 780.0 | 607.4 | 520.6 | 66.7% | 629.6 | 80.7% | 103.7% | 120.9%
160 MHz | 1560.0 | 1142.8 | 972.6 | 62.3% | 1178.7 | 75.6% | 103.1% | 121.2%
BER |  | 5.596E-07 | 5.712E-06 |  | 5.712E-06 |  |  | 
PER |  | 2.7% | 24.5% |  | 6.9% |  |  | 

## Slide 9
UDP Throughput (1.0 dB/dec AWGN)
Broadcom
 | SNR | 26.5 |  |  |  |  |  | 
UDP | NSS | 2 |  |  |  |  |  | 
 | SGI | 0 |  |  |  |  |  | 
MCS: | 9 | 8 | 9 | MCS9_64x4 | 9 | MCS9_256 | MCS9_256 | MCS9_256
 | MAX | 64x4 | 64x4 | MAX9 | 256x0 | MAX9 | MCS8_64x4 | MCS9_64x4
20 MHz | 173.3 | 144.4 | 145.0 | 83.7% | 154.4 | 89.1% | 106.9% | 106.5%
40 MHz | 360.0 | 295.2 | 296.1 | 82.2% | 315.1 | 87.5% | 106.7% | 106.4%
80 MHz | 780.0 | 617.5 | 617.4 | 79.2% | 657.5 | 84.3% | 106.5% | 106.5%
160 MHz | 1560.0 | 1161.9 | 1153.5 | 73.9% | 1231.1 | 78.9% | 106.0% | 106.7%
BER |  | 2.225E-07 | 2.243E-06 |  | 2.243E-06 |  |  | 
PER |  | 1.1% | 10.4% |  | 2.8% |  |  | 

## Slide 10
UDP Throughput (1.0 dB/dec AWGN)
Broadcom
 | SNR | 26.8 |  |  |  |  |  | 
UDP | NSS | 2 |  |  |  |  |  | 
 | SGI | 0 |  |  |  |  |  | 
MCS: | 9 | 8 | 9 | MCS9_64x4 | 9 | MCS9_256 | MCS9_256 | MCS9_256
 | MAX | 64x4 | 64x4 | MAX9 | 256x0 | MAX9 | MCS8_64x4 | MCS9_64x4
20 MHz | 173.3 | 145.2 | 153.3 | 88.4% | 156.6 | 90.3% | 107.9% | 102.2%
40 MHz | 360.0 | 296.9 | 312.9 | 86.9% | 319.6 | 88.8% | 107.7% | 102.2%
80 MHz | 780.0 | 620.9 | 652.5 | 83.6% | 666.8 | 85.5% | 107.4% | 102.2%
160 MHz | 1560.0 | 1168.2 | 1219.0 | 78.1% | 1248.6 | 80.0% | 106.9% | 102.4%
BER |  | 1.115E-07 | 1.119E-06 |  | 1.119E-06 |  |  | 
PER |  | 0.5% | 5.4% |  | 1.4% |  |  | 

## Slide 11: UDP Throughput (AWGN)
 | SNR | 26.8 |  |  |  |  |  | 
UDP | NSS | 2 |  | Slope | 1.6 | dB per decade PER |  | 
 | SGI | 0 |  |  |  |  |  | 
MCS: | 9 | 8 | 9 | MCS9_64x4 | 9 | MCS9_256 | MCS9_256 | MCS9_256
 | MAX | 64x4 | 64x4 | MAX9 | 256x0 | MAX9 | MCS8_64x4 | MCS9_64x4
20 MHz | 173.3 | 141.4 | 141.2 | 81.4% | 153.3 | 88.5% | 108.5% | 108.6%
40 MHz | 360.0 | 289.0 | 288.2 | 80.1% | 313.0 | 86.9% | 108.3% | 108.6%
80 MHz | 780.0 | 604.5 | 601.0 | 77.1% | 653.0 | 83.7% | 108.0% | 108.7%
160 MHz | 1560.0 | 1137.4 | 1122.9 | 72.0% | 1222.7 | 78.4% | 107.5% | 108.9%
BER |  | 6.558E-07 | 2.789E-06 |  | 2.789E-06 |  |  | 
PER |  | 3.2% | 12.8% |  | 3.4% |  |  | 

## Slide 12: UDP Throughput (Channel D)
 | SNR | 26.8 |  |  |  |  |  | 
UDP | NSS | 2 |  | Slope | 4 | dB per decade PER |  | 
 | SGI | 0 |  |  |  |  |  | 
MCS: | 9 | 8 | 9 | MCS9_64x4 | 9 | MCS9_256 | MCS9_256 | MCS9_256
 | MAX | 64x4 | 64x4 | MAX9 | 256x0 | MAX9 | MCS8_64x4 | MCS9_64x4
20 MHz | 173.3 | 120.5 | 114.6 | 66.1% | 145.4 | 83.9% | 120.7% | 126.8%
40 MHz | 360.0 | 246.4 | 234.0 | 65.0% | 296.8 | 82.4% | 120.5% | 126.8%
80 MHz | 780.0 | 515.3 | 488.1 | 62.6% | 619.3 | 79.4% | 120.2% | 126.9%
160 MHz | 1560.0 | 969.6 | 911.9 | 58.5% | 1159.5 | 74.3% | 119.6% | 127.2%
BER |  | 3.901E-06 | 7.024E-06 |  | 7.024E-06 |  |  | 
PER |  | 17.5% | 29.2% |  | 8.4% |  |  | 

## Slide 13: UDP Throughput (Channel D)
 | SNR | 28.5 |  |  |  |  |  | 
UDP | NSS | 2 |  | Slope | 4 | dB per decade PER |  | 
 | SGI | 0 |  |  |  |  |  | 
MCS: | 9 | 8 | 9 | MCS9_64x4 | 9 | MCS9_256 | MCS9_256 | MCS9_256
 | MAX | 64x4 | 64x4 | MAX9 | 256x0 | MAX9 | MCS8_64x4 | MCS9_64x4
20 MHz | 173.3 | 135.9 | 142.5 | 82.2% | 153.7 | 88.7% | 113.1% | 107.8%
40 MHz | 360.0 | 277.9 | 291.0 | 80.8% | 313.8 | 87.2% | 112.9% | 107.8%
80 MHz | 780.0 | 581.3 | 606.8 | 77.8% | 654.6 | 83.9% | 112.6% | 107.9%
160 MHz | 1560.0 | 1093.7 | 1133.8 | 72.7% | 1225.7 | 78.6% | 112.1% | 108.1%
BER |  | 1.452E-06 | 2.594E-06 |  | 2.594E-06 |  |  | 
PER |  | 6.9% | 12.0% |  | 3.2% |  |  | 

## Slide 14: UDP Throughput (Channel D)
 | SNR | 32 |  |  |  |  |  | 
UDP | NSS | 2 |  | Slope | 4 | dB per decade PER |  | 
 | SGI | 0 |  |  |  |  |  | 
MCS: | 9 | 8 | 9 | MCS9_64x4 | 9 | MCS9_256 | MCS9_256 | MCS9_256
 | MAX | 64x4 | 64x4 | MAX9 | 256x0 | MAX9 | MCS8_64x4 | MCS9_64x4
20 MHz | 173.3 | 144.6 | 159.2 | 91.9% | 158.0 | 91.2% | 109.3% | 99.2%
40 MHz | 360.0 | 295.7 | 325.0 | 90.3% | 322.5 | 89.6% | 109.1% | 99.2%
80 MHz | 780.0 | 618.4 | 677.8 | 86.9% | 672.9 | 86.3% | 108.8% | 99.3%
160 MHz | 1560.0 | 1163.6 | 1266.5 | 81.2% | 1259.9 | 80.8% | 108.3% | 99.5%
BER |  | 1.93E-07 | 3.43E-07 |  | 3.43E-07 |  |  | 
PER |  | 0.9% | 1.7% |  | 0.5% |  |  | 

## Slide 15: UDP Throughput (Channel D)
 | SNR | 32 |  |  |  |  |  | 
UDP | NSS | 2 |  | Slope | 4 | dB per decade PER |  | 
 | SGI | 0 |  |  |  |  |  | 
MCS: | 7 | 6 | 7 | MCS7_64x4 | 7 | MCS7_256 | MCS7_256 | MCS7_256
 | MAX | 64x4 | 64x4 | MAX7 | 256x0 | MAX7 | MCS6_64x4 | MCS7_64x4
20 MHz | 130.0 | 109.3 | 121.4 | 93.3% | 119.0 | 91.5% | 108.8% | 98.0%
40 MHz | 270.0 | 224.4 | 248.7 | 92.1% | 243.9 | 90.3% | 108.7% | 98.1%
80 MHz | 585.0 | 473.6 | 523.3 | 89.4% | 513.5 | 87.8% | 108.4% | 98.1%
160 MHz | 1170.0 | 903.3 | 993.9 | 84.9% | 975.6 | 83.4% | 108.0% | 98.2%
BER |  | 6.087E-09 | 1.083E-08 |  | 1.083E-08 |  |  | 
PER |  | 0.5% | 0.5% |  | 0.5% |  |  | 

## Slide 16: UDP Throughput (Channel D)
 | SNR | 17 |  |  |  |  |  | 
UDP | NSS | 2 |  | Slope | 4 | dB per decade PER |  | 
 | SGI | 0 |  |  |  |  |  | 
MCS: | 5 | 4 | 5 | MCS5_64x4 | 5 | MCS5_256 | MCS5_256 | MCS5_256
 | MAX | 64x4 | 64x4 | MAX5 | 256x0 | MAX5 | MCS4_64x4 | MCS5_64x4
20 MHz | 104.0 | 69.1 | 46.0 | 44.2% | 79.1 | 76.1% | 114.5% | 172.0%
40 MHz | 216.0 | 142.5 | 94.5 | 43.8% | 162.7 | 75.3% | 114.2% | 172.0%
80 MHz | 468.0 | 303.1 | 200.1 | 42.8% | 344.3 | 73.6% | 113.6% | 172.1%
160 MHz | 936.0 | 586.9 | 383.7 | 41.0% | 660.9 | 70.6% | 112.6% | 172.2%
BER |  | 1.26E-06 | 1.53E-05 |  | 1.53E-05 |  |  | 
PER |  | 6.0% | 53.0% |  | 17.5% |  |  | 

## Slide 17: UDP Throughput (Channel D)
 | SNR | 19 |  |  |  |  |  | 
UDP | NSS | 2 |  | Slope | 4 | dB per decade PER |  | 
 | SGI | 0 |  |  |  |  |  | 
MCS: | 5 | 4 | 5 | MCS5_64x4 | 5 | MCS5_256 | MCS5_256 | MCS5_256
 | MAX | 64x4 | 64x4 | MAX5 | 256x0 | MAX5 | MCS4_64x4 | MCS5_64x4
20 MHz | 104.0 | 72.1 | 77.8 | 74.8% | 90.5 | 87.0% | 125.4% | 116.3%
40 MHz | 216.0 | 148.6 | 159.9 | 74.0% | 186.0 | 86.1% | 125.1% | 116.3%
80 MHz | 468.0 | 316.2 | 338.4 | 72.3% | 393.7 | 84.1% | 124.5% | 116.3%
160 MHz | 936.0 | 612.3 | 649.0 | 69.3% | 755.6 | 80.7% | 123.4% | 116.4%
BER |  | 3.96E-07 | 4.65E-06 |  | 4.65E-06 |  |  | 
PER |  | 1.9% | 20.4% |  | 5.7% |  |  | 

## Slide 18: UDP Throughput (Channel D)
 | SNR | 19 |  |  |  |  |  | 
UDP | NSS | 2 |  | Slope | 4 | dB per decade PER |  | 
 | SGI | 0 |  |  |  |  |  | 
MCS: | 6 | 5 | 6 | MCS6_64x4 | 6 | MCS6_256 | MCS6_256 | MCS6_256
 | MAX | 64x4 | 64x4 | MAX6 | 256x0 | MAX6 | MCS5_64x4 | MCS6_64x4
20 MHz | 117.0 | 77.8 | 63.0 | 53.8% | 93.5 | 79.9% | 120.1% | 148.5%
40 MHz | 243.0 | 159.9 | 129.3 | 53.2% | 192.0 | 79.0% | 120.0% | 148.5%
80 MHz | 526.5 | 338.4 | 272.8 | 51.8% | 405.3 | 77.0% | 119.8% | 148.6%
160 MHz | 1053.0 | 649.0 | 520.3 | 49.4% | 773.7 | 73.5% | 119.2% | 148.7%
BER |  | 4.65E-06 | 1.13E-05 |  | 1.13E-05 |  |  | 
PER |  | 20.4% | 42.7% |  | 13.2% |  |  | 

## Slide 19: UDP Throughput (Channel D)
 | SNR | 19 |  |  |  |  |  | 
UDP | NSS | 2 |  | Slope | 4 | dB per decade PER |  | 
 | SGI | 0 |  |  |  |  |  | 
MCS: | 5 | 4 | 5 | MCS5_64x6 | 5 | MCS5_256x0 | MCS5_256x0 | MCS5_256x0
 | MAX | 64x6 | 64x6 | MAX5 | 256x0 | MAX5 | MCS4_64x6 | MCS5_64x6
20 MHz | 104.0 | 71.8 | 69.9 | 67.3% | 90.5 | 87.0% | 125.9% | 129.4%
40 MHz | 216.0 | 148.4 | 144.2 | 66.8% | 186.0 | 86.1% | 125.3% | 128.9%
80 MHz | 468.0 | 317.7 | 307.5 | 65.7% | 393.7 | 84.1% | 123.9% | 128.0%
160 MHz | 936.0 | 621.5 | 597.4 | 63.8% | 755.6 | 80.7% | 121.6% | 126.5%
BER |  | 3.96E-07 | 4.65E-06 |  | 4.65E-06 |  |  | 
PER |  | 2.9% | 29.0% |  | 5.7% |  |  | 

## Slide 20: UDP Throughput (Channel D)
 | SNR | 19 |  |  |  |  |  | 
UDP | NSS | 2 |  | Slope | 4 | dB per decade PER |  | 
 | SGI | 0 |  |  |  |  |  | 
MCS: | 6 | 5 | 6 | MCS6_64x3 | 6 | MCS6_256x0 | MCS6_256x0 | MCS6_256x0
 | MAX | 64x3 | 64x3 | MAX6 | 256x0 | MAX6 | MCS5_64x3 | MCS6_64x3
20 MHz | 117.0 | 81.9 | 71.8 | 61.4% | 93.5 | 79.9% | 114.2% | 130.2%
40 MHz | 243.0 | 167.6 | 146.9 | 60.4% | 192.0 | 79.0% | 114.5% | 130.7%
80 MHz | 526.5 | 352.2 | 307.2 | 58.4% | 405.3 | 77.0% | 115.1% | 131.9%
160 MHz | 1053.0 | 666.4 | 577.7 | 54.9% | 773.7 | 73.5% | 116.1% | 133.9%
BER |  | 4.65E-06 | 1.13E-05 |  | 1.13E-05 |  |  | 
PER |  | 15.8% | 34.2% |  | 13.2% |  |  | 

## Slide 21: Straw poll #1
Do you support the concept of allowing a longer BA window than the current value of 64 consecutive MAC Seq numbers?

## Slide 22: A New Block Ack Format
The next slides describe a proposal for increasing the BA window by creating a new variant of the BA frame = ExtendedBA (EBA)which supports a BA window of 256 MPDUs
LB193 CID 278 [1]
  Increase the maximum allowed MPDUs in the Block Ack frame to 256 by creating a new form of Block Ack.
  Rationale: need to enable greater throughput and efficiency at the higher rates that are created by the 11ac amendment

## Slide 23: BAR Control Field
New bit in the BAR Control field
EB = Extended Bitmap
Bits:
B0
B1
B2
B3
B4
B10
B12 B15
1
1
1
1
7
1
4
B11
BA Ack Policy
Multi-TID
Compressed Bitmap
GCR
Reserved
EB
Compressed Bitmap | EB | Interpretation
0 | 0 | Uncompressed Bitmap = 128 Bytes, Max Window = 64, fragments are supported
0 | 1 | Extended Bitmap = 32 Bytes, Max Window = 256, no fragmentation support
1 | 0 | Compressed Bitmap = 8 Bytes, Max Window = 64, no fragmentation support
1 | 1 | Reserved
TID_INFO

## Slide 24: Determining Response Type (option 1)
Within a DATA frame
  Redefine the meaning of Ack Policy=11b
ACK Policy = 00b indicates CBA within an AMPDU
  Outside of an AMPDU, 00b means Normal ACK
ACK Policy = 11b indicates EBA within an AMPDU
  Outside of an AMPDU, 11b means Block Ack
  Conflict with HT-Delayed BA?
  Does anyone care?

## Slide 25: Determining Response Type (option 2-7)
Option 2: Set BSSID I/G bit = 1 in DATA frame
  Requests an EBA response
Option 3: Use reserved bit within MPDU delimiter
Option 4: Frag=1111b with MoreFrag=1
Option 5: Use NEW Data Subtype = 1101
  Requires EBA response when Ack Policy = 00b
Option 6: VHT Control field 1 reserved bit
  Would prefer to align this bit with HTC field reserved bit
Option 7: Responder choice, NAV issue not serious

## Slide 26: Additional Request for EBA
EBA can also be transmitted
  When explicitly requested within a BAR that has the value CB, EB = 01b

## Slide 27: Negotiating Use of EBA
New Extended Capability bit advertises support
Pair of supporting STAs can negotiate use of EBA
  Use of EBA is implied by 64 < Buffer size value < 257 within ADEBA
Actual use of EBA is determined by Ack Policy settings in DATA frames of AMPDU and by CB, EB bit settings in BAR frames

## Slide 28: Straw Poll #2
Related to CID 278:
Do you support making changes to the BA protocol to support an increased maximum BA window size of 256?
Yes
No
Abs

## Slide 29: Straw Poll #3
Which option do you support for signaling a request for an EBA response in a DATA frame?
1:
2:
3:
4:
5:
6:
7:

## Slide 30: References
[1] 11-13-0233-07-000m-revmc-wg-ballot-comments.xls