## Slide 1: Response Frame Rate Selection
Date: 2013-03-27
Authors:

## Slide 2: Abstract
Propose a mechanism to allow responding STA to use a lower MCS in a response transmission
  I.e. lower than would otherwise be dictated by the existing response rate selection rules
    i.e. highest MCS in basic MCS set that is less than or equal to the eliciting frame’s MCS
  Proposal includes information exchange that allows eliciting STA to correctly predict the lower MCS so that DUR field accuracy can be preserved

## Slide 3: Terminology
All discussion applies to any exchange where there is a response frame
  E.g. CTS in response to RTS, e.g. Block Ack in response to DATA or AMPDU or Block Ack Request, ACK in response to MGMT, ACK in response to DATA, etc.
  The first frame in the exchange is called the eliciting frame
  A STA that transmits an eliciting frame is an eliciting STA
  A STA that transmits a response frame is a responding STA

## Slide 4: Problem Example
Two WLAN device that are communicating may have different transmit power levels
  There may be more than 10dB difference between the transmit power level of the two devices
The acknowledgment MCS selection is done with implicit assumption that the link margins are the same in both directions
  Simplest case when they are not the same – TX power is different!
  The response frame is transmitted at the highest MCS from the basic MCS set which has the same or a lower modulation than the eliciting frame
  Therefore, the response frame MCS is selected based on the MCS of the eliciting frame
  MCS adaptation happens on TCP Acks (i.e. real DATA MPDUs) but there is no MCS adaptation on the MAC ACKs so the MAC layer breaks earlier.
    MAC ACK adaptation is NOT ALLOWED! (see 9.7.6.5 Rate selection for control response frames)

## Slide 5: Specific example
Example:
  STA A transmitting at 30 dBm.
  STA B transmitting at 15 dBm.
STA A, with higher transmit power level, uses a high order modulation (16 QAM and 64QAM) to transmit eliciting frames and STA B can successfully receive these frames
STA B will use the highest MCS in the basic MCS set that has less than or equal modulation than the eliciting frame (e.g. 24Mbps) to transmit the response frame
STA A cannot receive the response frame successfully because STA B transmit power is significantly lower
  The combination of power and MCS is inadequate for the link
A sharp TPUT drop occurs because response frames are lost
The MCS of the response frame is not going to change unless the MCS of the eliciting frames transmitted by STA A changes to a lower order modulation
  MCS drop on STA A results in TPUT drop which is totally unnecessary if the response frame MCS could be decreased
This condition occurs when the MCS of the forward data is close to or below the highest basic MCS value

## Slide 6: Applicability
CTS
ACK
BA
FB frame

## Slide 7: Eliciting STA Solution (1)
Eliciting STA suggests a response frame MCS for a STA when it determines that such an MCS is needed
  Determination of need is established through:
    Explicitly delivered power level information, e.g. through explicit information exchange
    Measured receive power during a response frame reception at the eliciting STA
    Measured channel/BER/PER statistics for frames transmitted by the responding STA and received at the eliciting STA
    Explicitly delivered link measurement report information

## Slide 8: Eliciting STA Solution –> R + L
Eliciting STA uses previously described information to determine parameters R and L
Parameter R (reduction)
  The MCS of a response frame transmitted by a responding STA should be R tics below the MCS used for the eliciting frame transmission
Parameter L (Limit)
  L is the modulation/coding of the eliciting frame below which parameter R applies
  With the eliciting frame MCS at or above L, the responding STA does NOT apply parameter R to the responding MCS selection, instead, uses existing rules (see previous slides)

## Slide 9: Communication of R+L
Eliciting STA communicates R and L parameters to responding STA
  On Static basis
    E.g. during association exchange
  On semi-dynamic basis
    Using management frames to communicate changes at any time
  Within an eliciting frame (Dynamic basis)
    Not all eliciting frames need to carry MCS recommendation
    Responding STA continues to use last received instructions until new recommendation is delivered
    Need specific field to convey this information
  Within DUR value
    If DUR value allows longer response, responder may use longer response

## Slide 10: Signaling value of R
Provide means for a STA to indicate that responses should be at least R steps below the eliciting frame MCS
  If 9.7.6.5 Rate selection for control response frames outcome is already N steps below, then no adjustment needed
  MGMT frame that indicates value of R
    Needs to be sent to individual STA, but also allowed globally (i.e. to all members of the BSS)
    Needs to be sent as Instruction (e.g. DATA Originator to Responder)
    Needs to be sent as Information (e.g. Responder to DATA Originator)
DUR field must reflect expected response time
Propose New Public Action
  3 bits needed = Inform/Instruct_L, R[0:1]

## Slide 11: Eliciting STA Global Solution
If eliciting STA is an AP
Modify basic MCS set
  E.g. the eliciting STA, if it is an AP, can remove higher MCS values from the basic MCS set to disallow the use of those MCS values in response transmissions
Alternatively, the eliciting STA, if an AP, could provide different basic MCS sets for different STAs
  STAs with lower TX power may get basic MCS set that has lower rates
  This requires that an explicitly delivered basic MCS set is sent to individual responding STAs and that those STAs that receive such a basic MCS set ignore the broadcast basic MCS set that is normally transmitted by the AP
Only works if lowest rate is only Basic Rate

## Slide 12: Responder Determination of R and L
Responding STA receives retries of eliciting frames that it already successfully received
  Implying that the ACK was lost
    Responding STA should attempt to differentiate acknowledgement loss that is due to collision vs loss due to inappropriate MCS selection
Responding STA compares selected MCS values for the reverse link to required MCS for ACK
  Can also examine received SNR and explicitly determined eliciting TX power to determine forward link SNR and assume reciprocity
  If SNR is not adequate for responder’s TX power and ACK MCS value, then responder should use a lower MCS

## Slide 13: Simple Responding STA Solution
The response frame can simply be transmitted at the lowest MCSs for some STAs
  As a simple alternative, to avoid the necessity of determining relative TX power values and estimation of link margin and examination of retries
    Responding STA can simply use a reduced MCS for all response transmissions (reduced as compared to the requirement to use the highest MCS from the basic MCS set that is less than or equal to the MCS of the eliciting frame)

## Slide 14: Power difference indication
Each STA can indicate the power level it is using
  During association
  Using management frame exchange
    E.g. Link Measurement Request and report
      See 8.6.7.4 Link Measurement Request Frame Format
      The Link Measurement Request frame uses the Action frame body format and is transmitted by a STA to request another STA to respond with a Link Measurement Report frame to enable measurement of link path loss and estimation of link margin.
      See 8.6.7.5 Link Measurement Report Frame Format
  Per frame basis dynamically in the MAC header
    Requires new fields

## Slide 15: MCS Selection Using Channel/MCS feedback
Link adaptation is used to select MCS on the forward link (9.29 Link adaptation)
Same or similar methodology as forward link adaptation may be used to select the MCS for the response frame
  Let responding STA use its own MCS selection to limit MCS for response transmissions
    More safety margin may be used for the response frame i.e. a lower MCS may be selected for the response frame compared to data
    The difference between modulation of data and acknowledgement (safety margin) may be indicated during association

## Slide 16: Straw Poll #1
Related to CID 283:
Do you support the concept of allowing a responding STA to use a lower MCS for a response transmission than is currently prescribed by 9.7.6.5 Rate selection for control response frames, provided that DUR field accounts for the reduced MCS?
Yes
No
Abs

## Slide 17: Straw Poll #2
Related to CID 283:
Do you support the signaling of a directive for STA to respond using N steps below the normally computed value for a response transmission as currently prescribed by 9.7.6.5 Rate selection for control response frames, where N is communicated in a MGMT frame as shown in slide 10?
Yes
No
Abs

## Slide 18: References
[1] 11-13-0233-07-000m-revmc-wg-ballot-comments.xls