## Slide 1: TGah Miscellaneous PHY Updates
Date: 2013-05-13
Authors:

## Slide 2
Authors continued:
Slide 2
May 2013

## Slide 3
Authors continued:

## Slide 4: Outlines
1. Define Frequency Offset Tolerance Limit.
2. Revise the STBC Bit in SIG-A field in >=2MHz long preamble in the case of MU PPDUs.
3. Revise the Beam Change bit in SIG-A field in >=2MHz ling preamble in the case of SU PPDUs.

## Slide 5: 1. CFO Limits
Propose that 11ah devices keep the same frequency offset tolerance requirement from 11a/n/ac.
  i.e ±20 ppm.

## Slide 6: Pre-Motion-1
Do you agree to add the following sentence in TGah SFD?
  The draft specification shall support frequency inaccuracy maximum tolerance of ±20 ppm.

## Slide 7: 2. SIG-A Field For MU
As shown in [1], 11ac D5.0 removes the possibility of applying STBC in MU packet.
  The reason is: STBC is open-loop technology, but MU packet itself is beamformed packet where there is no case STBC can outperform beamforming.
For same reason, propose that in 11ah, for long preamble MU PPDU, STBC bit is reserved in SIG-A field.

## Slide 8: Pre-Motion-2
Do you agree to make the following change in R.3.2.1.1.E of TGah SFD?
  STBC: Same as in 11ac (Alamouti code on all streams or none), and set to 0 for MU PPDU.

## Slide 9: 3. Beam Change Field
In current SFD, the SIG/SIG-A field for >=2MHz preamble is defined as below.
 | Short preamble | Long preamble | 
 | SU | SU | MU
SU/MU Indication | - | 1 | 1
Length / Duration | 9 | 9 | 9
MCS | 4 | 4 | -
BW | 2 | 2 | 2
Aggregation | 1 | 1 | -
STBC | 1 | 1 | 1
Coding | 2 | 2 | 5
SGI | 1 | 1 | 1
GID | - | - | 6
Nsts | 2 | 2 | 8
PAID | 9 | 9 | -
Ack Indication | 2 | 2 | 2
Smoothing | 1 | - | -
Beam-change Indication | - | 1 | -
NDP Indication | 1 | - | -
Doppler | 1 | 1 | 1
Reserved | 2 | 2 | 2
CRC | 4 | 4 | 4
Tail | 6 | 6 | 6
Total | 48 | 48 | 48

## Slide 10: Background
Smoothing bit is defined only in short preamble.
In long preamble, beam change is defined to indicate Q matrix change between omni portion and data portion.
  If Beam Change is 0, then smoothing is recommended.
In long preamble, if Nsts>1, LTF1 and DLTFs are spatially mapped by the following equations:

## Slide 11: Issues
The beam change bit was proposed mainly for single stream cases:
  Qomni is CSD vector as in current SFD.
  When Qdata is different from Qomni, most likely the data portion is beamformed, therefore “channel smoothing is not recommended”.
  If it is unchanged, with a certain AGC design, receiver may combine LTF1 with DLTF1 to improve CE.
However, based on current definition, beam change bit is always 1 if Nsts>1, since Qdata is always different from Qomni.
  If Qdata is beamforming matrix, channel smoothing is not recommended.
  If Qdata is non-beamforming matrix (e.g. identity matrix), channel smoothing is recommended.
  But receiver has no idea on beamforming or not.
  For both cases, receiver can hardly benefit CE from combining LTF1 with DLTF(s).
  No implication on channel smooth-ability, different from short preamble and long preamble with Nsts=1 cases.
  This bit is almost wasted in this case.

## Slide 12: Proposed Solution
Re-name this field as “Beam Change/Smoothing”
  When Nsts=1, this field indicates beam change as in current SFD.
  When Nsts>1, this field means smoothing indication.
    Value 1 means smoothing is recommended as in short preamble.

## Slide 13: Pre-Motion-3
Do you agree with the following change in SFD R 3.2.1.1.E?
  In the table of 2MHz SIG-A, rename “beam-change indication” to “beam-change/smoothing indication”
  Replace item k below the table as:
    “Beam-change/smoothing indication bit: if Nsts=1, a value of 1 indicates that Q matrix is changed; a value of 0 indicates that Q matrix is un-changed. If Nsts>1, a value of 1 indicates that channel smoothing is recommended, otherwise channel smoothing is not recommended.
      Note: When Nsts=1, if the beam-change indication bit in long preamble is set to 0, the receiver may do channel smoothing. Otherwise, smoothing is not recommended. ”

## Slide 14: Motion
Move to adopt the proposed SFD text changes as shown in slides 6, 8 and 13.

## Slide 15: References
[1] 11-13-0054-00-00ac-proposed-resolution-on-cid-7103, Youhan Kim et al.