## Slide 1: Discussion On Basic Technical Aspects for HEW
Date: 2013-05-10
Authors:

## Slide 2: Abstract
This presentation discusses our views on some basic technical aspects for HEW Study group.
Covered aspects are:
  Uses Cases
  Traffic models
  Deployment scenarios
  Metrics
  Other issues
Notes: doc.: IEEE 802.11-yy/xxxxr0

## Slide 3: Use Cases for HEW
WLAN has been used under many different use cases.
Contemporary applications give rise to use cases, involving high network load and services requiring low latencies.
  HEW SG should concentrate on those use cases.
Different usage models were presented in [1].
  Majority of the services are using TCP IP.
  Latency and Packet error rate requirements are quite similar: 20-50ms, 1e-3 - 1e-8.
  Services are always Bi-directional in practice.
Achieved throughput over TCP is highly dependent on available bandwidth and end-to-end latency.
  Latency and Jitter has significant negative impact achieved bitrate.
  HEW SG should assume that latency in networks beyond 802.11 networks is low and decreasing in future.
If system capacity and latency are sufficient to provide high throughput data services, also voice services will work well
  Voice capacity enhancements will come as side product – voice capacity is not an essential target for HEW.

## Slide 4: Simplify Traffic Models
To obtain realistic results with high number of STAs.
  Traffic should be finite buffer (burst) and a single connection should not be overloading the system.
  System should be highly loaded as total.
Generic TCP/IP based traffic is a good starting point as used widely by different services.
  Simplified model could be considered
Both uplink and downlink should be considered simultaneously with different traffic split.
  Same spectrum resource shared between DL and UL.
  Services are bi-directional due to TCP - performance is degraded if either direction is not performing sufficiently well.
  Focus on DL biased traffic split.

## Slide 5: Deployments with high density
High density multi-floor office building
  Presenting a deployment where coordination between APs is possible by network management system.
High density multi-floor apartment building
  Presenting a deployment where coordination between APs is not necessarily possible by network management system.
Stadium or market place
  Public outdoor hotspot.
Each deployment OBSS issues must be considered.
Reasonable AP and STA placement
  APs are not located random manner.
STAs are connected to the best AP from radio link quality point of view.
  All APs should be accessible for STAs.
In all scenarios we should assume single frequency network problem as frequency reuse will happen.
  if we improve single frequency operation those improvements will work when more frequencies are available.
  Simplifies analysis and comparison.

## Slide 6: Metrics: Robustness
Robustness of the connection is essential for high user experience.
  Always when connected obtain certain “minimum bitrate”.
  OBSS – or high interference level are not excuses for the end-user.
Better block than drop
  User experience is worst if connection works for a small duration but then goes down – especially if user is not moving.
For all services minimum bitrate is needed
  even best effort WEB-surfing cannot tolerate long delays.
Typical evaluation criteria is 5 percentile point on:
  Average throughput over simulation rounds above MAC layer
  Average latency over simulation rounds above MAC layer

## Slide 7: Metrics: Spectral Efficiency
Spectral efficiency can be simply maximized by only serving the best STA
  This is clearly not the target of HEW.
Therefore distributions on how resources are used and achieved data rate are essential.
  95 percentile together with 5 percentile (robustness). Averaged over simulation rounds
  PF-scheduler in AP for DL data.
Maximum queuing time needs to be fixed.
  Packets are dropped due to extensive delays.
Different solutions can benefit differently on used deployments and how coverage is defined
  Bits/s/Hz/m^2 over full coverage area to present total system capacity.
  Outage criteria needs be defined and taken into account.

## Slide 8: Other Issues to be discussed
Supported Frequency bands
  2.4GHz and 5GHz, Other?
Backward Compatibility
  Similar as with .11ac.
  More relaxed with some impact to older generations?
  Performance in mixed deployments.
Baseline system capabilities to which comparison is done
  802.11n for 2.4Ghz
  802.11ac for 5GHz

## Slide 9: Conclusion
In this contribution we discussed several basic technical issues that should be addressed during HEW SG work.
It was discussed that several simplifications can be made from analysis point of view in
  Uses Cases
  Traffic models
  Deployment scenarios
From metrics both 5 and 95 percentile distribution point are needed to address robustness and overall system capacity.
  Packets are dropped due to extensive delays
  bits/s/Hz/m^2 over full coverage area to present total system capacity
Additionally we need to address
  Supported frequency bands
  Backward compatibility
  Baseline system capability

## Slide 10: References
[1] 11-13-0313-00 Usage Models for Next Generation Wi-Fi; Osama Aboul-Magd, et. al.