## Slide 1: Synch Frame Follow Up
Date: 2013-5-13
Authors:
Name | Affiliations | Address | Phone | email
Young Hoon Kwon | Huawei | 10180 Telesis Ct, Ste 400, San Diego, CA 92121 |  | younghoon.kwon@huawei.com
Yunsong Yang | Huawei |  |  | yangyunsong@huawei.com
Zhigang Rong | Huawei |  |  | zhigang.rong@huawei.com
Eric Wong | Broadcom |  |  | ewong@broadcom.com
Yongho Seok | LG Electronics | LG R&D Complex Anyang-Shi, Kyungki-Do, Korea |  | yongho.seok@lge.com
Huai-Rong Shao | Samsung |  |  | hr.shao@samsung.com
Alfred Asterjadhi | Qualcomm |  |  | 
Minyoung Park | Intel Corp. |  |  | minyoung.park@intel.com
Tom Tetzlaff | Intel Corp. |  |  | thomas.a.tetzlaff@intel.com
Emily Qi | Intel Corp. |  |  | emily.h.qi@intel.com
Su Khiong Yong | Marvell |  |  | skyong@marvell.com
Hongyuan Zhang | Marvell |  |  | Hongyuan@marvell.com
Sudhir Srinivasa | Marvell |  |  | sudhirs@marvell.com
Jinsoo Choi | LG Electronics |  |  | 
Jeongki Kim | LG Electronics |  |  | 
HanGyu Cho | LG Electronics |  |  | 

## Slide 2
Authors:
May 2013
Name | Affiliations | Address | Phone | email
Matthew Fischer | Broadcom | 190 Mathilda Place, Sunnyvale, CA | +1 408 543 3370 | mfischer@broadcom.com
Rojan Chitrakar | Panasonic |  |  | Rojan.Chitrakar@sg.panasonic.com
Ken Mori | Panasonic |  |  | Mori.ken1@jp.panasonic.com
Simone Merlin | Qualcomm | 5775 Morehouse Dr, San Diego, CA | 8588451243 | smerlin@qualcomm.com
Amin Jafarian | Qualcomm |  |  | 
Santosh Abraham | Qualcomm |  |  | 
Bin Tian | Qualcomm |  |  | 
George Cherian | Qualcomm |  |  | 
Menzo Wentink | Qualcomm |  |  | 
Hemanth Sampath | Qualcomm |  |  | 
VK Jones | Qualcomm |  |  | 
Sun, Bo | ZTE |  |  | sun.bo1@zte.com.cn
Lv, Kaiying | ZTE |  |  | lv.kaiying@zte.com.cn
Chiu Ngo | Samsung |  |  | chiu.ngo@samsung.com
Minho Cheong | ETRI | 138 Gajeongno, Yuseong-gu, Dajeon, Korea | +82 42 860 5635 | minho@etri.re.kr
Jae Seung Lee | ETRI |  |  | jasonlee@etri.re.kr
Hyoungjin Kwon | ETRI |  |  | kwonjin@etri.re.kr
Jaewoo Park | ETRI |  |  | parkjw@etri.re.kr
Sok-kyu Lee | ETRI |  |  | Sk-lee@etri.re.kr
Sayantan Choudhury | Nokia | 2075 Allston Way, Suite 200, Berkeley, CA 94704 | +1 510 599 9268 | sayantan.choudhury@nokia.com
Klaus Doppler | Nokia |  |  | 
Chittabrata Ghosh | Nokia |  |  | 
Sayantan Choudhury | Nokia |  |  | 
Esa Tuomaala | Nokia |  |  | 

## Slide 3
Authors:
Name | Affiliations | Address | Phone | email
Shoukang Zheng | I2R | 1 Fusionopolis Way, #21-01 Connexis Tower, Singapore 138632 | +65-6408 2000 | skzheng@i2r.a-star.edu.sg
Haiguang Wang | I2R |  |  | hwang@i2r.a-star.edu.sg
Wai Leong Yeow | I2R |  |  | wlyeow@i2r.a-star.edu.sg
Zander Lei | I2R |  |  | leizd@i2r.a-star.edu.sg
Yuan Zhou | I2R |  |  | yzhou@i2r.a-star.edu.sg
George Calcev | Huawei | Rolling Meadows, IL USA |  | George.Calcev@huawei.com
Osama Aboul Magd | Huawei |  |  | Osama.AboulMagd@huawei.com
Betty Zhao | Huawei |  |  | Betty.Zhao@huawei.com
David Yangxun | Huawei |  |  | David.Yangxun@huawei.com
Bin Zhen | Huawei |  |  | ZhenBin@huawei.com
ChaoChun Wang | MediaTek |  |  | chaochun.wang@mediatek.com
James Wang | MediaTek |  |  | james.wang@mediatek.com
Jianhan Liu | MediaTek |  |  | jianhan.liu@mediatek.com
Vish Ponnampalam | MediaTek |  |  | vish.ponnampalam@mediatek.com
James Yee | MediaTek |  |  | james.yee@mediatek.com
Thomas Pare | MediaTek |  |  | thomas.pare@mediatek.com
Kiran Uln | MediaTek |  |  | kiran.uln@mediatek.com
Anna Pantelidou | Renesas Mobile |  |  | 
Juho Pirskanen | Renesas Mobile |  |  | 
Timo Koskela | Renesas Mobile |  |  | 
Liwen Chu | STMicroelectronics |  |  | 
George Vlantis | STMicroelectronics |  |  | 

## Slide 4: Background
TGah defined synch frame transmission procedure for uplink traffic, which minimizes the time for medium synchronization for a STA that is changing from Doze to Awake in order to transmit [1]
  When requested by a STA, the AP sends a synch frame at the slot boundary or the target wake time of the STA, if the channel is idle, to help the STA quickly synch to the medium. (optional to AP and STA)
    It is recommended that the AP sends a Short CTS frame defined in 4.4.2.3 as a synch frame.
Therefore, for a STA that requested for a synch frame transmission, the UL-Synch capable AP shall schedule a synch frame at the slot boundary of the STA in the RAW or at the TWT of the STA.

## Slide 5: Background
TGah also defined RAW operation [2]:
  A Restricted Access Window (RAW) is divided in time slots.
  STA wakes up at TBTT and it listens to a Beacon frame that indicates the slot duration for each Restricted Access Window (RAW).
    Slot duration for each RAW may be different
  STA determines its channel access slot assigned by AP.
  STA may sleep before its channel access slot.
  STA shall start to access the channel at the slot boundary of its channel access slot based on EDCA.
  AP indicates whether the following TXOP rule is applied in each RAW:
    A TXOP or transmission within a TXOP shall not extend across a slot boundary
    If the above TXOP rule is applied, the STA does not wait for ProbeDelay when waking up at the slot boundary.

## Slide 6: Issue
In some situations, synch frame operation during RAW period may not be efficient, especially for a RAW for polling/trigger frames:
  If cross slot boundary is not allowed, as a STA does not wait for ProbeDelay when waking up at the slot boundary, the benefit of using synch frame diminishes.
  Slot duration within a RAW for polling/trigger frames may be very short, and in this case overhead due to synch frame can not be ignored.
  If some STAs request to use synch frame but some STAs not, the slot duration for all STAs within a RAW may need to include time for synch frame transmission, as slot duration is defined per RAW.

## Slide 7: Proposed Solution
AP sends synch frame only when synch frame is helpful, for example:
  An AP does not send a synch frame if a STA doesn’t need to wait Probe Delay when it wakes up.
  An AP does not send a synch frame if the overhead of the synch frame is over a threshold.
To be more specific, we propose the following restriction in AP’s synch frame transmission rule:
  An AP should not send a synch frame at each slot boundary within a RAW period if Cross-Slot Boundary transmission is not allowed within the RAW period.
  For a STA that requested for a synch frame transmission, the UL-Synch capable AP shall schedule a synch frame at the slot boundary of the STA at the TWT of the STA, or in the RAW if Cross-Slot Boundary transmission is allowed.
  If NAV setting is requested by a STA, even though Cross-Slot Boundary transmission is not allowed, AP shall send synch frame.

## Slide 8: Benefits
Doesn’t add any additional operational complexity
More efficient RAW operation, especially for polling/trigger frame transmission

## Slide 9: SP
Do you agree that an AP should not send a synch frame at each slot boundary within a RAW period if Cross-Slot Boundary transmission is not allowed within the RAW period unless NAV protection is requested by the STA?

## Slide 10: References
[1] IEEE 802.11-12/0840r1, AP assisted medium synchronization
[2] IEEE 802.11-12/0831r0, Uplink channel access general procedure