## Slide 1: Comments on Relay
Date: 2013-5-12
Authors:

## Slide 4: Introduction
In SFD of 802.11 AH, the relay framework is described as
  The draft specification shall support to use Probe Request for Relay discovery, and optionally, include information on AP-STA link budget.
    The STA initiates the discovery process.
    The STA selects a relay based on the probe responses received.
  However, the detail information of relay discovery is TBD in SFD. This contribution is to add the detail information of relay discovery for completion of SFD.

## Slide 5: Proposals
Relay Discovery IE
  A Relay Discovery IE can be optionally included in Probe Request, Probe Response or Beacon frame.
 | Element | Length | Relay Discovery Info | UL Min Data Rate | UL Mean Data rate | UL Max Data Rate | DL Min Data Rate | DL Mean Data Rate | DL Max Data Rate
Octets | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Common fields for Probe Request, Response and Beacon
Slide 5
Optional fields for Probe Request
Optional fields for Probe Response or Beacon
 | Delay Bound Requirement | Min PHY Rate Requirement
Octets | 1 | 1
 | Channel Utilization | Relay Station Count
Octets | 1 | 1

## Slide 6: Proposals
Relay Discovery Information Field
 | Relay Station Indication | Min Data Rate Included | Mean Data Rate Included | Max Data Rate Included | Delay and Rate Requirement Included/ Utilization and Count Included | Information Not Available | Optional Information Not Available | Reserved
Bits | B0 | B1 | B2 | B3 | B4 | B5 | B6 | B7

## Slide 7: Proposals
Relay Discovery Information Field (Continued)
  Relay Station Indication bit: the relay station shall set this field to “1”. Otherwise, this bit shall be set to “0”.
  Min Data Rate Included bit: if the UL and DL min data rate are included in the Relay Discovery IE, this bit shall be set to “1”. Otherwise, it shall be set to “0”.
  Mean Data Rate Included bit: if the UL and DL mean data rate are included in the Relay Discovery IE, this bit shall be set to “1”. Otherwise, it shall be set to “0”.
  Max Data Rate Included bit: if the UL and DL max data rate are included in the Relay Discovery IE, this bit shall be set to “1”. Otherwise, it shall be set to “0”.

## Slide 8: Proposals
Relay Discovery Information Field (Continued)
  Delay and Rate Requirement Included / Utilization and Count Included bit :
  In Probe Request, this bit means “Delay and Rate Requirement Included”. If the “Delay Bound Requirement” and “Min PHY Rate Requirement” fields are included in Relay Discovery IE, this bit shall be set to “1”. Otherwise, it shall be set to “0”.
  In the Probe Response or Beacon, this bit means “Utilization and Count Included” . if the “Channel Utilization” and “Relay Station Count” fields are included in the Relay Discovery IE, this field shall be set to “1”. Otherwise, it shall be set to “0”.
  Information Not Available bit: this bit shall be set to “1” if the relay station cannot provide requested information in the fixed fields of Relay Discovery IE. Otherwise, it shall be set to “0”.
  Optional Info Not Available bit: this bit shall be set to “1” if the relay station cannot provide the requested information of the optional fields. Otherwise, it shall be set to “0”.

## Slide 9: Proposals
UL and DL Min/Mean/Max Data Rates
  These fields shall be included if the bit of “Min Data Rate Included”, “Mean Data Rate Included”, and “Max Data Rate Included” is set to “1”.
  In the Probe Request frame, those fields denote the UL and DL minimum data rates, UL and DL mean data rates, or UL and DL maximum data rates of the direct path between the station and AP in the step of 100 kbps if they are included.
  In the Probe Response frame or beacon frame, those fields denote the UL and DL minimum data rates, UL and DL mean data rates, or UL and DL maximum data rates of relay link between the relay node and AP in the step of 100 kbps if they are included.

## Slide 10: Proposals
Delay Bound Requirement
  This field is included only in Probe Request if the “Delay and Rate Requirement Included” is set to “1”.
  This field indicates the delay bound requirement of the channel access through the relay node.
Min PHY Rate Requirement
  This field is included only in Probe Request if the “Delay and Rate Requirement Included” is set to “1”.
  This field indicates the minimum PHY data rate requirement set by the requesting station.
  The responding station determines whether or not to respond the Probe Request according to received information such as UL and DL Min/Mean/Max Data Rates, Delay Bound Requirement and/or Min PHY Rate Requirement, which depends on the implantation.

## Slide 11: Proposals
Channel Utilization
  This field is included only in the Probe Response if the “Utilization and Count Included” is set to “1”.
  This field denotes the ratio of time that relay observes the busy level on the relay link between the relay and AP. “255” means 100% busy and “0” means idle.
Relay Station Count
  This field is included only in the Probe Response if the “Utilization and Count Included” is set to “1”.
  This field denotes the number of stations currently associated with the relay node.

## Slide 12: Straw Poll
Do you support the new Relay Discovery IE defined in page 5 - 11?
  Yes:
  No:
  Abstain: