## Slide 1: ACK Indication and EIFS
Date: 2013-05-13
Authors:

## Slide 4: Introduction
11ah is currently using the following ACK indication field in the SIG for response frames:
It was intended to help a receiving STA decide whether to defer medium access in order to protect immediate response (ACK, BA, …)[1]
  And, based on that indication a receiving STA could go to sleep and/or calculate EIFS
However, ACK/CTS/BA can be normal or NDP packets (which have different lengths)
  Also, asymmetric BA is possible in 11ah (which does not follow MCS selection rules)
All these different types of frames make it difficult for 3rd party STAs to defer correctly
  ACK indication should enable prediction of the expected response length (rather than type)
    To allow 3rd party STAs correctly calculate EIFS or amount of time it can go to sleep
Intended receiver uses ACK policy and other rules specified in the spec. to identify the type of response

## Slide 5: Proposal: ACK Indication in SIG
Propose to re-map the ACK Indication in the SIG field to indicate the duration of
  NDP Control Response frames
  Normal Control Response frames
  Long Response frames (Speed Frame Exchange and Asymmetric BA)
Allows third party STAs to correctly calculate the duration of the response
  Enables dynamic EIFS calculation based on PHY header information only
    Independently of which MAC header is used (normal and short)
The intended receiver can determine its ACK policy based on
  Existing ACK policy rules and control response type negotiation as currently defined in the standard
ACK Indication in SIG | Response Type
0 | No Response
1 | NDP Response
2 | Normal Response
3 | Long Response

## Slide 6: ACK Indication 0: No Response
ACK Indication in SIG Field of received frame
  ACK Indication = 0: No Response
    No immediate response is expected
Third party receivers calculate EIFS as
  EIFS = DIFS
    Calculation is based on the value of ACK indication
      No need to decode the MAC header of received frame
And it may go to sleep for PPDU duration
  Once it has identified that it is not the intended receiver
    E.g., after SIG or MH of received frame
BW | 1MHz | >=2MHz
Curr. EIFS [ms] | 1.8 | 0.9?
Prop. EIFS [ms] | 0.26 | 0.26
Delta [slots] | 30 | 12
SIG
MH
Data
DIFS
STD EIFS
Delta
Prop. EIFS
Receiver invokes EIFS (RID) if either:
Goes to sleep after SIG/MH (new in 11ah)
There is no duration field in MH (new in 11ah)
FCS fails (as in 11ac)
FCS
Correct post EIFS (NAV) back off start

## Slide 7: ACK Indication 1: NDP Response
ACK Indication in SIG Field of received frame
  ACK Indication = 1: NDP Response
    Aggregation = 0  NDP ACK or NDP CTS
    Aggregation = 1  NDP ACK or NDP BA
Third party receivers calculate EIFS as
  EIFS = aSIFSTime + DIFS + NDPTxTime
    Calculation is based in the value of ACK indication
      NDPTxTime depends on BW of NDP response frame
        560us for 1MHz and 240us for >=2MHz NDP frames
  And they may go to sleep for PPDU duration + SIFS + NDPTxTime
Note: All NDP response frames of a given BW have the same duration
BW | 1MHz | >=2MHz
Curr. EIFS [ms] | 1.8 | 0.9?
Prop. EIFS [ms] | 0.98 | 0.66
Delta [slots] | 16 | 5
NDP
SIG
MH
Data
DIFS
Correct post EIFS (NAV) back off start
STD EIFS
Delta
Prop. EIFS
FCS
Receiver invokes EIFS (RID) if either:
Goes to sleep after SIG/MH (new in 11ah)
There is no duration field in MH (new in 11ah)
FCS fails (as in 11ac)

## Slide 8: ACK Indication 2: Normal Response
ACK Indication in SIG Field of received frame
  ACK Indication = 2: Normal Response
    Aggregation = 014 Byte Resp. (ACK, STACK or CTS)
    Aggregation = 132 Byte Resp. (BA, BAT, A-MPDUed ACK, TACK)
Third party receivers calculate EIFS as
  Aggregation = 0: EIFS = aSIFSTime + DIFS + ACKTxTime
  Aggregation = 1: EIFS = aSIFSTime + DIFS + BATxTime
    The response MCS is determined based on the PHY mandatory MCS set
  TxTime depends on response frame’s BW and MCS
  And they may go to sleep for PPDU duration + SIFS + RespTxTime
BW | 1MHz |  | >=2MHz | 
Curr. EIFS [ms] | 1.82 |  | 0.9 | 
Prop. EIFS [ms] | 1.82 | 2.78 | 0.9 | 1.1
Delta [slots] | 0 | -35 | 0 | -4
BA (MCS10)
SIG
MH
Data
DIFS
Correct post EIFS (NAV) back off start
STD EIFS
Prop. EIFS
Delta
FCS
Receiver invokes EIFS (RID) if either:
Goes to sleep after SIG/MH (new in 11ah)
There is no duration field in MH (new in 11ah)
FCS fails (as in 11ac)

## Slide 9: ACK Indication 3: Long Response
ACK Indication in SIG Field of received frame
  ACK Indication = 3: Long Response
    Speed frame exchange (asymmetric BA)
Third party receivers calculate EIFS as
  EIFS = aSIFSTime + DIFS + Max PPDUTxTime
    Calculation is based only in the value of ACK indication
EIFS shall be truncated by the TXer by transmission of a frame with ACK Indication <3 after the invited response (e.g., NDP ACK)
The response frame shall have ACK Indication 1 (NDP Response), so that the truncating NDP is also protected

## Slide 10: VHT Single MPDU
VHT single MPDU can have two possible responses
  ACK Indication = 1: NPD ACK
  ACK Indication = 2: 32 Byte response
A 32 Byte response can be
  ACK in A-MPDU with 4 delimiters (4+14+2+4+4+4 = 32)
  TACK (= 32)

## Slide 11: Dynamic EIFS Table
EIFS varies significantly for different control response types (min 664us, max 2784us)
  Proposed ACK indication allows all STAs to correctly calculate EIFS based on information available in the PHY Header of received packet
  Up to 16 (35 with no MCS rules!) slots difference between lowest and largest EIFS values for 1MHz
  Up to 9 slots difference between lowest and largest possible EIFS values for >=2MHz
*Table is for transmissions with MCS10@1MHz, MCS0@2MHz and MCS4 for both 1 and 2MHz
Bandwidth [MHz] | Response Type | Response Rate [Mbps] MCS0/MCS4 | Existing EIFS [ms] | Dynamic EIFS [ms]
1 | NDP ACK/BA | 0.15 | 1.824 | 0.984
1 | Normal ACK | 0.15/1.2 | 1.824 | 1.824/1.184
1 | Normal BA | 0.15/1.2 | 1.824 | 2.784/1.304
2 | NDP ACK/BA | 0.65 | 0.904 | 0.664
2 | Normal ACK | 0.65/3.9 | 0.904 | 0.904/744
2 | Normal BA | 0.65/3.9 | 0.904 | 1.104/784

## Slide 12: EIFS Rules - Summary
*EIFS calculation is based on rules described in slides 7-10
ACK Indication | Response | Aggregation | Response Length | EIFS Calculation*
0 | No Response | Any | 0 | DIFS
1 | NDP | Any | NDP | SIFS + DIFS + NDPTxTime
2 | Normal | 0 | NDP + 14 Bytes | SIFS + DIFS + ACKTxTime
 |  | 1 | NDP + 32 Bytes | SIFS + DIFS + BATxTime
3 | Long | Any | Max PPDU | SIFS + DIFS + MaxPPDUTxTime

## Slide 13: Straw Poll 1
Do you support the ACK indication as defined in slide 5?

## Slide 14: Straw Poll 2
Do you support the EIFS calculation for different ACK indications as described in slide 12?

## Slide 15: References
[1] 11-12-0119-00-00ah-early-ack-indication