## Slide 1
Slide 1
Authors:
Combining Process in Virtual CS Mechanism for 802.11ah
Date: 2013-05-06
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 1

## Slide 2
Slide 2

## Slide 3
Slide 3

## Slide 4
Slide 4
Abstract
This contribution provides specific process for combining RID and NAV in the virtual carrier sense (CS) mechanism used for 802.11ah STAs.

## Slide 5
Virtual CS mechanisms for 802.11ah (1/2)
The 11ah SFD has defined that two virtual CS mechanisms shall be provided by the MAC.
  The first mechanism is referred to as the NAV mechanism.
  The second virtual CS mechanism is referred to as the Response Indication Deferral (RID).
The CS mechanism needs to combine the NAV state, RID and the STA's transmitter status with physical CS to determine the busy/idle state of the medium.
Slide 5

## Slide 6
Virtual CS mechanisms for 802.11ah (2/2)
RID begins immediately after the reception of a frame with RXVECTOR parameter ACK_INDICATION that has a value of ACK or BA or Not ACK, BlockAck or CTS.
A STA that is undergoing RID shall not initiate a non-response transmission.
Slide 6

## Slide 7
Comparison of two Virtual CS mechanisms
The features of RID mechanism are:
  The value of RID is obtained based on a rough estimation. When ACK_INDICATION is Not ACK, BlockAck or CTS, RID continues for MAX_PPDU + ACK + 2 * SIFS or until PHY-RXSTART.indication, whichever comes first.
  The value of RID is always updated after the reception of a frame with RXVECTOR parameter ACK_INDICATION.
The features of NAV mechanism are:
  The value of NAV is accurate based on the “Duration” field of the received frame.
  STAs update their NAV with the received Duration field only when the new NAV value is greater than the current NAV value.
Slide 7

## Slide 8
Issue and Solution Principle
  The STA needs to combine the NAV state, RID and the STA's transmitter status with physical CS to determine the busy/idle state of the medium. And how to perform the combining process needs to be specified.
  As one principle for the combining process, when Duration is available in the received frame, it’s preferred to use Duration instead of RID since Duration is more accurate than RID to determine the medium state.
    If a third-party STA only obtains ACK_INDICATION
      the Virtual CS mechanism should be based on both NAV and RID, and
      the CS mechanism shall combine the conditions NAV != 0, RID != 0, STA’s transmitter status = “not transmitting” with physical CS = idle to determine the busy/idle state of the medium.
    If a third-party STA obtains both of ACK_INDICATION and Duration from a received frame,
      the Virtual CS mechanism should be based on NAV only, and
      the CS mechanism shall combine the NAV!=0 and the STA‘s transmitter status = “not transmitting” with physical CS = idle to determine the busy/idle state of the medium.
Slide 8

## Slide 9
Proposal
  We propose an unified combining process as follows:
    the Virtual CS mechanism should be based on both NAV and RID, and
    If the STA obtains both ACK Indication and Duration from the single reception, the STA shall reset RID to zero.
    The medium condition at the MAC is BUSY if PHY_CS indicates BUSY or the NAV counter has a non-zero value or the RID counter has a non-zero value or STA transmitter status is equal to “transmitting”.
      MediumBUSY = (PHY_CS == BUSY) OR ( NAV != 0) OR (RID != 0) OR (STA transmitter status == transmitting)
Slide 9

## Slide 10
Conclusion
  In this contribution, we proposed to specify how a STA combines the RID, NAV and the STA‘s transmitter status with physical CS to determine the busy/idle state of the medium with an unified combining process.
Slide 10

## Slide 11: Straw-Poll
Do you support the unified CS mechanism combing process as defined in slide 9?
Y
N
A
Slide 11

## Slide 12: References
[1] IEEE Std 802.11™-2007
[2] IEEE802.11-13/1137r14SFD
Slide 12

## Slide 13
Thank you!
Slide 13