## Slide 1: HEW scenarios and evaluation metrics
Date: 2013-05-16
Authors:

## Slide 2: Abstract
This document details some possible scenarios, evaluation methodologies and metrics for consideration by HEW SG in its efforts to develop PAR and 5C

## Slide 3: Outline
The motion in March meeting creating HEW SG was based on a strawpoll stating the following aim:
  to enhance 802.11 PHY and MAC in 2.4 and 5GHz with a focus on:
    Improving spectrum efficiency and area throughput
    Improving real world performance in indoor and outdoor deployments
      in the presence of interfering sources, dense heterogeneous networks
      in moderate to heavy user loaded APs
We presented in 13/0331r5 [1] some usage models and deployment scenarios, and identified key problems for HEW to solve corresponding to the above focus points
In this document, we discuss some approaches HEW SG may consider to develop full scenarios, methodologies and metrics
  to allow for efficient evaluation of proposed techniques – balancing real-world accuracy and reasonable simulation complexity

## Slide 4: Mapping usage models to evaluation scenarios
In [1] we proposed HEW focus on improving efficiency in three categories:
  dense networks with large no. of STAs
  dense heterogeneous networks with large no. of APs
  outdoor deployments
In the next slide we suggest five possible real-world scenarios for evaluation, comprising:
  combinations of key illustrative usage models that co-exist in these scenarios
  mapping of these usage models to the above three categories
  the corresponding key issues for HEW to address

## Slide 5
Scenario | Usage model | Managed? | Large no. of STAs | Large no. of APs | Outdoor | Key issues for HEW
Urban outdoor | Offload to outdoor hotspots | Yes |  |  |  | - OBSS interference - PHY robustness - Mgmt frame o/h - User multiplexing
 | Offload to Community Wi-Fi | Partial |  |  |  | 
 | D2D discovery (smart cities, etc) | No |  |  |  | 
Station / shopping mall | Offload to indoor hotspots (e.g. co-deployed with LTE picocell) | Yes |  |  |  | - OBSS interference - Mgmt frame o/h - User multiplexing - Fairness and load balancing
 | Portal/offload to in-store AP | No |  |  |  | 
 | D2D discovery (retail, etc) | No |  |  |  | 
Stadium / auditorium | Portal/offload to dense hotspots | Yes |  |  |  | - OBSS interference - User multiplexing
 | Cellular tethering | No |  |  |  | 
Home (dense apartments) | Offload to home gateway, IPTV | No |  |  |  | - OBSS interference
 | Wireless display (STB to TV, etc) | No |  |  |  | 
Enterprise | SaaS, UCC, HD video conference | Yes |  |  |  | - OBSS interference - User multiplexing - Traffic prioritization
 | Wireless display (desktop, projector), storage and docking | No |  |  |  | 
 | Private APs (personal, neighbor) | No |  |  |  | 

## Slide 6: Considerations on scenarios definition
Each real-world scenario is formed from the layering of multiple (independent) networks corresponding to multiple usage models
  multiple scenarios may be needed to efficiently and realistically quantify the benefits of proposed techniques with respect to all the key issues
The focus of HEW implies greater use of system-level (vs link level) simulations than in 11n or 11ac, especially to model the impact of OBSS
  however, evaluation requirements should not be unnecessarily arduous since extremely high simulation complexity would discourage submission of proposals
It may make sense to use complete real-world scenarios to evaluate “down-selected” / “full” proposals, while allowing proposals of specific techniques to be evaluated using just certain layers/elements of the scenarios
  reduce simulation complexity to the minimum needed for accurate evaluation

## Slide 7: Illustration of a real-world scenario
enterprise-managed ESS
for corporate intranet
wireless display/docking at each desk in office booth area
wireless HD projector (teleconference)
standalone BSS for private network
neighboring building ESS
Enterprise scenario
Figure is simplified for illustration – does not represent an actual scenario proposal

## Slide 8: Illustration of corresponding partial scenarios
To evaluate techniques to improve efficiency for corporate ESS in presence of high density wireless display pairs
To evaluate techniques to improve efficiency in an ESS with regular grid layout
To evaluate techniques to improve link-level performance for a particular application (e.g. UHDTV)
 tentative proposal of scenario parameters given in Appendix

## Slide 9: Considerations on frequency reuse
Channel selection/assignment assumptions may have a major impact on simulation complexity and apparent efficiency gains of proposed techniques
Dynamic channel selection, for both managed and unmanaged networks, may be assumed for evaluation of certain proposed techniques
  e.g. sensing-based or coordinated channel selection techniques
  simulations would be run over all channels (complete 2.4 and/or 5 GHz bands)
Static channel assignment may be a default assumption for other techniques
  unmanaged networks: each AP operates on randomly assigned channel
    exception: WFD pairs operating in concurrent mode with an infrastructure network typically use the same channel (due to single radio)
  managed networks: channel assignment is planned, typically frequency reuse = 3
    we may also consider frequency reuse = 1 for certain proposed techniques

## Slide 10: Illustration of hotspots with frequency reuse = 3
e.g. hotspots using social channels on 2.4 GHz
Channel 1 Channel 6 Channel 11
minimum Rx sensitivity / CCA threshold
Can consider each channel separately
  e.g. Channel 1
Frequency reuse occurs between non-overlapping parts of dashed circles
  independent CCA processes in each circle
STAs at cell edge operate at relatively high MCS
  since cell edge well inside dashed circle (= MCS 0)
  good robustness at cell edge

## Slide 11: Illustration of hotspots with frequency reuse = 1
e.g. hotspots using social channels on 2.4 GHz
Channel 1
Wider system bandwidth and/or reduced interference with other networks (operating on different channels) are possible
To enable effective frequency reuse (non-overlapping dashed circles), STAs at cell edge will operate close to MCS 0
  e.g. through reduction of Tx power
  leads to poor robustness at cell edge
May be a target approach for new techniques that can mitigate this issue
  each frequency reuse scheme may imply a different technical solution
minimum Rx sensitivity / CCA threshold

## Slide 12: Considerations on traffic models
Appropriate traffic models may be considered for each usage model (layer)
  especially to appropriately model OBSS interference
For offload usages, the approach of 3GPP may be reused
  full buffer (simplicity) and non-full buffer (realism) – TR36.814 [2]
Other usage models may have specific characteristics
  e.g. fixed-bandwidth RTP stream for wireless display
  e.g. high prevalence of management frames for D2D discovery and idle STAs
Some usage models may be modeled with a specific traffic mix
  especially to model impact of multiplexing mixed traffic from different users on intra-BSS MAC efficiency
For example, hotspot traffic may typically comprise a mix of large packets (web, video, etc) and also small packets (ACKs, etc)

## Slide 13: Evaluation metrics
For system-level evaluation of regular grid ESS networks (e.g. hotspots), the classical metrics used by 3GPP may be considered:
  Cell edge (5%) and median (50%) throughput, aggregate capacity per cell
For multi-layer (heterogeneous) and irregular networks, “area spectral efficiency” may also be a useful global metric
In certain scenarios, we imagine other metrics may also be valuable to evaluate in the context of specific user requirements, e.g.
  For hotspots at a train station, how many users can simultaneously achieve at least a minimum throughput (e.g. 2 – 5 Mbps)
    correlating to satisfactory QoE for most mobile usages
  For wireless display at desk booths in enterprise, how many such connections can coexist in an office without adversely the corporate intranet ESS

## Slide 14: Summary
A layered approach to defining key scenarios may help to achieve consistency in evaluation methodologies while allowing appropriate balance between real-world accuracy and simulation complexity
Dynamic and static channel assignment schemes may both be appropriate
  For static case, we may consider frequency reuse = 3 as well as 1 and/or others
Accurately modeling of interference and MAC efficiency may require consideration of appropriate non-full buffer and mixed traffic models
Classical system-level evaluation metrics used by 3GPP may be candidates for evaluating single, regular-grid ESS networks
  Other metrics such as area throughput and scenario-specific metrics may also be considered

## Slide 15: References
[1] IEEE 802.11-13/0331r5 - L. Cariou - “High-Efficiency WLAN”
[2] 3GPP TR 36.814 v9.0.0 – “Further Advancements for E-UTRA physical layer aspects”
IEEE 802.11-09/0161r2 – R. de Vegt – “802.11ac Usage Models Document”
Aruba Networks white paper “WLAN RF Architecture Primer: Single-Channel and Adaptive Multi-Channel Models”

## Slide 16: Appendix - Proposal of complete scenarios
Scenario | Usage model | Managed? | Topology layers
Urban outdoor | Offload to outdoor hotspots | Yes | 1 AP/25,000m2 in grid, 2-4 SPs, 50-100 STAs/AP
 | Offload to Community Wi-Fi | Partial | 1 AP/house randomly located, 1-5 STAs/AP
 | D2D discovery (smart city, etc) | No | 1 AP/100-10,000m2, 50-100 STAs/2,500m2
Station / shopping mall | Offload to indoor hotspots (e.g. co-deployed with LTE picocell) | Yes | 1 AP/2,500m2 in grid, 2-4 SPs, 50-100 STAs/AP
 | Portal/offload to in-store AP | No | 1 AP/625m2 randomly located, 1-10 STAs/AP
 | D2D discovery (retail, etc) | No | 1 AP/100-1,000m2, 50-100 STAs/2,500m2
Stadium / auditorium | Portal/offload to dense hotspots | Yes | 1 AP/100m2 in grid, 1 SP, 50-100 STAs/AP
 | Cellular tethering | No | 1 AP/50m2 in grid, 1-3 STAs/AP
Home (dense apartments) | VoD/IPTV and web (HGW) | No | 1 AP/house randomly located, 10-50 STAs/AP
 | Wireless display (e.g. STB-TV) | No | 0-3 pairs/house, random AP location, STAs 2-10m from AP
Enterprise | SaaS, UCC, HD video conf. | Yes | 1 AP/250m2 in grid, 1 SP (+1 neighbor), 20-50 STAs/AP
 | Wireless display (desktop, projector) and storage | No | 0-50 pairs/250m2, STAs 0.5-3m from AP
 | Private APs (personal, neighbor) | No | 1-5 APs/250m2 randomly located, 1-5 STAs/AP