## Slide 1
Date: 2013-05-12
Authors:
Non-TIM Allocation Followup

## Slide 2: Authors:

## Slide 3
Authors:

## Slide 4: Introduction
Tgah accept concept of window for non TIM STAs only[1]
  AP may indicate to TIM STAs RAW information during which no TIM STA is allowed to contend.
  AP can group non-TIM STAs supporting TWT in the same group. Then, if assigned TWTs are in the current beacon interval, AP can protect TWTs by RPS IE included in beacon from the channel access of other groups of STAs listening the beacon.
  This minimizes contention between non-TIM STAs and other TIM STAs.
In this contribution, we propose to signaling methods for resource protection of non-TIM STAs.

## Slide 5: Problem
AID grouping of TWT STAs should be performed for indicating which AID range of STAs is allowed to operate at the assigned RAW.
  According to their TWTs and wakeup intervals, their TWTs are contiguously assigned.
  After each TWT setup, AP should reassign the TWT STA’s AID for RAW protection.
However, a TWT STA can make multiple TWTs with different wakeup intervals.
Also, even a TIM STA can make TWT agreement with NDP Paging setup, e.g. for flows having the periods less than one beacon interval.
In these cases, to incorporate TWT STA’s AID into RAW Group subfield in the RPS IE, AP should reassign the STA’s AID per RAW. It can be burden on AP.

## Slide 6: Various TWT setups
From the TWT protocol perspective, AID grouping of TWT STAs is not required to do so:
  1) As to multiple TWTs setup, a TWT agreement can identified by a flow identifier. For example, proposed Tgah Draft[2] suggested “A single pair of STAs can create multiple TWT agreements. Each unique TWT agreement is identified by a Flow Identifier.”
  2) As to TWT grouping, one TWT group is identified by Group ID representing a set of STAs with adjacent TWT values, not by their AID grouping.
  3) An NDP Paging frame sent from a NDP Paging Requester is identified by its P-ID fixed when NDP Paging setup.

## Slide 7: 1 bit indication proposal
To protect the TWTs from TIM STAs as RAW, we propose to define new 1 bit of RPS IE which indicates the resource for TWT STAs.
  STAs listening the beacon should check the 1 bit of RPS IE whether the RAW is for TWT STAs or not.
  Checking AID range by using the RAW Group subfield is not needed.
  It can also be applied to the resource for NDP paging STAs.
Short RAW Description
indication
Short RAW Description
indication

## Slide 8: Additional RAW for non-TIM STAs
Note that Non-TIM STA = TWT STA + unscheduled active polling STA.
So-called ‘non-TIM’ RAW is a RAW that only non-TIM STAs are allowed to access medium, in order to minimize contention between non-TIM STAs and other TIM STAs.
In some cases, the ‘non-TIM’ RAW is needed
  AP wants for non-TIM STAs to defer channel access to a RAW in order to reduce contention within the scheduled slot/RAW, which is caused by unexpected access by non-TIM STAs such as wakeup of unscheduled active polling STAs.
  In case that before TWT is assigned for a STA requesting TWT or TWT STA does not finish data exchange within a TWT, the STA has no scheduled TWT and thus operates as unscheduled active polling STA.

## Slide 9: Resource Protection of unscheduled active polling STAs
Method 1 - Using AID range of unscheduled active polling STAs as a normal RAW
  Their AID grouping done at association
  RAWs for unscheduled ones mean that only unscheduled active polling STAs are allowed to contend => both TIM STAs and TWT STAs are not allowed to access
  Good for the deferred channel access of only unscheduled active polling STA
  However, unnecessary fields of RPS IE are used
Method 2 - To reduce signaling overhead, extending 1 bit indication of TWT STAs to unscheduled active polling STAs for non-TIM RAW
  In method 1, exact AID range interpretation may not be applied to TWT STAs because TWT STAs don’t check beacons.
  Even when TWT STAs check non-TIM RAW indication of the RPS IE set to 1, if their assigned TWTs are not included in the RAW, they are not allowed to access.
  Thus, AP can make RAW for unscheduled active polling STAs by using the 1 bit indication for short RAW description in slide 7.

## Slide 10: Conclusion
In this contribution, we propose to specify how to signal RAW for non-TIM STAs.
  No AID reassignment needed for STA grouping
  Unnecessary RAW Group field of RPS IE omission
  Extension to unscheduled active polling STAs

## Slide 11: Straw Poll
Do you support , in TGah Spec Framework document, to introduce 1 bit Short RAW Description indication in RPS IE and frame format as in slide 7,
  When the bit is set, the access is restricted to previous identified STAs, e.g. TWT STAs or doze awake cycle rescheduled STAs ?
Yes:
No:
Abstain:

## Slide 12: References
[1] IEEE 802.11-12-0867-00-00ah ETRI non-TIM Allocation
[2] IEEE 802.11-13-0500-00-00ah INTEL Proposed TGah Draft Amendment