## Slide 1: Sub-Setting
Date: 2013-11-12
Authors:

## Slide 2: Abstract
This presentation describes alternative solutions to the general sub-setting and “per-port” VLAN mapping problems. This would help support modelling infrastructure associations between 802.11ak stations and 11ak APs as point-to-point links.

## Slide 3: 802.11ak AP-> STA “Sub-Setting” Need

## Slide 4: 802.11ak AP-> STA “Sub-Setting” Need
Assume IEEE 802.11 Access Point (AP) to client station (STA) associations are modeled as a set of point-to-point (p2p) links.
  But 802.11, like other wireless media is inherently a multi-access link type media with many stations physically capable of receiving a transmission, not p2p.
For unicast data, things work fine as any station to which a frame is not addressed just discards it so it looks like p2p.
  For multicast or broadcast data frames in 802.11, the AP always transmits it to the associated STAs (if necessary, a STA unicasts the frame to the AP first). In this case, there are three problems as listed on the next slide.

## Slide 5: 802.11ak AP-> STA “Sub-Setting” Need
When an AP sends a multi-destination data frame, there are reasons why only some STAs should accept it and possibly receive different versions of the frame:
  If it was sent to the AP by a STA, that STA should not get the data frame back (the “reflection” problem).
  If spanning tree or other protocols block the “p2p port” at the AP, the STA should not receive it (the “sub-setting” problem).
  To model bridge port VLAN/priority mapping, different STAs should receive the data frame with different tags or no tags (can be viewed as sub-setting for each tagging).

## Slide 6: 802.11ak AP-> STA “Sub-Setting” Need
For more on these problems, see the “Sub-Setting” parts of 11-12/1441r1, “Problem list for P802.1Qbz / P802.11ak point-to-point model”
Generally speaking, these problems apply only to data frames. 802.11 Control / management frames and the like are always between STAs and can be handled by existing mechanisms.

## Slide 7: Alternative Solutions

## Slide 8: Alternative Solutions
Current solutions cannot adequately solve the problems:
Serial unicast:
  The simplest solution would be to not use broadcast/multicast at all. Just unicast data frames from the AP separately to each STA that should receive the frame with the tagging appropriate for that STA. But if there are multiple STAs, this will use up much more airtime that multicast / broadcast would use thus blocking the channel.

## Slide 9: Alternative Solutions
Current solutions (cont):
Blocking port to STA:
  The desire to block the “p2p” links for data to some STAs at the AP could be accomplished by blocking STA input ports instead. But you would need a control/confirmation protocol. During the time period when you don’t know if the AP to STA command has taken effect, you must use serial unicast or the like.

## Slide 10: Alternative Solutions
Current solutions (cont):
VLAN mapping at STA input:
  The problem of wanting different tag mappings on multicast data frames from the AP for different STA receivers could be solved by configuring the STAs so that the tag mapping is done at the STA input. But that requires a new control protocol between the AP and STAs that includes an acknowledgement of when the configuration has taken effect. Before receiving that acknowledgement, the behavior of the STA is unknown and some other strategy, such as serial unicast, must be used.

## Slide 11: Alternative Solutions
Current solutions (cont):
Special Multicast Addresses:
  It has been proposed to solve sub-setting for data frames by having a special multicast MAC upper 24 bits so that you could bit encode which STA is to receive the frame into the lower 24 bits. This has a 24-station limit problem and the problem that if different tagging is required, multiple copies must still be sent. Alternatively, you could dynamically negotiate which set of STAs some special multicast addresses referred to using a protocol similar to 802.1BR, but that requires a negotiation protocol between AP and STA and has an indeterminate behavior window of time.

## Slide 12: Alternative Solutions
Explicit Receivers:
An 11ak AP can send multi-destination MSDUs to 11ak STAs in a special frame that includes:
  The list of 11ak STAs to accept the frame (or the list of 11ak STAs to drop the frame)
  Optional tagging specification for the frame for each STA
  May require sending two frames, one for 11ak STAs and one for legacy STAs, which other solutions also require.
This solution solves all the problems with one mechanism.

## Slide 13: Comparison
(1) Some airtime taken up by protocol to tell non-AP STAs about blocking, VLAN mapping and by serial unicast during period of uncertainty before command has been acknowledged. (2) Some overhead for aggregation and control block but some savings by abbreviating common tagging across aggregated PDUs.
 | Airtime | Protocol Required | Data Overhead Bytes | VLAN / Priority Mapping
Serial Unicast | Issue | Good | Terrible in the General Case | Good
Command non-AP STA | OK (1) | Issue | Good | Good
Special Multicast | OK (1) | Issue | 6 | Issue
Explicit Receiver | Good | Good | 12+/- (2) | Good

## Slide 14: Details of an Explicit Receivers Solution

## Slide 15: An Explicit Receivers Solution
Using A-MSDU aggregated frames may help because, if the additional information on receivers and tagging is the same for multiple frames, it need only be given once. But a similar solution could be based on other frame types.

## Slide 16: The 802.11ak Aggregated Frame
802.11ak A-MSDU
Aggregated
Frame Header
Control Block
802.11ak A-MSDU frame indicated by special multicast DA.
MSDU 1
…
First block inside 11ak A-MSDU frame is special. It specifies which STAs should process the rest of the frame(s) and with what tags (prefix bytes). See next slide. (11-13/0693 suggests using a special tag but there does not appear to be a provision for tags at the aggregate level.)
Frame or frames of actual data with true source and destination MAC addresses.
MSDU 2
(Could use A-MPDU. Restriction of Aggregated frames to unicast fixed in 802-11aa.)

## Slide 17: Special Control Block Format
11ak Control
Block
SubType = 0 (4-bits)
Length= 12-bit length of Control
Block in bytes
8 flag bits
Exclude bit = 0 -> include
Exclude bit = 1 -> exclude
DPsize = 8-bit size of default
prefix in bytes
DefPF = Default Prefix (tagging)
AID = 16-bit Association
IDentifier
…
List of AID Items.
If Flags exclude bit is 1, each AID Item is just an 2-byte AID. The MSDUs in the aggregation are processed by the STAs whose AID is NOT listed. If a STA’s AID is listed, it drops the A-MSDU.
The next slide give the format of an AID Item when the top bit of the flags is 0 (include list).
AID Item
AID Item
AID Item
Flags
DPsize
DefPF
SubType
Length

## Slide 18: “Include List” AID Item Format
Control Word = 8 bits of flags +
8 bits of prefix info size in bytes
Top Flag bit = 0 -> use specified prefix
= 1 -> use default prefix
11ak
Control
Block
Other Include List AID Items formatted the same as the first.
AID
Item
AID Item
AID Item
Control Info
Prefix Info
AID
With an Include List indicated by the Control Block, if the STA’s AID is NOT in the list, the 11k non-AP STA drops the aggregated frame. If the STA’s AID is in the list, the STA processes the MSDU(s) in the rest of the A-MSDU but, before processing each of them, inserts the “Prefix Info” (or DefPF info if flag set) into the MSDU just after the DA/SA and before the rest of the MSDU.
…

## Slide 19: Some Additional Notes
AP can combine unicast of and new A-MSDU aggregated multi-casting of a data frame as it chooses.
AP can send to all 11ak STAs by just specifying a null list of AIDs to be excluded.
The “prefix information” is normally tagging information but can be arbitrary pre-fix bytes. For example, when sending several IPv4 frames with the same VLAN, the VLAN tag and IPv4 Ethertype can be abstracted out into the default prefix information saving some space.

## Slide 20: References
IEEE Std. 802.11-2012
12/1207r1, “802.11 GLK Draft PAR”
12/1441r1, “Problem list for P802.1Qbz / P802.11ak point-to-point model”
13/0693r0, “Comparison of Receiver Subset Techniques”