## Slide 1: Active Scanning for 11ah Follow Up 2
Date: 2013-05-10
Authors:
Name | Affiliations | Address | Phone | Email
Jae Seung Lee | ETRI | 161 Gajeong-dong, Yuseong-Gu, Daejoen, Korea | +82 42 860 1326 | jasonlee@etri.re.kr
Minho Cheong | ETRI |  | +82 42 860 5635 | minho@etri.re.kr
Hyoungjin Kwon | ETRI |  | +82 42 860 1698 | kwonjin@etri.re.kr
Jaewoo Park | ETRI |  | +82 42 860 5723 | parkjw@etri.re.kr
Sok-kyu Lee | ETRI |  | +82 42 860 5919 | sk-lee@etri.re.kr
Minyoung Park | Intel | Hillsboro, OR | +1 503 712 4705 | minyoung.park@intel.com
Tom Tetzlaff | Intel |  |  | thomas.a.tetzlaff@intel.com
Emily Qi | Intel |  |  | emily.h.qi@intel.com
Huai-Rong Shao | Samsung |  |  | hr.shao@samsung.com
Chiu Ngo | Samsung |  |  | chiu.ngo@samsung.com
Eric Wong | Broadcom | 190 Mathilda Place, Sunnyvale, CA | +1 408 922 6672 | ewong@broadcom.com
Matthew Fischer | Broadcom |  |  | mfischer@broadcom.com
Yongho Seok | LG Electronics | LG R&D Complex Anyang-Shi, Kyungki-Do, Korea | +82-31-450-1947 | yongho.seok@lge.com
Jinsoo Choi | LG Electronics |  |  | 
Jeongki Kim | LG Electronics |  |  | 
HanGyu Cho | LG Electronics |  |  | 

## Slide 2: Authors:
Jae Seung Lee, ETRI
Name | Affiliations | Address | Phone | Email
Su Khiong Yong | Marvell |  |  | skyong@marvell.com
Hongyuan Zhang | Marvell |  |  | Hongyuan@marvell.com
Sudhir Srinivasa | Marvell |  |  | sudhirs@marvell.com
Simone Merlin | Qualcomm | 5775 Morehouse Dr, San Diego, CA | +1 858 845 1243 | smerlin@qualcomm.com
Santosh Abraham | Qualcomm |  |  | 
Menzo Wentink | Qualcomm |  |  | 
Alfred Asterjadhi | Qualcomm |  |  | 
Amin Jafarian | Qualcomm |  |  | 
Hemanth Sampath | Qualcomm |  |  | 
VK Jones | Qualcomm |  |  | 
Chittabrata Ghosh | Nokia | Berkeley, CA | +1 650 200 7566 | chittabrata.ghosh@nokia.com
Klaus Doppler | Nokia |  |  | 
Sayantan Choudhury | Nokia |  |  | 
Esa Tuomaala | Nokia |  |  | 
Osama Aboul-Magd | Huawei |  |  | Osama.AboulMagd@huawei.com
George Calcev | Huawei | Rolling Meadows,IL |  | George.Calcev@huawei.com
Young Hoon Kwon | Huawei |  |  | Younghoon.kwon@huawei.com
Betty Zhao | Huawei |  |  | Betty.Zhao@huawei.com
David Yangxun | Huawei |  |  | David.Yangxun@huawei.com
Bin Zhen | Huawei |  |  | ZhenBin@huawei.com
Sun, Bo | ZTE |  |  | sun.bo1@zte.com.cn
Lv, Kaiying | ZTE |  |  | lv.kaiying@zte.com.cn

## Slide 3: Authors:
Jae Seung Lee, ETRI
Name | Affiliations | Address | Phone | Email
Ken Mori | Panasonic |  |  | Mori.ken1@jp.panasonic.com
Rojan Chitrakar | Panasonic |  |  | Rojan.Chitrakar@sg.panasonic.com
Haiguang Wang | I2R | 1 Fusionopolis Way, #21-01 Connexis Tower, Singapore 138632 | +65-6408 2000 | hwang@i2r.a-star.edu.sg
Shoukang Zheng | I2R |  |  | skzheng@i2r.a-star.edu.sg
Wai Leong Yeow | I2R |  |  | wlyeow@i2r.a-star.edu.sg
Zander Lei | I2R |  |  | leizd@i2r.a-star.edu.sg
Yuan Zhou | I2R |  |  | yzhou@i2r.a-star.edu.sg
ChaoChun Wang | MediaTek |  |  | chaochun.wang@mediatek.com
James Wang | MediaTek |  |  | james.wang@mediatek.com
Jianhan Liu | MediaTek |  |  | jianhan.liu@mediatek.com
Vish Ponnampalam | MediaTek |  |  | vish.ponnamplam@mediatek.com
James Yee | MediaTek |  |  | james.yee@mediatek.com
Thomas Pare | MediaTek |  |  | thomas.pare@mediatek.com
Kiran Uln | MediaTek |  |  | kiran.uln@mediatek.com
Anna Pantelidou | Renesas Mobile |  |  | 
Juho Pirskanen | Renesas Mobile |  |  | 
Timo Koskela | Renesas Mobile |  |  | 
Liwen Chu | STMicroelectronics |  |  | 
George Vlantis | STMicroelectronics |  |  | 

## Slide 4: Introduction
Short Probe Response frame has been introduced in TGah
This contribution proposes followings:
  Frame Format of the short Probe Response
  Definition of the Probe Response Option bitmap
Jae Seung Lee, ETRI

## Slide 5: Background
Short Probe Response frame format has been defined in 11ah SFD but there is TBD in the subfield definition
It is adopted in 11ah SFD that optional information requested to be included in the short Probe Response is categorized into 8 bitmaps but detailed information included in the bitmap is TBD in current SFD
Jae Seung Lee, ETRI

## Slide 6: Short Probe Response format
Design Approach: Use format similar to existing Short Beacon format
  Make the subfield design identical to current short Beacon format
  Change Sequence and Access Network Options field are added
Use existing SSID IE rather than creating a new field
  It can be included in the Optional IE part of the short Probe Response frame
Capability and Beacon Interval
  They can be included in an Information Elements with other necessary subfields and included in the Optional IE part
Jae Seung Lee, ETRI
Slide 6

## Slide 7: Short Probe Response format
Change Sequence subfield
  Including Change Sequence subfield makes the format of the short Probe Response frame identical to the short beacon frame
  Change Sequence subfield is just an 1 octet – not much overhead to include it in the short Probe Response and it may help probing process
    STA may overhear the short probe responses in the same BSS, although it is an implementation issue
    If it finds the Change Sequence in the short Probe Response has been changed, then it can use the same System Information Update procedure as defined for short beacon
Jae Seung Lee, ETRI
Slide 7

## Slide 8: Short Probe Response format
Beacon Interval subfield
  Short Probe Response is used for immediate association to the AP, and Beacon Interval is required for association
  In baseline spec (802.11-2012), it is specified that
  “The beacon period is included in Beacon and Probe Response frames, and a STA shall adopt that beacon period when joining the BSS, i.e., the STA sets its dot11BeaconPeriod variable to that beacon period”
  Beacon Interval can be included in an Information Elements with other necessary subfields and included in the Optional IE part
Jae Seung Lee, ETRI
Slide 8

## Slide 9: Short Probe Response format
Timestamp
  Only 4 LSB of the TSF timer value of the AP is included in the Timestamp subfield in the short Probe Response
  Full timestamp is required for the STA if the STA wants to use the short Probe Response frame for immediate association
    It is necessary to include 4 MSBs of the TSF at the AP in the short probe response to make the STA associate immediately with the AP
    We can add the field for full timestamp (we call it ‘TSF Completion field’) in an Information Elements with other necessary subfields and included in the Optional IE part
    The IE can be used by both Short Probe Response frame and short beacon frame
Jae Seung Lee, ETRI
Slide 9

## Slide 10: Short Probe Response format
Short Beacon Compatibility Element
  Short Beacon Compatibility Element contains Capability, Beacon Interval, and TSF Completion subfield
  These information is necessary for short probe response to associate with the AP immediately
  We can include the Short Beacon Compatibility element in the Optional IE part of the short Probe Response frame
  No need to define new subfields for these information
  Short Beacon Compatibility Element can be used for both Short Beacon frame and Short Probe Response frame
Jae Seung Lee, ETRI
Slide 10
Element ID | Length | Capability | Beacon Interval | TSF Completion
Octets: 1 1 2 2 4

## Slide 11: Short Probe Response format
Short Probe Response frame format:
  Either Compressed SSID or Full SSID is included.
  When a full SSID is included, existing ‘SSID IE’ is included in the Optional IE part.
    SSID IE is present only if full SSID is requested.
  Change Sequence field and optional Access Network Options field are included
  Short Beacon Compatibility Element may be included in the optional IE part.
  Other optional IE can be included in the optional IE part
Note: Fields in white color already included in the current 11ah spec framework
Jae Seung Lee, ETRI
Slide 11
FC | DA | SA | Time stamp | Change Sequence | Next TBTT (option) | Compressed SSID | Access Network Options (option) | Optional IEs | FCS
2 6 6 4 1 3 4 1 var 4
(octets)

## Slide 12: Short Probe Response format
Frame Control Field format:
Comparison: Short Beacon format in 11ah spec Framework
  Short Probe Response and Short Beacon have almost identical frame format
Jae Seung Lee, ETRI
Slide 12
Protocol Version | Type | Subtype | Next TBTT present | Full SSID Present (0: compressed SSID, 1: Full SSID ) | Interworking Present | BSS BW | Security | Reserved
Bits: 2 2 4 1 1 1 3 1 1

## Slide 13: Probe Response Option bitmap
Recap: Probe Response Option IE format in current Draft
  Information to be included in the short Probe Response is categorized into 8 bitmaps
  Only bitmaps with at least one 1 are included in the Probe Response Option IE
  Define bitmap 0 as a default bitmap that contains frequently used options
    If only bitmap 0 is chosen to be included in the Probe Response Option IE, Probe Response Group bitmap may be omitted
Jae Seung Lee, ETRI
Slide 13
Element ID | Length | Probe Response Group bitmap | Probe Response Option bitmap 0 | ……. | Probe Response Option bitmap n
Octets: 1 1 1 1 1

## Slide 14: Design Approach (1/2)
Include most frequently used options in bitmap 0
  If only options in bitmap 0 are requested, then Probe Response Group bitmap can be omitted – size of the Probe Response Option IE can be reduced
Include options that are likely to be used together in the same bitmap
  Setting any bit in the option bitmap makes the bitmap (1 octet) included in the Probe Response Option IE
  If the options that are used together are grouped into different bitmaps, then multiple bitmaps are included in the Probe Response Option IE and increase the size of the IE
  Make the options defined in the same amendment grouped into the same bitmap as possible
    The STA that implemented the amendment may request several options defined in the amendment
    The STA that has not implemented the amendment will never request the options in the amendment (For example, Sensor node will not use 11u features)
Jae Seung Lee, ETRI
Slide 14

## Slide 15: Design Approach (2/2)
Do not include options that will not be used by the 11ah STAs
  Elements related to FH, DSSS, ERP or elements related to 11n, 11ac, 11ad will not be used by 11ah STAs
  It is not likely that Mesh and IBSS will be used in 11ah
Include options that the STA may explicitly request to the AP
  For example, Channel Switch Announcement, Quiet, and Extended Channel Switch Announcement element are not adequate for a STA to explicitly request these elements.
  These elements are included when the AP determines that it will perform channel switch or channel quieting, so they should not be included in the bitmap
Jae Seung Lee, ETRI
Slide 15

## Slide 16: Bitmap Design (1/3)
Bitmap 0
  Options specific to short probe response format itself will be frequently used, so bits to request them are included in bitmap 0 (Request Full SSID, Request Next TBTT, and Request Access Network Options)
  Probe Response Completion IE and Supported rates are required for immediate association, so bits to request them are included in bitmap 0
  11ah Capability element will be frequently used by 11ah STAs, and 11ah may use Extended Capabilities element to indicate some capability of 11ah STAs such as Non-TIM Support, etc, bits to request them are included in bitmap 0
Other options specific to 11ah STA are grouped into the same bitmap (bitmap 1)
  These options will be used together frequently by 11ah STAs
11k related options are grouped into one bitmap (bitmap 3)
11u related options are grouped into one bitmap (bitmap 5)
Jae Seung Lee, ETRI
Slide 16

## Slide 17: Bitmap Design (2/3)
11v options are grouped into one bitmap (bitmap 4)
  Four 11v related options are included
  Request CF Parameter Set (for PCF), Request DSE registered location (for 11y), and Request Mobility Domain (for 11r) are included in bitmap 4 in the remaining fields in bitmap4
Other Options for baseline spec except 11k, 11v, and 11u and that are frequently used are included in bitmap 2
  Request EDCA Parameter Set, Request RSN, Request Extended Supported Rates, etc…
Bitmap 6 and 7 are reserved for future extension
  QMF Policy (11ae) and QLoad Report (11aa) in the REVmc draft may be added in the future
  New elements are being defined in 11ai (currently 5 elements), and they can be added in the future
Jae Seung Lee, ETRI
Slide 17

## Slide 18: Bitmap Design (3/3)
Options that are not included in the bitmap
  FH, DSSS, ERP related elements are not included since they are not used in 11ah
  Mesh and IBSS related elements are not included since they might not be used in 11ah
  HT Capabilities, HT Operation, 20/40 BSS Coexistence, and Overlapping BSS Scan Parameters are not included since they are used only in 11n and not used in 11ah
  Channel Switch Announcement, Quiet, and Extended Channel Switch Announcement element are not included since it is not adequate for a STA to explicitly request theses elements.
    These elements are included when the AP determines that it will perform channel switch or channel quieting
  Other elements defined in 802.11-2012 except above elements in this slide are defined in the bitmap can be optionally requested to be included in the short probe response frame
Jae Seung Lee, ETRI
Slide 18

## Slide 19: Probe Response Option bitmap (1/2)
Probe Response Option bitmap 0 (Default bitmap): contains frequently used options
Request Short Beacon Compatibility IE: request Short Beacon Compatibility IE (Capability, Beacon, Timestamp Completion)
Request S1G Capability: request S1G Capabilities element
Bitmap 1: contains options for additional 11ah related features
Bitmap 2: contains options frequently used in the baseline spec
Jae Seung Lee, ETRI
Slide 19
Request Full SSID | Request Next TBTT | Request Access Network Options | Request Short Beacon Compatibility IE | Request Supported Rates | Request S1G Capability | Request Extended Capabilities | Reserved
Bits: 1 1 1 1 1 1 1 1
Request RPS | Request Segment Count | Request TSF Timer Accuracy | Request Relay Discovery | Request RootAP BSSID | Reserved | Reserved | Reserved
Bits: 1 1 1 1 1 1 1 1
Request Country | Request Power Constraint | Request TPC Report | Request Extended Supported Rates | Request RSN | Request BSS Load | Request EDCA Parameter Set | Request Supported Operating Classes
Bits: 1 1 1 1 1 1 1 1

## Slide 20: Probe Response Option bitmap (2/2)
bitmap 3: contains 11k related options
Bitmap 4: contains options related to 11v and other misc options (Mobility domain, CF Parameter Set, DSE registered location)
Bitmap 5: contains 11u related options
Jae Seung Lee, ETRI
Slide 20
Bits: 1 1 1 1 1 1 1 1
Request Measurement Pilot Transmission | Request Multiple BSSID | Request RM Enabled Capabilities | Request AP Channel Report | Request BSS Average Access Delay | Request Antenna | Request BSS Available Admission Capacity | Request BSS AC Access Delay
Request Mobility Domaind | Request DSE registered location | Request CF Parameter Set | Request QoS Traffic Capability | Request Channel Usage | Request Time Advertisement | Request Time Zone | Reserved
Bits: 1 1 1 1 1 1 1 1
Request Interworking | Request Advertisement Protocol | Request Roaming Consortium | Request Emergency Alert Identifier | Reserved | Reserved | Reserved | Reserved
Bits: 1 1 1 1 1 1 1 1

## Slide 21: Summary
We proposed TBD fields for the Short Probe Response frame format
  We make the subfield design identical to current short Beacon format
  Change Sequence and Access Network Options field are added
  Existing SSID IE is used instead of creating a new field
  Short Beacon Compatibility Element may be included in the optional IE part that includes Capability, Beacon Interval, and TSF Completion subfield
We proposed detailed information included in the Probe Response Option bitmap
Jae Seung Lee, ETRI

## Slide 22: Straw Poll 1
Do you support to add the frame format of Short Probe Response frame as follows to the spec framework document under R.4.4.1.4.B?
  R.4.4.1.4.B: Short Probe Response frame contains Timestamp, Change Sequence, either Compressed SSID or full SSID, optional Duration to Next Full Beacon Next TBTT, optional Access Network Options, other TBD optional fields and optional IEs
    When a full SSID is requested, Full SSID IE is included in the Optional IE part in the short probe response frame
    Short Beacon Compatibility Element may be included in the optional IE part .
    Frame control field of Short Probe Response frame contains Next TBTT Full Beacon present field, Full SSID Present field which indicates whether Full SSID or Compressed SSID is should be included, BSS Bandwidth field, and Security field, and Interworking Present field other TBD Presence of optional fields
<Short Probe Response frame>
<Frame Control Field>
Yes: No: Abstain:
Jae Seung Lee, ETRI
FC | DA | SA | Time stamp | Change Sequence | Next TBTT (option) | Compressed SSID | Access Network Options (option) | Optional IEs | FCS
2 6 6 4 1 3 4 1 var 4
(octets)
Protocol Version | Type | Subtype | Next TBTT present | Full SSID Present (0: compressed SSID, 1: Full SSID ) | Interworking Present | BSS BW | Security | Reserved
Bits: 2 2 4 1 1 1 3 1 1

## Slide 23: Straw Poll 2
Do you support to add the definition of Probe Response Option bitmap as in slide 19 and 20 in the SFD?
Yes:
No:
Abstain:
Jae Seung Lee, ETRI

## Slide 24: Motion 1
Move to include the frame format of Short Probe Response frame as follows to the spec framework document under R.4.4.1.4.B?
  R.4.4.1.4.B: Short Probe Response frame contains Timestamp, Change Sequence, either Compressed SSID or full SSID, optional Duration to Next Full Beacon Next TBTT, optional Access Network Options, other TBD optional fields and optional IEs
    When a full SSID is requested, Full SSID IE is included in the Optional IE part in the short probe response frame
    Short Beacon Compatibility Element may be included in the optional IE part .
    Frame control field of Short Probe Response frame contains Next TBTT Full Beacon present field, Full SSID Present field which indicates whether Full SSID or Compressed SSID is should be included, BSS Bandwidth field, and Security field, and Interworking Present field other TBD Presence of optional fields
<Short Probe Response frame>
<Frame Control Field>
Yes: No: Abstain:
Jae Seung Lee, ETRI
FC | DA | SA | Time stamp | Change Sequence | Next TBTT (option) | Compressed SSID | Access Network Options (option) | Optional IEs | FCS
2 6 6 4 1 3 4 1 var 4
(octets)
Protocol Version | Type | Subtype | Next TBTT present | Full SSID Present (0: compressed SSID, 1: Full SSID ) | Interworking Present | BSS BW | Security | Reserved
Bits: 2 2 4 1 1 1 3 1 1

## Slide 25: Motion 2
Move to include in the SFD the definition of Probe Response Option bitmap as in slide 19 and 20 in the SFD?
Yes:
No:
Abstain:
Jae Seung Lee, ETRI

## Slide 26: References
[1] IEEE 802.11-12/0869r0 Active Scanning for 11ah
[2] IEEE 802.11-13/0308r0 Active Scanning for 11ah Follow Up
[3] IEEE 802.11-11/1137r14 Proposed Specification Framework for TGah
Jae Seung Lee, ETRI