## Slide 1: DSRC Supporting Information
Date: 2013-05-13
Authors:

## Slide 2: Abstract
Additional supporting information is supplied pertinent to DSRC and the 5.9 GHz spectrum discussions.

## Slide 3: DSRC vs. WAVE
DSRC – Dedicated Short Range Communications
  General term with relatively long history. Until what is now the 802.11p usage, the term was most commonly applied to electronic toll collection transponders
WAVE – Wireless Access in Vehicular Environment
  Created to avoid confusion with previous examples of DSRC. “This is not just another toll tag.”
In general the terms are interchangeable, WAVE is used when there may be confusion with earlier examples of DSRC.

## Slide 4: References
Introduction to “Connected Vehicle Test Bed” by Intelligent Transportation Systems Joint Program Office of the US DoT (plus links to related sites)
  http://campaign.r20.constantcontact.com/render?llr=shwsbvdab&v=001ETD-u6eVKYs1BauYC_CeK8zc1HVjvDXQq0sz5Z5Zl7Fy0VL4LivSMqZ_6PENUSQ8tam3TczwN_KCit1PkncJVlRwRDJWS-zUCBSpy02VvApOW3vvjHI94w%3D%3D
“Connected Vehicles and the Impacts of Spectrum Sharing” by the Auto Alliance (follow other links also)
  http://www.autoalliance.org/index.cfm?objectid=D6D03A50-B755-11E2-B62D000C296BA163&goback=.gde_2120902_member_239612580

## Slide 5: Requirements Summary
Vehicle speeds to 200kph
Hundreds of vehicles in communication zone at a time
Response times on the order of 100ms
Operation whenever/wherever vehicles may be
Communications range of up to 1000 m for select uses
Many overlapping zones/applications
Safety of life level of reliability
Initial requirements analysis done about 12 years ago, constantly being updated

## Slide 6: DSRC Architecture
PHY
MAC (including channel coordination)
LLC
WSMP
IPv6
UDP/TCP
1609.11
Management
Security
Higher Layer Standards
1609.2
1609.1
1609.3
1609.4
802.11