## Slide 1: Liaison Report for OmniRAN EC SG
Date: 2013-05-16
Authors:

## Slide 2: Abstract
This presentation contains the May 2013 IEEE 802.11 liaison report for OmniRAN EC SG.

## Slide 3: Key Activities
Currently focused on responding to EC request for:
  Gap analysis of use cases point out relevant areas to be covered by IEEE 802 that are not covered by other SDO’s.
  Articulate scope of OmniRAN based on gap analysis.
  Identify relevant IEEE 802 work items
Approve scope document for OmniRAN
Dropped the WLAN Hotspot roaming use case for gap analysis
Representative use cases for gap analysis include:
  SDN use case
  3GPP trusted WLAN use case
  Smart Grid use case

## Slide 4: Access Network Abstraction by OmniRAN
OmniRAN provides a generic model of an access network based on IEEE 802 technologies
Access Network
Terminal
Core
Service
Medium
Medium
Data Link
Physical
Network
Transport
Application
Data Link
Physical
Data Link
Physical
Data Link
Physical
Network
Transport
Application
Network
Network
Medium
Medium
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
Core
R2
R1
R3
OmniRAN Architecture
Access Network
Terminal

## Slide 5: OmniRAN Reference Points capture the functions of an access network
Reference Points denote the interconnections between functional entities of an access network, i.e.:
  R1 between terminal and base station:
    Access link, technology specific
  R2 between terminal and core network:
    User & terminal authentication, subscription & terminal management
  R3 between access network and core network:
    Authorization, service management, user data connection, mobility support, accounting, location
  R4 between access networks:
    Inter-access network coordination and cooperation, fast inter-technology handover
  R5 between core networks to enable co-use of access networks:
    Inter-operator roaming control interface
Reference Points build the foundation for realizing interoperability for real world access networks.
The Reference Points capture the control information necessary to allow dynamic control of network functions by a central entity (core).

## Slide 6: OmniRAN Scope
OmniRAN provides an abstraction of access networks based on IEEE 802 technologies.
Reference Points reflect IEEE 802 specific control information
  R1 is completely covered by IEEE 802 specifications
  R2 and R3 are mainly carrying control information for IEEE 802 functions
  R4 enhances direct cooperation among multiple IEEE 802 access networks
  R5 is present for conceptual purposes to forster the cooperation among cores.
    Attributes carried on R5 may mostly be identical to the attributes defined for R3
OmniRAN Specification in the scope of IEEE 802 would consist of
  a normative part defining control attributes and referencing the DL SAP
  an informative part outlining the overall architecture
  an informative part proposing the usage of particular IP protocols and the mapping of the IEEE 802 attributes into the IP protocols.

## Slide 7: Objectives for July
Teleconferences: June 20 at 09:00 ET– details on OmniRAN SG website
Complete use case and gap analysis
Identify potential standardization topics for IEEE 802

## Slide 8: References
OmniRAN website
  http://www.ieee802.org/OmniRANsg/
Document repository for OmniRAN:
  https://mentor.ieee.org/omniran/documents
Link to May 2013 OmniRAN Agenda:
  https://mentor.ieee.org/omniran/dcn/13/omniran-13-0030-03-ecsg-may-2013-waikoloa-agenda.pptx
Scope Document
  https://mentor.ieee.org/omniran/dcn/13/omniran-13-0032-05-0000-ieee-802-scope-of-omniran.pptx