## Slide 1: A perspective on what any High Efficiency Wireless TG should and should not do
1 May 2013
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco | +1 408 5253346 | brianh@cisco.com
Andrew Myles | Cisco | +61 418 656587 | amyles@cisco.com
Reza Hedayat | Cisco | +1 469 2552656 | rehedaya@cisco.com

## Slide 2: HEW should focus on speed & efficiency; with WFA & vendors focusing on issues not needing new standards
Situation
Bad news
Good news
Next
steps
Wi-Fi has grown from almost nothing in 2000 to over 1.5 billion devices per annum in 2012
… with Wi-Fi used in an increasingly diverse range of product categories
Wi-Fi is a victim of its own success, with poor performance in some environments
…with performance not helped by Wi-Fi sometimes operating in a very harsh radio environment
It has been demonstrated Wi-Fi can operate in dense, BYO Client, multi-vendor environments
Improve Wi-Fi in dense, BYOD, multi-vendor environments
… with Wi-Fi Alliance & vendors taking responsibility for Wi-Fi where new standards are not needed
…and HEW focused on speed features, attaching efficiency features as mandatory add-ons

## Slide 3: Wi-Fi has grown from almost nothing in 2000 to over 1.5 billion devices per annum in 2012 …
Chart: Wi-Fi chipsets sold per annum (millions)
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012
Chips | 5.3864 | 7.4811 | 23.064 | 43.1876 | 81.5233 | 158.7633 | 203.5783 | 307.2064 | 459.6031 | 591.295 | 906.2209 | 1138.2786 | 1500

## Slide 4: ... with Wi-Fi used in an increasingly diverse range of categories
Chart: Wi-Fi Alliance product certifications per annum (by category)
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012
PCs & Computing | 37 | 89 | 237 | 298 | 482 | 398 | 272 | 318 | 320 | 330 | 441 | 610 | 450
Networking Equipment | 30 | 55 | 137 | 145 | 256 | 245 | 256 | 354 | 358 | 446 | 538 | 741 | 943
Consumer Electronics | 6 | 9 | 10 | 35 | 60 | 158 | 485 | 680 | 1007
Mobile Handsets | 1 | 7 | 18 | 59 | 58 | 106 | 226 | 477 | 724 | 946
Other | 1 | 1 | 1 | 2 | 20 | 20 | 48 | 49 | 135 | 162

## Slide 5: The bad news: Wi-Fi is a victim of its own success, with poor performance in some environments …
CSMA/CA style protocols in high density environments can “waste” lots of airtime resolving contention
BYOD means a diversity of devices must be managed, often based on capabilities of least capable devices
Legacy devices waste airtime because of protection mechanisms; low legacy rates just waste airtime
High density environments often have networks under multiple administrations making management hard (especially soft APs/WFD)
Many devices contain poorly implemented mechanisms for high density:
Sticky roaming
Inefficient rate shifting
Too much use of low rates
Poor use of RTS/CTS
Inappropriate TX powers
Too many Probe Req/Resp
…
Contention
BYOD
Legacy
Authority
Implementations
Poor Network
Performance

## Slide 6: … with performance not helped by Wi-Fi sometimes operating in a very harsh radio environment
  Wi-Fi operated in what is commonly known as unlicensed spectrum, which generally means Wi-Fi systems must:
    Avoid interfering with others
    Accept interference from others
  Wi-Fi systems must particularly avoid interfering with
    Satellites in some of 5GHz bands
    Radar in most of the 5GHz bands
  Wi-Fi systems must particularly deal with interference from
    Microwave ovens in 2.4GHz
    Other systems, eg Bluetooth, Zigbee, Wi-Fi and others
  It is never possible to “guarantee” anything in this harsh radio environment, despite desires by many for a “guarantee”

## Slide 7: The good news it has been demonstrated Wi-Fi can operate in dense, BYO Client, multi-vendor environments
  Cisco has a dedicated BU that focuses on the use of Wi-Fi in stadiums, mainly for streaming multiple camera angles & general browsing
  Another BU focuses on the needs of Service Providers
  Collectively Cisco has successfully serviced the needs of many high profile sports events and industry conferences
    E.g., London Olympics, multiple Super Bowls, large vendor events (Cisco Live!, others), large industry events (Mobile World Congress), etc
  The analysis of TBs of data related to the high density events had resulted in just a few key lessons:
    Successful Wi-Fi operation is possible in dense, BYO Clients, multi-vendor environments
    Measurement & management is vital, including features like those standardized by 802.11k/v
    Many problems relate to poor implementations, not inadequate standards; the fixes to these problems are often dependent on business constraints

## Slide 8: Next steps: improve Wi-Fi in dense, BYOD, multi-vendor environments both within & outside HEW
HEW should …
HEW should NOT…
HEW should …
Encourage WFA & Wi-Fi vendors to be responsible for aspects of Wi-Fi where no new standards are needed
Let WFA & vendors focus on the many opportunities to
  Leverage existing standards
  Fix poor implementations not designed with high density in mind
Attempt to provide “guaranteed, deterministic” access
Invent new protocols without understanding why old protocols have yet to succeed
Recognise “speed” is probably needed as focus to help make HEW a success
  Port 8SS, DL-MU-MIMO & 256QAM to 2.4GHz
  Full duplex (A ⇆ B simultaneously)
Consider attaching “efficiency” features as un-signalled features (hence mandatory)

## Slide 9: The Wi-Fi Alliance & vendors can take responsibility for Wi-Fi where need new standards are not needed
  The lessons from existing Cisco experiences deploying Wi-Fi in dense, BYO Clients, multi-vendor environments suggest some obvious activities
    Leverage existing standards
    Fix poor implementations not designed with high density in mind
  Neither activity has much to do with potential standardization work in IEEE 802.11 HEW SG
  These activities are better dealt with by:
    Equipment vendors:
      Certifying existing standards through the Wi-Fi Alliance
      Actively attempting to refine poor implementations (particularly relevant to reference design vendors)
    Wi-Fi Alliance
      Providing a forum to identify implementation & deployment issues
      Developing “best practices” guidelines for implementation and deployments
      Defining improved certification testing

## Slide 10: There are many examples of Wi-Fi issues that could appropriately be dealt with by WFA & vendors
Identified issue | Possible fix | Responsibility
Use of 1 & 2Mb/s wastes substantial airtime | Discourage use of 802.11b rates out of the box | WFA best practice Vendors
802.11b-only devices waste airtime because they need protection mechanisms | Discourage certification of 802.11b-only devices | WFA best practice Vendors
Soft APs (and Wi-Fi Direct devices) are often unmanaged, congregate in crowds, yet aren’t designed for high density, causing interference to managed infrastructure APs | Discourage regulators from loosening DFS rules to allow 5GHz operation for soft APs without radar detection Best practice document for soft APs (limit power; delete low MCSs from operational set, adjust how often management frames are sent) | WFA Spectrum TG 802.18 WG 802.11 Regulatory SC Vendors WFA best practice

## Slide 11: There are many examples of Wi-Fi issues that could appropriately be dealt with by WFA & vendors
Identified issue | Possible fix | Responsibility
Poor roaming algorithms resulting in “sticky AP” problem or flapping AP problem | Best practice document for roaming behaviour Certification and deployment of 11v BSS Transition mechanism | WFA best practice WFA certification Vendors
Suboptimal rate adaptation | Consider certification & deployment of MCS Feedback Disable 11b rates & 6-12 Mbps as operational/supported | WFA best practice WFA certification Vendors
Inefficiency caused by insufficient use of aggregation | Encourage more use of A-MPDU Encourage use of A-MPDU of A-MSDU | WFA best practice WFA certification Vendors
Inefficiency caused by insufficient use of “spatial aggregation” | Encourage use of DL-MU-MIMO Note: likely to be part of second WFA certification of “ac” | WFA certification Vendors

## Slide 12: There are many examples of Wi-Fi issues that could appropriately be dealt with by WFA & vendors
Identified issue | Possible fix | Responsibility
Airtime filled with too many Beacons, Probe Req/Resp, particularly at low data rates Note: soft APs are worst offenders | Best practices for management frame use & rate policies Limit Primary to Ch 1, 6, 11 Note: possible overlap with 11ai | WFA best practice Vendors IEEE?
Poor quality implementations (e.g. client going to PS mode & and doze state without confirmation from AP => excess retries; overlength TXOPs) | Define best practice for protocol conformance / issues list Consider certifying protocol conformance | WFA best practice / issues list WFA certification Vendors
Excess collisions caused by a lack of spectrum/power management, wasting airtime | Consider certification of appropriate “hooks” in 11v (eg Channel Usage) & 11k/ac (Power Constraint, VHT Transmit Power Envelope) | WFA certification Vendors

## Slide 13: There are many examples of Wi-Fi issues that could appropriately be dealt with by WFA & vendors
Identified issue | Possible fix | Responsibility
Vendors have not deployed useful features from 11e, 11k, 11v and 11r in WMM-AC, Voice-Enterprise certifications | Encourage all vendors to “do the right thing” by the industry and their customers!  | WFA Vendors
Many vendors have not supported certification of useful features from 11k, 11v, 11ae in NPS, WNM, etc | Encourage all vendors to “do the right thing” by the industry and their customers!  | WFA certification Vendors

## Slide 14: HEW should not attempt to provide “guaranteed, deterministic” access
  There are some who want Wi-Fi to provide “guaranteed and deterministic” access
  Unfortunately, this requires secure and trusted access across time, space, frequency and administrative domain for both new and legacy devices
  This is hard enough, but it also requires knowledge of and control over interferers in unlicensed spectrum, which is almost impossible!
  Academia and the “standards world” have been studying and attempting to solve this problem for decades … and failing!
  It is time to recognize that Wi-Fi does not need and is not likely to ever achieve “guaranteed and deterministic” access
  Rather, Wi-Fi just needs to continue doing what it has always done – provide “good enough” in a nasty, uncontrolled, unlicensed environment;
  “Good enough” may even be “mostly predictable” in some environments

## Slide 15: HEW should not invent new protocols without understanding why old protocols failed
  There are many examples where:
    A feature has been standardized in 802.11
    The feature has not been certified and/or adopted
    The features have been subsequently extended
    The feature has not ben certified and/or adopted … and REPEAT
  The classic example is polled access
    First PCF …
    Then HCCA in 802.11e
    Then managed OBSS overlap in 802.11aa
  The answer to a mal-adopted protocol is NOT to invent a new protocol.
  Rather first one needs to understand the business/HW/SW/wireless constraints that prevented adoption/certifications … and then understand what, if anything, has changed

## Slide 16: “Speed” is probably needed as focus to help make HEW a success
  Success for new 802.11 amendments in the past has always required users to be excited …so that semi-conductor vendors can justify developing a new generation of chips
  Unfortunately the primary feature that appears to excite users is “speed” … the biggest possible “number on the box”
    11g/n were successes, with 11ac/ad waiting to be successes
    11e/h/j/k/r/s/v/w/z/aa/(ae) are yet to achieve strong success in the market
    11i was a different – security is a threshold requirement
    11u is different too – and not yet a success!
  This suggests that HEW probably needs an element of speed in its feature set to help drive success
  Maybe efficiency focused features can be “sold” as speed, or maybe we can attach them to the speed features by making them non negotiable? ie un-signalled

## Slide 17: HEW should consider efficiency features attached to features focused on speed
Speed features
  Port 11ac features like 8SS, 256 QAM and DL-MU-MIMO to 2.4GHz
  Full duplex Wi-Fi between peers
    Needs vetting by semi-vendors – is this ready for prime-time?
Efficiency features
  Support for elements of 11k/v/ae; & other efficiency extensions
  Interference nulling (better reuse between overlapping BSSs)
    Need for an amendment is less clear; most schemes need antennas ∝ number of clients to null, so helps in some cases but not others
  OFDMA
    But, most valuable in transition with mixed BW capabilities
  UL-MU-MIMO