## Slide 1: FILS Piggy-Backing Aspects
Date: 2013-05-15
Authors:
Name | Company | Address | Phone | email
René Struik | Struik Security Consultancy | Toronto ON, Canada | USA: +1 (415) 690-7363 Toronto: +1 (647) 867-5658 Skype: rstruik | rstruik.ext@gmail.com
Note: Material extracted from 13/201r8

## Slide 2: FILS Key Establishment
STA
AP
Association Request
Beacon/Probe Resp.
Authentication Request
Authentication Response
Association Request
Key
Establishment
Key
Confirmation
TTP
online/offline assistance
with authentication
FILS key establishment protocol options provided:
FILS Authentication with TTP, based on ERP
(two flavors: with or without “PFS” (ERP+ECDH, resp. ERP)  see next slides)
Authentication without online TTP, based on ECDH and ECDSA certificate
Slide source: 13/324r0

## Slide 3: Adding “piggy-backed info” to protocol flows …
STA
AP
Association Request
Beacon/Probe Resp.
Authentication Request
Authentication Response
Association Request
Key
Establishment
Key
Confirmation
TTP
Services
+ piggy-backed info response
+ piggy-backed info request
Authentication help
Configuration help
IP address assignment
Authorization
Subscription
credentials
Piggy-backing info along FILS authentication protocol:
Higher-layer set-up, including IP address assignment
Authorization functionality, subscription credentials, etc.
See details elsewhere in presentation
Slide source: 13/324r0

## Slide 4: FILS Security Status
Current Status:
Three FILS authentication protocol options specified:
  FILS Authentication with Trusted Third Party
  FILS Authentication with Trusted Third Party and “PFS”
  FILS Authentication without Trusted Third Party
Main differences:
  Different trust assumptions
  Different assumption on “pre-existing” system set-up
  Different assumptions on online availability of the “backbone network”
Common elements:
  All have only four protocol flows
  All implemented via Authentication/Association Request/Response frames
  All allow piggy-backing of other info along Association frames
  (e.g., IP address assignment)
Current Work in Progress:
How to deal with large objects (e.g., certificates, higher-layer data objects)
How to specify main piggy-backing details (e.g., on IP address assignment)
Slide source: 13/324r0

## Slide 5
Questions
1. How to deal with large objects (e.g., certificates, higher-layer data objects)?
Intra-frame fragmentation. DISCUSSED ELSEWHERE
How to handle large objects that fit within a single frame
Inter-frame fragmentation. DISCUSSED ELSEWHERE
How to fragment FILS frames, if these become too long due to large objects
2. How to specify main piggy-backing details (e.g., on IP address assignment)?
Flexibility re AEAD authenticated encryption mode. DISCUSSED HERE
Authentication and potential encryption of piggy-backed information

## Slide 6
Authenticated Encryption (1)
General mechanism
After AEAD protection
Now with Information elements:
or...
or...
Main problem: How to pinpoint the portions that are encrypted? (only problem for recipient)
Header
Payload
Header
Secured Payload
Authentication of entire frame
0
7
1
3
4
6
5
8
9
A
0
7
1
3
4
6
5
8
9
A
0
7
1
3
4
6
5
8
9
A
Encrypted segments starts here

## Slide 7
Authenticated Encryption (2)
How to pinpoint the portions that are encrypted? (only problem for recipient)
Recipient can easily find this “L”-symbol: simply parse received message (and remove this “L”-symbol)
Does this also work for other “encryption ON/OFF” combinations?
0
7
1
3
4
6
5
8
9
A
0
7
1
3
4
6
5
8
9
A
L
0
7
1
3
4
6
5
8
9
A
“L”
1
1
2
2
L
“L”
2

Encryption length indicator IE
(4 octets)

## Slide 8
Authenticated Encryption (3)
Does this also work for other “encryption ON/OFF” combinations?
YES! Exploit structure in IEs: encryption/decryption is essentially on “unordered” set of IEs.
Step 1 @sender: massage in right form (split frame into “to be encrypted elements” and “other data”)
Step 2 @sender: encrypt and put “L”-symbol (encryption indicator IE) in place
0
7
1
3
4
6
5
8
9
A
0
7
1
3
4
6
5
8
9
A
0
1
3
6
8
9
7
4
5
A
Other
data
To be encrypted data
1
A
3
4
0
7
5
6
8
9
“L”

## Slide 9
Authenticated Encryption (4)
Step 1 @recipient: find encryption indicator, length of encrypted segment, decrypt and verify authenticity, and remove “L”-symbol
(NOTE: encryption indicator is always “on the left”)
Step 2 @recipient: massage “decrypted data” and “other data”, so that IEs will be in ascending order.
0
1
3
6
8
9
7
4
5
A
Other
data
Decrypted data
1
0
3
4
5
A
7
6
8
9
“L”
0
7
1
3
4
6
5
8
9
A
1
A
3
4
0
7
5
6
8
9
“L”

## Slide 10
Authenticated Encryption (5)
What about complexity?
Step 1 @sender: massage in right form (split frame into “to be encrypted elements” and “other data”)
Scan data from left to right and partition string according to “Encryption ON/OFF” indication
Step 2 @recipient: massage “decrypted data” and “other data”, so that IEs will be in ascending order.
Scan leftmost elements of two substrings and build combined string according to order IE Identifiers.
Step 2 @sender: encrypt and authenticate and put “L”-symbol (encryption length indicator IE) in place
Step 1 @recipient: find encryption indicator, length of encrypted segment, decrypt and verify authenticity, and remove “L”-symbol
0
7
1
3
4
6
5
8
9
A
0
1
3
6
8
9
7
4
5
A
Other
data
To be encrypted data
1
0
3
4
5
A
7
6
8
9
“L”
1
0
3
4
5
A
7
6
8
9
“L”

## Slide 11
Authenticated Encryption (6)
Summary:
Flexible authenticated encryption scheme:
Sender has full control over which portions to encrypt
(e.g., encryption of vendor-specific info, specific higher-layer objects)
Recipient can always decrypt-and-verify, irrespective of sender’s security policy
Limited incremental cost:
Requires new 4-octet information element (“encryption indicator element”)
This allows recipient to always easily find “encrypted data” and “other data”
Requires single left-to-right scan of string on sender’s and recipient’s side
Implementation cost scan operation insignificant:
*Scan on recipient’s side only after decrypt-and-verify, so no schedule impact
*Scan on sender’s side may be trivial and can be anticipated by sender
Notes:
AEAD scheme described has minimal complexity, in the following sense:
Any AEAD scheme where one cannot statically determine size and/or location of “encrypted data” from frame itself requires introduction of “encryption indicator IE”
Any scheme where one wishes to have “encrypted data” together, so that AEAD crypto inputs can be easily determined, requires some type of “scan” operation

## Slide 12
Authenticated Encryption (7)
Summary:
Flexible authenticated encryption scheme:
Sender has full control over which portions to encrypt
(e.g., encryption of vendor-specific info, specific higher-layer objects)
Recipient can always decrypt-and-verify, irrespective of sender’s security policy
Implementation choices:
Any implementer who does not care about flexibility (i.e., its security policy is to always encrypts the entire frame), does not need to implement “scan” on sender’s
side. In that case, encrypt-and-authenticate coincides with usual CCM mode.
Any implementer whose incoming frame processing considers IEs as a set, i.e., unordered, does not need to implement “scan” on recipient’s side. In that case, decrypt-and-verify coincides with usual CCM mode.
Result: (“Best of both worlds”)
Implementers who do not like flexibility/generality can go their way
Implementation of “encryption indicator element” allows others who do like flexibility to go their way as well (“peaceful coexistence”)

## Slide 13
Authenticated Encryption (8)
Options:
1. No flexibility. Always encrypt FILS Association Request/Response “body”
2. Some flexibility. Allow only encryption of “first chunk”…
No re-ordering of IEs at all.
3. Full flexibility. Allow encryption of any chunks, as set by senders policy…
Potential re-ordering of IEs “under the hood”. Put “right” as part of AEAD routine.
Details in 13/582r0.
Header
Secured Payload
Header
Secured Payload
Visible Chunk
“L”
Header
Secured Payload
Visible Chunk
“L”

## Slide 14
Authenticated Encryption – Straw Poll
  Implement flexible encryption scheme as specified in 13/582r0:
  Introduce new Information Element (IE) as “security indicator element” (4-octets), so as to indicate length of encryption segment following
  Facilitate Option #2 of previous Slide (#22).
  For clarity: This only applies to FILS Association frames
Yes
No
“Don’t Care”
Need more information
Result:

## Slide 15
Authenticated Encryption – Motion
Instruct the editor to incorporate changes to D0.5, as indicated in 13/582r0
Yes
No
Abstain
Result: Y/N/A