## Slide 1: Comparison of IE fragmentation proposals
Date: 2013-05-15
Authors:
Name | Affiliations | Address | Phone | email
Hiroki Nakano | Trans New Technology, Inc. | Kyoto, JP | +81-75-213-1200 | cas@gmail4.trans-nt.com

## Slide 2: Abstract
This presentation compares proposals of the following proposals to fragment IEs:
    311r2
    478r2

## Slide 3: Comparison
Normative text | 311r2 | 478r2
Supplementary slides | 201r10 | 487r0
Basic method | Split data into Multiple Fragment IEs | 
Splitting rule | Multiple 255 byte-long IEs + a small IE for the residue | 
IDs of types of data | New series | Same as existing IEs
IE ordering | No change (ascending order) | Add a new exception (See the next slide)
Top IE of a series | Fragment IE | According to data
Last IE of a series | Fragment IE having less than 255 byte-long data | Fragment IE before another IE than Fragment IE
Size of encoded data (n mod 255 != 0) | n + 2 * int(n / 255) + 3 | n + 2 * int(n / 255) + 2
(n mod 255 == 0) | n + 2 * int(n / 255) + 3 | n + 2 * int(n / 255)

## Slide 4: Draft P802.11REVmc_D1.4 Page 619 Line 53
The frame body components specified for many management subtypes result in elements ordered by ascending Element ID, with the exception of the MIC Management element (8.4.2.54 (Management MIC element)). If present, the MIC Management element appears at the end of the robust management frame body. See 9.25.6 (Element parsing) on the parsing of elements.

## Slide 5: Strawpoll
Which proposal do you like?
311r2
478r2
Don’t care

## Slide 6: References
11-13-0201-10-00ai-fils-handling-of-large-objects.pptx
11-13-0311-02-00ai-proposed-resolutions-for-assigned-security-cids.docx
11-13-0478-02-00ai-fragmenting-large-ies.docx
11-13-0487-00-00ai-how-to-fragment-an-ie.ppt