## Slide 1: Introduction of EUHT
Date: 2013-05-15
Authors:

## Slide 2: Abstract
Briefly introduce EUHT( Enhanced Ultra-high Throughput)

## Slide 3: Outline
Background
Technical Overview
Status Update
Co-existence with other systems

## Slide 4: Background
Started the development in 2009
Aim to meet the requirements like
  High efficiency
  Dense deployment of users
  QoS
  Independent IPR
Funded by National Science and Technology Major Projects
  2010/2012/2014
Cooperated with industrial/academic partners
通信计
量中心

## Slide 5: Technical Overview
Parameters
Features
Frame Structure
EUHT Transmitter

## Slide 6: Parameters
Sub-carrier Interval | 78.125KHz
FFT Window | 12.8us
Cyclic Prefix | 1.6us
Data Sub-carrier | 224 With 20MHz
Spectrum Aggregation | Mode I/II, up to 80MHz BW
MIMO | Up to 8 Streams
Max. MCS | 256QAM，7/8 code rate

## Slide 7: Features
Scheduling Based
Supports Multi-User MIMO
Spectrum Aggregation

## Slide 8: Scheduling
CAP ( Central Access Point )
  Grant the users to access
  Allocate resources to users
Scheduler
DL Packets Queues
Channel Est.
Scheduler
Channel Est.
S.R.
UL Packets Queues
CAP
STA
Based on QoS Scheduling
Based on QoS Scheduling

## Slide 9: Multi-User MIMO
Support both implicit and explicit CSI feedback
CSI feedback delay can be controlled by UL scheduling
Group the CSI to reduce the feedback overhead

## Slide 10: Spectrum Aggregation
Support both non-continuous and continuous aggregation

## Slide 11: Frame Structure
S-Preamble | frame detection, coarse sync., AGC | UL-SRCH | UL schedule request channel
L-Preamble | accuracy sync., channel est. | UL-RACH | UL random access channel
SICH | broadcast frame structure | DL-TCH | DL transmission channel
CCH | allocate DL/UL-TCH resources | UL-TCH | UL transmission channel
DL-SCH | DL channel sounding | DGI | transition interval from DL to UL
UL-SCH | UL channel sounding | UGI | transition interval from UL to DL

## Slide 12: EUHT Transmitter

## Slide 13: Status Update
Standardization
  Announced as Chinese industrial standard in Feb, 2012
    Draft is free to download from MIIT website
  Will become Chinese national standard for middle-short range wireless communication system this year
Industrial Applications
  Fixed Wireless Backhaul
  City Video Surveillance System
  Subway Communication System
  …

## Slide 14: Co-Existence with Other Systems
The primary working band will be 5GHz
  5150~5350 MHz
    Open for systems with tx power < 200mW, indoor applications only
  5470 ~ 5725 MHz
    Reserved for systems with independent IPR
  5725 ~ 5850 MHz
    Apply before use
It is possible that EHUT and other systems work at the same band
  Co-existence may need to be considered in advance

## Slide 15: Thank you!