## Slide 1
Adding performance parameters to WNM for better network management
Date: 2013-07
Authors:
Name | Affiliations | Address | Phone | email
Chen Yanming | China Mobile | 16A,Danling Street, Haidian District, Beijing, China, 100080 | +86 10 52696688-3045 | chenyanming@cmdi.chinamobile.com
Slide 1
        doc.: IEEE 802.11-13/0692
JUL 2013

## Slide 2: Topics
Background
Proposal
Straw Poll
Slide 2

## Slide 3: Background(1)
WLAN can bypass the traditional communication traffic and supply the immature next generation communication systems, such as LTE, etc.
Operators have already deployed carrier-grade WLAN networks, coming along with huge number of customers.
Using China mobile for example,
  Deployed more than 300 million access point
  There are more than 30 equipment vendors
Slide 3

## Slide 4: Background(2)
Because of the higher requirement of users, operators must pay more attention to their network quality .
Still taking the quality request of China Mobile for example, we ask:
  The successful rate of terminals connecting to Aps should over 90%.
  We allowed some APs does not work, but the “not work” rate should below 3% in normal hotspot and below 1% in VIP hotspot
We need better network management, especially the performance management.
There are some useable MIB nodes in 802.11k and 802.11v can help us to do the management, but they are not enough.
Slide 4

## Slide 5: Proposal(1)
Adding some nodes into 802.11 WNM MIB, which can satisfy the requirement of both 802.11 and operators.
For example：
  Suggest to add the node “AssocFailTimes ” into MIB, which means “Statistics the connection failure times when an AP start working”.
  802.11benefit : the parameter above can guide a terminal connecting to an AP which has less connection failure times.
  Operator benefit : Get the value of “AssocFailTimes” to calculate the successful rate of terminal connecting to AP, which can be used to analyze the network problem and help us to resolve it.
  The both sides can benefit from it.
Slide 8

## Slide 6: Proposal(2)
We suggest to add the following nodes:
              Index
Get these information through SNMP protocol or by file transfer mode.
Slide 9
Node name | Explanation | Level | Classification
AssocTimes | Statistics terminal-connection times when an AP start working | A | performance
AssocFailTimes | Statistics the connection failure times when an AP start working | A | performance
ReassocTimes | The times of terminals re-connecting to an AP | A | performance
PreAssCannotShiftDeassocFailSum | The failure times of terminals re-connecting to an AP | A | performance
UplinkDataOctets | The number of data package received by an AP | A | performance
DwlinkDataOctets | The number of data package sent by an AP | A | performance
ApStationOnlineSum | The current user number of an AP | A | performance

## Slide 7: Straw Poll
Is it meaningful and necessary of this proposal?
  Yes
  No
  Abstain
Slide 10

## Slide 8
Thank you！
Slide 11