## Slide 1: Evaluation Methodology and Simulation Scenarios
Date: 2013-07-15
Authors:

## Slide 2: Outline
In [1] we presented a diverse set of topics such as
  Metrics of interest
  System simulation examples from 11ac
  Target gains
  Simulation scenarios
In this contribution we focus on providing initial thoughts towards defining a simulation methodology and simulation scenarios documents.

## Slide 3: Simulation Methodology
As discussed previously, the focus of HEW is on improved aggregate area throughput in scenarios with large number of STA and in dense (indoor and outdoor) environments.
PHY PER simulations should continue to be used to verify point to point performance or aspects that need this type of simulation, especially new PHY features.
However, as discussed in [1], of increased importance in HEW is performing system simulations to assess performance of multi-STA and multi-BSS using metrics such as aggregate throughput (across all BSS) and 5% (cell edge) throughput.
Here we provide a general structure for such simulation. Specific details will depend on the specific scenario and specific MAC/PHY features to be investigated.
As discussed in [1], PHY/MAC system simulations may be used separately in order to:
  Simplify (using abstraction) some of the MAC/PHY details respectively
  Speed up development (by reducing dependency of PHY on MAC and vice versa)
  Improve insight as to the specific reason for performance gains/losses (a more difficult thing to assess in multi-STA multi-BSS environments that include all possible PHY and MAC details).
  Some proposed techniques may not require all PHY/MAC details in order to evaluate gains

## Slide 4: System Simulation - General Description
A system simulation is comprised of multiple drops and multiple TXOP.
  A drop is defined by a known AP and STA locations. Simulating multiple drops is important in order to randomize STA location to better assess issues such as OBSS interference and intra-BSS throughput (as these issues are highly dependent on the relative path loss between AP and STA).
  In a TXOP a set of transmissions occur. Multiple TXOP (with typical aggregate duration >1sec) are required to assess performance of a given set of APs and STAs configuration. A’warm-up’ period may be used for some parameters to converge.
MAC parameters that need to be defined (a simplified version may be used for a PHY system simulation):
  Beacon periodicity
  Aggregation policy
  Usage of RTS-CTS or CTS2SELF
  EDCA parameters (AC, CWmin, CWmax, AIFSN)
  CSMA backoff procedures, energy and preamble detection
  Basic rate set
  If other MAC schemes are proposed they need to be defined (e.g. RAW as in 11ah)
PHY parameters that need to be defined per AP and per STA (a simplified version may be used for a MAC system simulation):
  Transmission BW (could be different in different BSS)
  Number of antennas (could be different for different STA)
  Transmission scheme- SU OL, SU BF, MU
  Channel model (multipath fading, Doppler, path loss, shadowing etc..)
  PHY abstraction method (combining PER sims with system sims is prohibitive) – see Appendix for more details

## Slide 5: Cont.
Link adaptation needs to be defined –
  MCS choice (genie could be used to assess upper performance bound but not realistic performance).
  Transmission mode selection SU OL vs. BF vs. MU should be described (transmission mode can be fixed or dynamic).
Traffic model should be defined (full buffer vs. Poisson arrival) for all links
Other system parameters such as frequency reuse should be specified as needed.
General simulation structure:
For drop=1:N {
  APs and STA are dropped (randomly or in fixed locations) in a given area following certain placement rules (specifics depend on the scenario).
    If simulation time is an issue, multiple drops’ locations can be agreed beforehand in order to minimize the number of drops and enable multiple companies’ results comparison.
  STAs are associated with APs (typically based on path loss but could use other rules if some AP are not be available (e.g. belonging to a different apartment or operator) in some scenarios.
  For TXOP=1:M {
    Perform transmissions consistent with all the parameters defined previously and collect metrics
  }
}

## Slide 6: Simulation Scenarios
Ref. [2] compiles the proposed use cases.
After reviewing [2] we think that similar to our proposal in [1] two main use cases that are new relative to 11ac require simulations to asses performance:
  Outdoor deployments – generally new scenario. This scenario may also require improved performance for large number of STA since the range of the AP is larger (Pico AP).
  Indoor/Outdoor dense deployments such as in dense urban apartments, stadiums, airports and enterprise environments whereby the emphasis is on maximizing the aggregate throughput in all BSS as opposed to a point to point link improvement
We propose here a minimal set of two general simulation scenarios that provide good representation of all use cases.

## Slide 7: Scenario 1: Outdoor with/without Indoor
1a – Outdoor only (indoor assumed on different frequency)
  Operator deployed Hotspot Pico (covering an airport terminal, shopping center, park, neighborhood) with typical inter site distance (ISD) 100-200m
  AP location on a regular grid with some random perturbation
    e.g. random location within a circle centered at grid points with radius equaling 20% of ISD
  AP power up to 30dBm (per regulatory limitations in both 2.4GHz and 5GHz). STA power up to 15dBm (current smartphone Tx power)
  Up to 100 users in BSS. Number of AP varies depending on the assumed frequency re-use
  All users are assumed outdoors
1b – Outdoor + Indoor
  This scenario has outdoor (large) and indoor (small) cells in order to test cross interference issues when those BSS share the same frequency with overlapping areas (small cells may be completely within large cell range)
  The outdoor and indoor APs are each dropped in the same area but with different density and use different channel model (outdoor/indoor).
  Outdoor users associate to outdoor AP or indoor AP (if within a defined range). Indoor users associate to indoor AP.
    X% of users dropped within Y[m] of indoor AP, out of which 80% are indoor and 20% outdoor. All those users associate with indoor AP
    (100-X)% of users dropped randomly throughout the area, assumed to be outdoor and associate with outdoor AP.

## Slide 8: Scenario 2: Dense Deployment
2a - Planned deployment (enterprise, stadium, airport terminal, train station):
  AP density is set higher at ISD=15-30m
  AP location on a regular grid with some perturbation
  AP and STA power variable.
  N STAs per AP and M APs.
    Values of N and M TBD.
    The product NxM may need to be limited to control simulations run-time.
    N may also be reduced to about 10 when assuming full buffer traffic (representing much larger number of STA with more realistic traffic).
  All BSS use the same channel model (outdoor or indoor).
  One or multiple operators (impacting association rules)
2b - Unplanned deployment (high density apartments)
  K floors with M apartments per floor. Apartment size 100 sq.m.
  One or more AP located randomly within each apartment.
  N STA per AP.
  Limitations on KxNxM similar to scenario 2a.
  Each AP only supports traffic from STA in the same apartment

## Slide 9: Summary
Proposed initial thoughts on two documents – system simulation methodology and simulation scenarios.
Propose to start developing those documents.

## Slide 10: References
  [1] 11-13-0486-01-0hew-metrics-targets
  [2] 11-13-0657-02-0hew-hew-sg-usage-models-and-requirements-liaison-with-wfa

## Slide 11: Appendix - PHY Abstraction
High level guidelines:
  Start from an agreed upon AWGN per-MCS SISO performance curves
  With one receive antenna:
    Compute SINR per tone – the ‘S’ term is a function of the Tx power and channel. The ‘I’ term is due to OBSS, intra-BSS interference or MU-MIMO. Note that ‘I’ could vary during a packet due to shorter interfering packet than the desired or start of new interfering packet midway through the desired packet.
    Calculate the per-tone capacity (log2(1+SINR), could be constrained to 256QAM) and average across all tones
    From 2, derive the averaged SINR per tone.
    Transform back to MCS using the MCS table
  With multiple receive antennas:
    SINR should reflect the receive combining output from all antennas.
    For MIMO simulation, linear per-stream SINR can be computed.