## Slide 1: Possible Approaches for HEW
Date: 2013-07-12
Authors:

## Slide 2: Abstract
This submission shows ideas for performance improvement in a densely deployed environment of APs and/or STAs .
Straw polls about candidate mechanisms for HEW are included at the tail of this submission.

## Slide 3: Changing Landscape around WLAN offload
  Increasing Cellular LTE Terminals
  Emerging LTE-Advanced Terminals
  Increasing 5GHz Compliant STAs
  Increasing Private APs
  (Mobile Routers, Tethering Terminals)
  Users choose LTE/LTE-A unless WLAN offers better QoE* whenever connected. (*not a theoretical throughput)
  5GHz will no more be a last resort.
  Unmanageable interference will damage QoE noticeably.

## Slide 4: Major Cause of Performance Degradations
Congestion
  Congestion is caused by inefficient resource allocation to management/control frames rather than user’s data frames.
Interference
  Interference affects performance where sufficient SNIR margin is not available.
Frame Conflicts/Losses
  Frame Conflicts/Losses are caused by hidden terminal effects, overlapping BSSs, etc.

## Slide 5: Congestion (1/4) Recap. from slide 9 of doc. 13/523r2
(Frames)
Many management frames were observed on 2.4GHz channel during 5 minutes monitoring. They occupied almost 65% of all frames.
Current time usage on 2.4GHz band is not effective.
Channel Utilization
80~90%
Below 10%

## Slide 6: 1. Congestion (2/4)
Here is available airtime:
0
100
Occupied
If 90% of airtime, for example, is occupied by frames, Inter-Frame Space and CW…
It’s surely congested.

## Slide 7: 1. Congestion (3/4)
When airtime is occupied mainly by data frames,
Data
it’s congested but efficient.
When airtime is occupied by more management/control frames,
Data
it’s congested and not efficient.
Management/Control

## Slide 8: 1. Congestion (4/4)
When many STAs are associated, allocated time per STA is small. It is possible to allocate more airtime per STA by limiting number of associated STAs.
Shared by many STAs
Shared by less STAs
Slower
Faster
It is preferred for HEW to use more airtime for data frames.
Reducing management/control frames and limiting number of associated STAs are possible improvements for better QoE.

## Slide 9: 2. Interference (1/2)
There must be no problem when RSSI satisfies required S/(N+I).
N+I level increases where APs/STAs are densely deployed.
dBm
Distance from AP
Received Signal Strength
of AP signal
Noise + Interference
Sources of N+I
Non-WLAN signal
Very weak WLAN signal
Internal noise
Required SNR
Coverage area
0
Not-weak WLAN signals should be considered as sources of congestion.

## Slide 10: 2. Interference (2/2)
How can we mitigate bad effects of interference?
  STAs have to be connected to an AP only in the area where sufficient S/(N+I) is available, i.e. places that are close enough to an AP.
It is very important that STAs keep as silent as possible when they are not associated with an AP in order to suppress air congestion.
Candidate solution is to make STAs communicate with an AP only within a distance from the AP which is close enough to overcome interference issues.

## Slide 11: 3. Frame Conflicts/Losses (1/3)
Frame conflicts occur by existences of hidden STAs.
Case 1 (single AP):
AP
STA1
STA2
Conflict
STA1 & 2 are visible from AP.
STA1 &2 are much far. They are hidden terminals each other.
Sometimes frames from STAs will run into in that case.
HCCA is known as one of solutions to avoid issues of hidden terminals.
Hidden terminals

## Slide 12: 3. Frame Conflicts/Losses (2/3) OBSS management
Case 2 (multiple APs):
  11aa provides measures for managing OBSS environment by exchanging QLoad Report.
QLoad Report
QLoad Report
QLoad Report
QLoad Report delivers QoS load information between APs.
It also enables coordination of scheduled HCCA TXOPs among APs.

## Slide 13: 3. Frame Conflicts/Losses (3/3) Time reuse coordination
As an analogy of channel reuse concept of cellular, time (T) reuse coordination among APs may provide measures to prevent frame conflicts in OBSS environment.
T1
T3
T2
T1
T3
T2
T1
T3
T2
T1
T3
T2
T3
T1
T2
This scheme may mitigate frame conflicts/losses in this area.
Enhancement of HCCA and OBSS management may be candidate solutions for HEW.
The real world will be definitely different from this pattern.

## Slide 14: Other considerations
Mixed operation with legacy devices,
Usage improvement of 2.4GHz band,
Adaptation to real world,
And more…

## Slide 15: Summary
Congestion
  It is more efficient to transmit more Data frames rather than Management/Control frames.
  Limiting number of associated STAs delivers better QoE.
Interference
  It will be a solution to prevent communication at cell edge for mitigating bad effects from interference.
Frame conflicts/losses
  It may be a candidate solution to enhance HCCA and OBSS management function.

## Slide 16: Straw Poll -1
Do you agree that limiting number of associated STAs should be one of the functions of “High Efficiency WLAN” for obtaining minimum QoE in environment densely deployed APs and STAs?
Yes :
No :
I don’t know / Need more studies :

## Slide 17: Straw Poll -2
Which one can mitigate bad effects of congested WLAN situation?
Combination of existing standards :
New standards :
Both of 1 & 2 :
I don’t know / Need more studies :

## Slide 18: Straw Poll -3
Which one will mitigate bad effects of interference in WLAN environments?
Combination of existing standards :
New standards :
Both of 1 & 2 :
I don’t know / Need more studies :

## Slide 19: Straw Poll -4
Do you like to study resource coordination among neighboring APs to increase aggregated area throughput and to mitigate frame conflicts as mentioned in Slide 12 & 13 of this document?
Yes :
No :
Need more info/studies :
This poll is just for getting common interests of the floor.
It’s not requiring any commitments.

## Slide 20: References