## Slide 1: Discussions on System Level Simulation Methodology
Date: 2013-7-16
Authors:

## Slide 2: Outline
Slide 2
Reference HEW usage models
Proposals on simulation scenarios for selected use cases
Performance metric
Channel model considerations
Traffic model considerations
Summary
Wu Tianyu
Notes: doc.: IEEE 802.11-08/1101r3
September 2008
        John R. Barr, Motorola, Inc.
Page 2

## Slide 3: Reference HEW usage models (extracted from usage models document[1]) (1)
Slide 3
Wu Tianyu
 |  |  |  | AP distance (m) | STA density (/m^2) | Indoor /outdoor | Interference
1 | high density of APs and high density of STAs per AP | a | stadium | 12~20 | 0.5 | I | Same ESS/P2P/TD-LTE
 |  | b | airport/train stations | 15~20 | 0.6 | I | Same & Multi ESS/ P2P/TD-LTE
 |  | c | exhibition hall | 5~10 | 1 | I | Same ESS/ individual AP/P2P/TD-LTE
 |  | d | shopping malls |  |  | I | Same ESS/ individual APs/ TD-LTE
 |  | e | E-Education | ? | 40~60 per AP | I | Same ESS/P2P
2 | high density of STAs | a | Dense Wireless Office | <50 | 20~30 STA per AP | I | Same and Multi ESS/ P2P
 |  | b | public transportation | inf | 100/30 | I | surrounding outdoor environment for public transports
 |  | c | lecture hall | ? | 300/10000 | I | neighbors, other WLANs
Notes: doc.: IEEE 802.11-08/1101r3
September 2008
        John R. Barr, Motorola, Inc.
Page 3

## Slide 4: Reference HEW usage models (2)
Slide 4
Wu Tianyu
3 | high density of APs (low/medium density of STAs per AP) | a | dense apartment building | 5~20 | 5/100 | I | unmanaged overlapping networks
 |  | b | Community WiFi | ? | ? | I/O | private and public traffic
4 | new outdoor deployments | a | Super dense urban Street | 20~50 | 0.5~1 | O | Same&Multi ESS/ individual AP/ P2P/ LTE
 |  | b | Pico-cell street deployment | 150~200? | ? | O | 
 |  | c | Macro-cell street deployment | 500 | 180 per sector (0.0025) | 20%O/80%I | 
Proposals on simulation scenarios in the following slides are developed mainly based on the use cases highlighted in RED.
Notes: doc.: IEEE 802.11-08/1101r3
September 2008
        John R. Barr, Motorola, Inc.
Page 4

## Slide 5: Simulation Scenario for Category 1
Slide 5
Wu Tianyu
Category 1: high density of APs and high density of STAs per AP
Indoor area
10 APs are deployed on two parallel lines with 20 m inter-AP distance (0.25 AP/100m2) .
1000 STAs are randomly dropped within the 4000 m2 (100m x 40m) area (100 STAs/AP).
Notes: doc.: IEEE 802.11-08/1101r3
September 2008
        John R. Barr, Motorola, Inc.
Page 5

## Slide 6: Simulation Scenario for Category 2
Slide 6
Wu Tianyu
Category 2: high density of STAs
  Indoor area
  3 APs are placed in a line with a distance of 50 meters between each other. (0.04AP/100m2)
  300 STAs uniformly distributed in the room 150m x 50m. (100 STA/AP)
Notes: doc.: IEEE 802.11-08/1101r3
September 2008
        John R. Barr, Motorola, Inc.
Page 6

## Slide 7: Simulation Scenario for Category 3
Slide 7
Wu Tianyu
Category 3: high density of APs (low/medium density of STAs per AP) [4]
  Indoor area
  2-floor building with 3 meter high. 10 apartments on each floor.
  One AP in each apartment of 10mx10m randomly positioned. (1AP/100m2)
  20 STA per floor randomly positioned in each floor (2 STAs/AP) .
Notes: doc.: IEEE 802.11-08/1101r3
September 2008
        John R. Barr, Motorola, Inc.
Page 7

## Slide 8: Simulation Scenario for Category 4
Category 4: new outdoor deployment
  Outdoor area: AP co-site with small cell, Refer to 3GPP TR36.872 [2]
  For each operator
    4 AP uniformly random dropping within cluster area with radius of R1=50m.
    40 STA uniformly random dropping within cluster area with radius of R2=70m.
  2 operators are overlapped in the same cluster area.
Slide 8
Notes: doc.: IEEE 802.11-08/1101r3
September 2008
        John R. Barr, Motorola, Inc.
Page 8

## Slide 9: Performance metric
Performance Metric |  | Definition | Calculation method
Aggregated Throughput per AP (bps) |  | The aggregated throughput of an AP | Sum number of bits transmitted by AP in the target period of time / the target period of time
Area Throughput (bps/m2) |  | The total throughput recorded in the unit target region | Sum throughput of all APs in the target region/ Area of the target region
QoS: | Delay(ms) | QoS metric for delay insensitive applications: Given a target packet loss rate, the average delay of the packets | Total delay of a number of packets / The number of packets
 | Packet Loss rate | QoS metric for delay sensitive applications such as conversational video and voice: Give the target delay (20ms for VoIP for example), the average percentage of packet loss. The lost packets include all outage packets and all dropped packets due to over delay | Total number of packets lost / The total number of packets transmitted
Slide 9
Notes: doc.: IEEE 802.11-08/1101r3
September 2008
        John R. Barr, Motorola, Inc.
Page 9

## Slide 10: Channel Model Considerations
Channel model | Application Environments | Central frequency | Bandwidth | velocity | Simulation Scn
TGn/ac channel B | Residential(Intra-room, room-to-room) | The model can be used for both 2 GHz and 5 GHz frequency bands | Maximum support 1.28GHz | v0=1.2 km/h]for11n v0=0.089 km/h for 11ac | Scn 3
TGn/ac channel C | Residential/small office(Conference room, classroom) |  |  |  | 
TGn/ac channel D | Typical office(Sea of cubes, large conference room) |  |  |  | Scn 2
TGn/ac channel E | Large office(Multi-story office, campus small hotspot) |  |  |  | Scn 1
TGn/ac channel F | Large space (indoors/outdoors) (Large hotspot, industrial, city square) |  |  | v0=1.2 km/h] for 11n v0=0.089 km/h for 11ac v1=40 km/h for 11n/ac | Scn 4
IMT-A Uma | Urban macro | 2GHz~6GHz | 100MHz | 0~350 km/h | [3]
IMT-A Umi | Urban micro |  |  |  | 
Discussion: Considering the IMT channels can only support up to 100MHz bandwidth, can we use Channel F in outdoor scenarios?
Slide 10
Notes: doc.: IEEE 802.11-08/1101r3
September 2008
        John R. Barr, Motorola, Inc.
Page 10

## Slide 11: Traffic Model Considerations
Slide 11
Wu Tianyu
Traffic model for the following applications shall be considered
  Video Streaming
    Including UHD (8k*4k) and VHD (4k*2k)
    Both Lightly-compressed and compressed.
  VoD control
  Video Conference
  Audio / HD audio streaming
  VoIP
  File transfer
    Content download (photo camera)
    Internet file transfer (email/web/chat)
    Local file transfer, printing
  Remote user/Cloud desktop
  Infinite source model
Discussion:
  How to mix multiple traffic types for each scenario?
  How to model the new traffic types, e.g. VDI?
Notes: doc.: IEEE 802.11-08/1101r3
September 2008
        John R. Barr, Motorola, Inc.
Page 11

## Slide 12
Summary
4 simplified simulation scenarios are proposed corresponding to the 4 categories of use cases:
  Scenario 1: high density of APs and high density of STAs per AP
  Scenario 2: high density of STAs
  Scenario 3: high density of APs (low/medium density of STAs per AP)
  Scenario 4: new outdoor deployment
The performance metrics of AP throughput, Area throughput, delay and packet loss can be used in simulation according to functional requirements.
The detail designs for each scenarios are FFS, e.g. channel model, traffic mixture etc.

## Slide 13: References
July 2013
Wu Tianyu
Slide 13
Slide 13
[1] 11-13-0657-02-0hew-hew-sg-usage-models-and-requirements-liaison-with-wfa
[2] 3GPP R1-132812 TR 36.872 small cell enhancements
[3] ITU-R M.2135-1 (12/2009) Guidelines for evaluation of radio interface technologies for IMT-Advance
[4] 11-13-0538-02-0hew-dense-apartment-building-use-case-for-hew
Notes: doc.: IEEE 802.11-08/1021r0
July 2008
        Peter Loc
Page 13
doc.: IEEE 802.11-08/1101r3
September 2008
        John R. Barr, Motorola, Inc.
Page 13