## Slide 1: Effect of Power Save on Time-Sensitive Multicast Services
Date: 2013-07-14
Authors:

## Slide 2: Abstract
Several time-sensitive services use multicast addressing to reach many devices simultaneously. Two examples are NTP and the Clair Global Aermonix audio delivery system for concerts and music festivals. However, when any device on the BSS requests to enter Power Save mode, the AP buffers all multicast packets to all clients until the next DTIM beacon frame, regardless of whether the device has joined that time-sensitive multicast service or not. This causes added latency, compromising those time-sensitive services. This paper presents the problem and possible solutions for the WG to consider.

## Slide 3: Multicast During Power Save Mode
IEEE 802.11-2012, 10.2.1.1, fourth paragraph:
  “If any STA in its BSS is in PS mode, the AP shall buffer all group addressed BUs and deliver them to all STAs immediately following the next Beacon frame containing a DTIM transmission.”
This is true no matter which multicast services each client STA has joined.

## Slide 4: Time-Sensitive Multicast Services (1)
Audio & Video Streams for Large Audiences
  Concert Sonics “Aermonix” system
  Designed for large events: 1,000 to 100,000 clients
    Music festivals, Rock concerts, Theatrical, Symphonies, Operas, Sports, Etc.
    20 to 2,000 clients/AP
    Delivers “Front of House” stereo audio mix to every client device in the venue via IEEE 802.11
    Improved audio experience, especially for listeners farthest from the stage
      Restores high frequencies lost in acoustic path
      Eliminates reverberation effects due to hard surfaces
    Must deliver the audio data stream faster than the speed of sound.
      Aermonix app time aligns the audio data to the sound from the stage speakers

## Slide 5: Time-Sensitive Multicast Services (2)
Network Time Protocol (RFC 5905)
  Supplies time and date information for any client device on the Internet
  Defines the accuracy of the client’s internal time of day services
Any other service requiring low latency delivery to many clients
  Often, but not necessarily, audio or video services.

## Slide 6: Power Save on Multicast Services (1)
Any device associated with the AP can initiate Power Save mode.
  Even devices that have not joined the multicast service.
  This causes all audio packets to buffer until the next DTIM beacon frame, typically 100 msec max.

## Slide 7: Power Save on Multicast Services
Scenario: Music Festival
  Hundreds of users listening to the audio stream on an AP
  One user connects their device with the AP.
  After association, the device enters Power Save mode, causing group addressed audio packets to wait until the next DTIM beacon frame.
  Suddenly, the audio stream to hundreds of listeners is buffered longer than the acoustic propagation time from the speakers.
  Audio experience for hundreds of listeners is destroyed by this one new device.
  The new device is not even a member of the audio multicast service.

## Slide 8: Effect of Power Save on Audio Latency
Max. added latency = 100 msec.
Max. added latency = 100 msec.
100 msec. Beacon Interval
5.8 msec
Isochronous Packet Intervals
100 msec. Beacon Interval
Isochronous Packet Intervals
2.9 msec.
Isochronous Packets @ 256 Audio Samples/Packet
Buffered Packets @ 256 Audio Samples/Packet
Isochronous Packets @ 128 Audio Samples/Packet
Buffered Packets @ 128 Audio Samples/Packet

## Slide 9: Existing Solutions
Use Directed Multicast Service
  AP converts all multicast packets to clients to unicast. (IEEE 802.11-2012, Section 10.23.15)
  Channel can only support 20 to 30 clients
Change DTIM Beacon Interval
  DTIM = 1, Beacon Interval = 10 to 20 msec.
  For NTP, this still adds 10 to 20 msec of timing uncertainty.
  For concerts, it adds 3 to 7 meters (11 to 22 feet) minimum latency, eliminating many potential listeners in the venue.
  Increases channel load with additional beacons.
Neither of these are adequate long term solutions.

## Slide 10: Possible Solutions
If client requesting PS mode has not joined the multicast service associated with the incoming group addressed packet:
  Do not buffer the group addressed packets for that service.
Reserve a traffic class and associated queue for unbuffered multicast services.
  Limited number of queues
Other alternatives?
  Where would this work belong in the WG?

## Slide 11: Going Forward
Straw Poll:
  Should the WG pursue solutions to this problem?
    Yes
    No
    Abstain
If so, then:
  Form a new Study Group?
  Assign this to the IEEE 802.11 Architecture Group?
  Assign this to a different existing group? (HEW?)

## Slide 12: References
IEEE 802.11-2012, “Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications.
RFC 5905, “Network Time Protocol Version 4: Protocol and Algorithms Specification”, Mills, et al, IETF, June 2010.
Aermonix, Andrei Krishkevich, iTunes Store, updated 01 July 2013.
  https://itunes.apple.com/us/app/aermonix/id630108107?mt=8