## Slide 1: HEW Usage Scenarios Categorization
Date: 2013-07-14
Authors:

## Slide 2: Abstract
In this presentation we follow on from 13/0514 and categorize usage models, down select models to cover a range of categories, and provide more detail on select usage models.

## Slide 3: Usage Scenario Categorization
AP Density
Client Density
Single versus multiple management domains
Indoor/Outdoor

## Slide 4: Single Management Domain

## Slide 5: Applications and Requirements in Single Management Domain
Stadium
  Video
    Point-of-Sight Selective Mobile Broadcasting
    Event broadcast, multicast
    Reception of VHD video feed highly compressed, 100 Mbps
  Internet/Server Access
    User upload
    Internet access; 20 Mbps
    ESPN (or equivalent) for supplemental content
  Cellular offload
    Cellular tethering / mobile hotspot
  1 AP / 50-100 sq.m.; up to 100 STAs / AP
  Large indoor or outdoor
Large Office Enterprise
  Unified communications
  Cloud-based Virtual Desktop Infrastructure: 100 Mbps, best effort.
  Wireless display
    desktop, projector
    Tele-presence / video conferencing
    VHD: ~600Mbps, jitter is <30 ms, delay is < 30ms, 1.0E-7 PLR*.
    Multicast
  Wireless docking and storage
  Large indoor
Other
  Many devices associating to an AP simultaneously (e.g. start of class, lecture, or public transportation)
  Online gaming; 100 Mbps, < 20 ms jitter; < 20 ms latency
  Video on Demand, 20Mbps / STA
  *under review, aim to relax requirement by resiliency of upper layers

## Slide 6: Multiple Management Domains

## Slide 7: Applications and Requirements in Multiple Management Domains
Dense Outdoor Hotspot
  Video streaming, 20-100 Mbps / STA
  Internet/Server Access, 10-20 Mbps / STA
  Online gaming; 20 Mbps
  The inter-AP distance 10~200m
  User density .1-1 user/m^2
  Cellular offload
  D2D discovery
  Real-time Video Analytics & Augmented Reality
  wearable devices
  Seamless hand-over between Cellular & WiFi
Dense Apartment / Residential (indoor)
  Building automation and connectivity (e.g. security, utilities)
  Cellular offload
  Compressed video streaming, 20-100 Mbps
  Uncompressed streaming, > 1 Gbps
  Internet access, 20 Mbps
  Online gaming
  Inter-AP distance 5-30m
Other
  Indoor location
  Push, data download (e.g. coupons at the mall)

## Slide 8: Usage Model: Dense use of wireless docking in large office enterprise
Pre-Conditions:
User has operational WLAN network for Internet access and general data networking. The wireless network used for storage and display may or may not be part of the other operational WLAN network.
Application:
User can wirelessly display the output of the computer to monitor.
User can wirelessly store data from a computer to a harddrive.
Environment:
Devices are operating in close proximity to other similar clusters in a multi-cube office. Transmissions are mostly LOS.
Traffic Conditions:
Potential interference from overlapping networks (e.g. neighbors, other WLANs). Data transfers and video display should be operational simultaneously.
Use Case:
User sits down to their desk, turns on their computer.
Computer wirelessly forms an association to an external hard drive and the display with minimal user configuration.
User works for extended hours without a visible sign that the display is using wireless technology.
User stops working, then turns off computer.

## Slide 9: Further details
Docking / P2P
  Wireless Display
    target video rate: up to 300-600 Mbps
    Latency: <30 msec (30 frames/ sec; 1 frame latency)
    Connection: mobile device to display
  Keyboard, mouse:
    Low latency
    Low throughput
    Connection: K/M to mobile device
  External storage & other peripherals
    storage
      Short bursts of peak rate (e.g. USB3): 500-600 Mbps
      Connection: bi-directional between mobile device and external storage
    Other peripherals
      Data rate:
      Latency:
Standard network access from AP
  10-20 Mbps
Cubicle size
  3x3 meter
  Docking solution every cube

## Slide 10: Usage Model: Stadium
Covered in 11-13/0657r1, slide 17

## Slide 11: Usage Model: Dense Outdoor Hotspot
Covered in 11-13/0657r1, slides 37-40

## Slide 12: Further details on Real-time Video Analytics & Augmented Reality
Upload of image/video
Image
  uplink
  descriptor data rate: 100kbps
  Latency not an issue
Video
  Video on uplink
  Round trip delay (for getting information back): 10’s msec
  data rate: ?
  Textual/vector information on downlink
Density of devices, many people using on their smart phone in close proximity

## Slide 13: Further details on wearable devices
Propagation environment
  Body area network
Multimedia requirements
  640x480 : 1-2 Mbps
  PLR: 10^-5 or 10^-6*
  Quality: MOS
  Latency: 10’s of msec
  Uplink
Severe limitations on power consumption, size, antennas and EIRP
Connectivity: either to an AP or companion device
Density of devices: many people wearing in close proximity

## Slide 14: Usage Model: Dense Apartment / Residential
Covered in 11-13/0657r1, slides 33-34

## Slide 15: References
https://mentor.ieee.org/802.11/dcn/13/11-13-0657-01-0hew-hew-sg-usage-models-and-requirements-liaison-with-wfa.ppt
https://mentor.ieee.org/802.11/dcn/13/11-13-0514-00-0hew-usage-scenarios-and-applications.pptx
https://mentor.ieee.org/802.11/dcn/07/11-07-2988-04-0000-liaison-from-wi-fi-alliance-to-802-11-regarding-wfa-vht-study-group-consolidation-of-usage-models.ppt