## Slide 1: Functional Requirements in HEW
Date: 2013-07-16
Authors:

## Slide 2: Introduction
There have been many presentations to discuss various use cases until May meeting
In order to go over functional requirements,
  Categorize use cases based on environment characteristics (e.g. indoor/outdoor condition, AP/STA density) first as we’ve done in [1]
  Discuss technical aspects which are going to be essentially enhanced in HEW
Based on that, functional requirements and considerable performance metrics are presented

## Slide 3: Use Case Categorization
Environment | Deployment density and use cases |  | Characteristics
Indoor | High density of both APs and STAs | Stadium Airport/train stations Exhibition hall Shopping mall E-education | Possibly planned deployment Simultaneous real-time service users - information of voucher, flight, class, etc
 | High density of APs | Dense apartment building Community Wi-Fi | Private APs independently set up Partial mix of indoor and outdoor
 | High density of STAs | Dense wireless office Public transportation Lecture hall | Possibly planned deployment Simultaneous real-time service users - online meeting, lecture contents, etc

## Slide 4: Use Case Categorization (cont’d)
Environment | Deployment density and use cases |  | Characteristics
Outdoor | High density of both APs and STAs | Super dense urban street Pico-cell street deployment Macro-cell street deployment | Higher probability of unplanned deployment High quality of services under outdoor channel impairment
Throughput-demanding | Depending on places | Home with high-end devices (multimedia distribution) Smart car | Demand on high throughput - Single/multi-STAs

## Slide 5: Technical Aspects on Scenarios
Indoor scenario
  Environment: high density (AP or STA or both)
    Planned deployment
      E.g. E-education, dense wireless office, public transportation, lecture hall , stadium, airport/transportations, exhibition hall, shopping mall where coordination between APs may be possible by a network management system
      AP location can be manageable and average number of accessing users may be predictable
    Unplanned deployment
      E.g. Dense apartment building, community Wi-Fi where coordination between APs may not be possible due to different network managers/operators
      AP location may be random in different places and floors (there could be also independent/private APs), which will result in more difficult OBSS problem with unmanageable interference

## Slide 6: Technical Aspects on Scenarios (cont’d)
  Requirements
    Distributed system throughput
      STAs in BSS fringe area can suffer from significant performance degradation from many OBSS under HEW scenario
      Unlike conventional Wi-Fi that has pursued mostly high system throughput, HEW may take into account BSS edge throughput enhancement as well as overall system throughput (“Distributed” traffics)
      Enabling technologies:
        Interference management or OBSS control (e.g. frequency reuse/sectorized beamforming, power control, etc)
        Scheduled channel access like OFDMA

## Slide 7: Technical Aspects on Scenarios (cont’d)
  Requirements
    Seamless data transfer
      A user can suffer low quality of service from overloaded medium access
      Real-time service couldn’t be reliably served to the user when a lot of STAs try to access medium simultaneously
      Link set-up needs to be fast and manageable without knowing traffic condition in aspect of end user
      Enabling technologies:
        Overhead reduction on control/management frames
        Efficient polling and prioritized transmission based on services
        Well distributed channel access and backoff mechanism (e.g. specifically effective in very high density)
        Access load balancing (association control among APs)
        Seamless handover (doesn’t mean support for high mobility but rather support smooth migration to AP with minimized management overhead)

## Slide 8: Technical Aspects on Scenarios (cont’d)
Outdoor scenario
  Environment: high density (both AP and STA) and channel impairment
    Most are probably unplanned deployment in outdoor where coordination between APs may not be possible due to many different network and users
      E.g. Super dense urban street, pico-cell street deployment, macro-cell street deployment
    Besides density issue, there could be more challenges in outdoor, which let us check PHY feature enhancement to cover those issues as shown in the previous contribution [2]
<Examples of using larger FFT against delay spread in outdoor>
InH
InH
InH
InH

## Slide 9: Technical Aspects on Scenarios (cont’d)
  Requirements
    What we discussed in dense indoor case (previous slides) are similarly considered in outdoor case
    Outdoor specific: Performance reliability in outdoor channel
      Longer delay spread causes inter-symbol interference and fast channel variation makes the channel information outdated and distorted, which are going to degrade user performance and BSS coverage [3]
      For outdoor use cases, it is good to consider functionalities to make system reliable in a given range
      Enabling technologies:
        Longer CP or larger FFT size, fast feedback channel, enhanced link adaptation mechanism, HARQ
          Need to check first on existing technologies and consider further enhancement if needed

## Slide 10: Technical Aspects on Scenarios (cont’d)
Throughput-demanding scenario
  Environment: density is depending on places
    Support for throughput enhancement is the most important feature in this scenario
      E.g. Home with high-end devices (multimedia distribution), smart car
  Symbolic feature to show the attractive to the market/end user aspect
    Most of new standards have pursued for this requirement
    End users wouldn’t take surrounding traffic condition into account
  Requirements
    Throughput enhancement
      Consideration on increase of maximum achievable throughput
      Enabling technologies:
        Increase of the streams of DL-MIMO, the order of modulation, the size and number of available BW
        Introducing UL-MIMO

## Slide 11: HEW Functional Requirements
Issues | Functional Requirements | Performance metric
OBSS problem in BSS fringe area: low data rate in edge users | Distributed system throughput | Minimum per device throughput Average areal throughput [4]
Overloaded medium access: low quality of user experience | Seamless data transfer | Average access delay* Average round trip delay** X number of active real-time service users
Outdoor channel impairment: larger delay spread and fast channel variation | Performance reliability in outdoor channel | Average user throughput***
Demand on high throughput | Throughput enhancement | Single-STA throughput (Aggregated) multi-STAs throughput
*: measured from the time the DCF or EDCAF MPDU which is ready for transmission
(i.e., begins CSMA/CA access) until the actual frame transmission start time [5]
**: measured from the time for packet Tx + acknowledge which affects the throughput rate
***: at X km given BSS range

## Slide 12: Conclusion
Unique identification on HEW SC
  With respect to the environments
    Hotspots for public access and cellular offload in dense area
    Outdoor usage model (including indoor + outdoor)
  With respect to the applications
    Fairness for all users
    Emphasis on quality of experience
    Mix of multi-clients and multi-traffics
Features required in HEW
  Fair traffic distribution to most users
  High quality of user experience
  Performance immunity on outdoor condition
  Enhanced single/multi-STAs throughput

## Slide 13: Reference
[1] 11-13-0657-02-0hew-hew-sg-usage-models-and-requirements-liaison-with-wfa
[2] 11-13-0536-00-0hew-hew-sg-phy-considerations-for-outdoor-environment
[3] 11-13-0843-00-0hew-Further evaluation on outdoor Wi-Fi
[4] 11-13-0486-01-0hew-hew-metrics-targets
[5] IEEE Std 802.11TM-2012