## Slide 1: HEW Study Group Documentation
Date: 2013-07-15
Authors:

## Slide 2: Abstract
This presentation provides our view on the Study Group documentation that could help define PAR and enhance TG spec development.

## Slide 3: Background: 11ac PAR and Documentation
11ac PAR focused on optimizing link throughput in an isolated BSS.
  PAR: “A maximum multi-station (STA) throughput (measured at the MAC data service access point), of at least 1 Gbps and a maximum single link throughput (measured at the MAC data service access point), of at least 500 Mbps.”
Techniques & potential gains over 11n were understood even during SG phase.
  MIMO, 80 MHz BW, MU-MIMO etc.
  11ac 5C feasibility demonstration was relatively easy.
The following documents were not needed until TG phase.
  Channel model document
  Simulation scenario document
  Functional Requirements and Evaluation Methodology document

## Slide 4: HEW PAR and Documentation
    HEW study group formed in March 2013 has a focus on improving efficiency & area throughputs in indoor and outdoor environments, dense networks, moderate to heavy user loaded APs, and presence of interfering sources.
HEW SG is faced with a different set of challenges compared to VHT SG.
  Don’t understand what metrics to use in PAR.
  Don’t understand how to assess feasibility.
  Don’t know how to quantify gains over 11ac.
Hence, HEW SG may need some additional “guiding” documents to help form PAR metrics and scope.
  These documents can be leveraged by TG, to create the appropriate TG documents, and help accelerate overall spec development process.

## Slide 5: Proposed Document Creation in SG
Revised Usage Model Document incorporating WFA feedback.
  To have clear understanding of key categories and priorities for HEW.
Simulation Scenario document and Channel Model document.
  Identify a minimum set of representative simulation scenarios (e.g.: residential, enterprise and/or outdoor metro).
  Identify initial set of associated parameters and metrics.
  Should be representative of the Usage Models.
Evaluation Methodology document.
  Identify initial guidelines to evaluate gains of technology proposals.
  Includes channel models, metrics and MAC/PHY simulation details.
Note: Above SG Documents can be developed in parallel.

## Slide 6: Benefits of Early SG Documentation
Help form PAR metrics and scope.
Establishes well-defined scenarios and test methodology to evaluate potential gains and feasibility.
  Needed anyway in TG to reproduce/verify results or show gains.
  Avoids scenarios where proposals use “concocted simulations” to show gains.
Accelerate TG process.
  Why wait until TG launch to start developing these documents ?
  Early documentation avoids lengthy “process” debates in TG phase.

## Slide 7: Strawpoll
Do you agree with the proposal to develop the following SG documents ?
  Simulation scenario document
  Channel model document
  Evaluation methodology document
  These SG documents can be leveraged by TG, to create the appropriate TG documents.
  Yes -
  No -
  Abstain -