## Slide 1: 802.11ak Architecture
Date: 2013-07-16
Authors:

## Slide 2: Abstract
This presentation discusses
802.11ak architecture
802.11ak / 802.11 co-existence

## Slide 3: 802.11ak & 802.11 Co-existence
The 802.11ak architecture does not interfere with the existing 802.11 architecture
802.11ak BSS has its own SSID
  802.11ak non-AP STAs only are associated to 802.11ak AP STAs
    An attempt to associate a non-11ak non-AP STA to an 11ak BSS will always end in failure
    A BSS of mixed 11ak and non-11ak non-AP STAs is not possible

## Slide 4: 802.11ak & 802.11 Co-existence
Simplified interoperability
  Limited to BSS overlap
    11ak MSDU header must be discriminable and ignored by non-11ak STAs
  11ak Unicast MSDU address mapping could use the 4 MAC address for inner (P2P 11ak link) and outer MAC addresses
  11ak Multicast MSDU inner address mapping is TBD (but could use any new defined field to specify the MC set)

## Slide 5: 802.11ak MAC Port Services
The association of an 11ak non-AP STA to an 11ak BSS will result in
  the 11ak AP exports to its upper layers an instance of a MAC Port service of the point-to-point 11ak link instance between this AP and the associated 11ak non-AP STA
  the 11ak non-AP STA exports to its upper layers an instance of a MAC Port service of the point-to-point 11ak link instance between this non-AP STA and the 11ak AP to which it associated
  Note: 802.11ak Rev1 does not support non-AP STA to non AP STA direct links

## Slide 6: 802.11 and 802.11ak Architecture Co-existence Illustration: [1] The “Physical” View

## Slide 7: 802.11 and 802.11ak Architecture Co-existence Illustration : [2] The “Logical” View
11ak AP
11ak AP
11ak STA
11ak STA
11ak STA
cf Fig 4-6 IEEE Std 802.11™-2012

## Slide 8: 802.11 and 802.11ak Architecture Co-existence ESS across 11ak Link
roaming