## Slide 1: Further evaluation on outdoor Wi-Fi
Date: 2013-07-14
Authors:

## Slide 2: Introduction
Various outdoor use cases are discussed as HEW use cases
Compare to indoor environments, outdoor environments have quite different channel characteristics
  We should consider outdoor channel impact such as larger delay spread and larger channel variation.
During the May (2013) meeting, we provided some simulation results for outdoor channel model [1]
  Throughput loss due to inter-symbol-interference
  Larger channel variation due to larger number of channel taps
In this contribution, we provide further evaluation on outdoor channel model
  Frame Error Rate (FER) of SIG field and data field for different CP size
  Mean Square Error (MSE) of SIG field and data field for different CP size

## Slide 3: Outdoor features – delay spread
The maximum excess delay increases as distance between STA and AP increases [1]
<Examples of the maximum excess delay in outdoor channel(UMa) [1]>

## Slide 4: Outdoor features – delay spread
Larger delay spread causes larger inter-symbol-interference (ISI) which degrades system performance.
To solve the impact of larger delay spreads, we considered longer CP length by increasing FFT size while maintaining CP ratio for a given bandwidth, or by increasing CP ratio while maintaining FFT size [1].
In this contribution, we compare normal CP length (0.8us) and longer CP length (3.2us) for 20MHz bandwidth with 64 FFT size.

## Slide 5: Frame Error Rate Evaluation (1)
Following figures show FER performance for different STA location.
Quite severe FER performance degradation is observed for normal CP length.

## Slide 6: Frame Error Rate Evaluation (2)
Following figures show FER performance of SIG for different SNR or different effective SNR*.
Due to ISI effect, FER performance can’t be measured by SNR correctly, especially for normal CP length.
* see appendix for detail derivation

## Slide 7: Frame Error Rate Evaluation (3)
Following figures show FER performance of data frame (1ms) for different SNR or different effective SNR.

## Slide 8: Mean Square Error Evaluation (1)
Following figures show MSE performance for different STA location.
Quite severe MSE performance degradation is observed for normal CP length.

## Slide 9: Mean Square Error Evaluation (2)
Following figures show MSE performance of SIG for different SNR or different effective SNR.
Due to ISI effect, MSE performance can’t be measured by SNR correctly, especially for normal CP length.

## Slide 10: Outdoor features – Channel Variation
Due to different large scale fading effects, outdoor channel is varying faster than indoor channel even for same STA speed[1].
  if fast variations happen, it can lead to severe distortion of transmitted symbols or signals.
    Severe distortion of signal is able to lead problem of followings
      estimation, detection, loss of SNR, synchronization
  So, in order to the operation in outdoor environments, we should consider the effective Countermeasure to cut the impact of large channel variation

## Slide 11: Evaluation of Channel Variation
Following figure shows MSE variation according to time in outdoor channel model (UMa).
MSE saturation is observed for longer frame length for high SNR region.

## Slide 12: Conclusion
Quite severe system performance degradation is observed for system with normal CP length.
Due to ISI effect, SNR can’t measure system performance correctly.
  Effective SNR can measure system performance correctly while it is difficult to measure at STA.
  Discrepancy between SNR and effective SNR will bring further performance loss in link adaptation.
Worse channel estimation performance is expected for longer frame length especially for high SNR region.
  This is critical for higher MCS level.

## Slide 13: Appendix

## Slide 14: Channel Model
Scenario | UMa | 
 | LoS | NLoS
Delay Spread (log10(s)) | (-7.03,0.66)* | (-6.44,0.39)*
K-factor (K) (dB) | (9,3.5)* | N/A
Delay distribution | Exp | Exp
Delay scaling parameter | 2.5 | 2.3
Number of cluster | 12 | 20
Per cluster shadowing std ζ (dB) | 3 | 3
LoS probability as a function of distance, d(m) |  | 
* (μ,σ)
For SNR evaluation, we assume noise figure 5dB, cable loss 2dB, signal power 1W for 20MHz.
See page 30-41 of reference [2]

## Slide 15: Channel Model
Scenario |  | Path loss (dB) Note: fc is given in GHz and distance in m! | Shadow fading std (dB) | Applicability range, antenna height default values
Urban Macro (UMa) | LoS | PL = 22.0 log10(d) + 28.0 + 20 log10(fc) |  = 4 | 10m< d1 < d′BP (1)
 |  | PL = 40 log10(d1) + 7.8 – 18 log10(h′BS) –18 log10(h′UT) + 2 log10(fc) |  | d′BP < d1 < 5 000 m(1)
 | NLoS | PL = 161.04 – 7.1 log10 (W) + 7.5 log10 (h) – (24.37 – 3.7(h/hBS)2) log10 (hBS) + (43.42 – 3.1 log10 (hBS)) (log10 (d)  3) + 20 log10(fc) – (3.2 (log10 (11.75 hUT))2  4.97) |  = 6 | 10 m < d < 5 000 m h = avg. building height (20 m) W = street width (20 m) hBS = 25 m, hUT = 1.5 m
hBS = 25 m, hUT = 1.5 m, d′BP = 4 h′BS h′UT fc/c, h′BS = hBS – 1.0 m, h′UT = hUT – 1.0 m

## Slide 16: Delay profile vs. CP length
And we need to have proper modeling on how channel and CP impact performance.
One of possible modeling is as follows [3]:
TFFT is FFT period
CP is CP period
|αm|2 is power of m-th tap
τm is delay of m-th tap including OFDM symbol timing

## Slide 17: Simulation Assumption
 | CP1 | CP4
FFT size | 64 | 64
Used data subcarriers | 52 | 52
Symbol length with CP | 4us | 6.4us
CP length | 0.8us | 3.2us
Center frequency | 2.4GHz | 
Bandwidth | 20MHz | 
Channel model | UMa 3km/h | 
Channel Estimation | Least Square | 
Distance | 50, 75, 100, 125, 150, 200 m | 
Packet structure | Preamble +Data frame | 
Preamble | L-STF/LTF/SIG+VHT-SIG-A/STF/LTF/SIG-B =40 us | 
Data frame | SERVICE(2bytes) +MAC header(40bytes) +Data +Tail(6bits) +Padding | 
Notes: 천진영씨 update 부탁드립니다.

## Slide 18: References
[1] IEEE 802.11-13/0536r0- Wookbong Lee et al., “HEW SG PHY Considerations For Outdoor Environment,” May 2013
[2] Report M.2135, “Guidelines for evaluation of radio interface technologies for IMT-Advanced, ” available at http://www.itu.int/pub/R-REP-M.2135
[2] IST-4-027756 WINNER II D1.1.2 V1.2, “WINNER II channel models,” available at http://www.ist-winner.org/deliverables.html