## Slide 1: New Technique: Enabling Real World Improvement By Exposing Internal MAC State
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco | +1 408 5253346 | brianh@cisco.com

## Slide 2: HEW Has an Important Focus on Real World Performance
Do you support starting a new study group called “high efficiency WLAN” to enhance 802.11 PHY and MAC in 2.4 and 5GHz with a focus on:
    Improving spectrum efficiency and area throughput
    Improving real world performance in indoor and outdoor deployments
    in the presence of interfering sources, dense heterogeneous networks
    in moderate to heavy user loaded APs

## Slide 3: Problem: Real World Performance is Hard to Measure; Poor Performance is Hard to Root Cause
  An AP/client/[sniffer] can measure
    Medium utilization
    Retry rate of its transmitted packets
    Rate of retry bit being set
    Its throughput
    But oftentimes not understand
      Which STAs are contributing to high medium utilization (get PLCP headers but not MAC addresses)
      Why are retries happening (poor SNR/rate selection, contention with which STAs at what times, hidden node collisions with which STAs at what times and what RSSIs, non-Wi-Fi interference, etc)
      Why throughput is poor (retries, exposed node problem, non-Wi-Fi interference, etc)
  And then the right mitigation technique is hard to determine
  Existing Layer 1 solutions help to detect non-Wi-Fi-interference and the existence of collisions but many Layer 2 questions remain unanswered

## Slide 4: New Technique: Exposing Internal MAC State
  Infrastructure can reconstruct “all” wireless activity if each STA reports:
    Transmit:
      When each STA transmitted, for how long and with what bandwidth
      Successful or not
      CW and backoff values
      Buffer depths
    Receive:
      When each STA saw CCA busy & at what level
      When each STA detected a PLCP header and for what duration
      And the TA if available
  Observation: at 500 Mbps, we can fit 250 bytes into 4 us
    A STA can transmit a lot of MAC state with minimal new OTA overhead
    STA can send a HW-assisted final MDPU, in an A-MDPU, containing recent MAC state

## Slide 5: Exposed MAC State can enable a Virtuous Circle of Optimization
STAs expose their state
Infrastructure aggregates state and constructs complete wireless view
Infrastructure performs “what-if analysis”
Infrastructure adapts its and STAs’ MAC/PHY behavior to maximize UE
  Network tuning can lead to 2-10x improvements in dense networks (13/545r1)
  Robust, automated tuning is the holy grail

## Slide 6: MAC state is reported intermittently for the recent history, with redundancy for lost frames
  MAC state is reported for a window of the recent past
    No transmission is associated with reception events
    Control frames / 11a/b/g transmissions can’t carry MAC state in a final MDPU
  MAC state may be repeated across a few A-MDPUs
    Since any transmission can fail to be received
TX Data
RX
Only PLCP received OK
TX RTS
RX
CCA only
TX BA
MAC state, reporting recent transmissions, (A)MPDU receptions, PPDU receptions, CCA events
TX Data

## Slide 7: Status
  More R&D is required to make this proposal ready for standardization
    What are the right contents?
    What is the right encoding?
    How much repetition is enough / too much?
    Do we have the right control knobs; are new knobs required?
    Can we quantify the kinds of automated gains that are possible?

## Slide 8: Sample Contents within 250 octet Budget (1/2)
  4 most recent transmissions:
    Primary channel (1 octet) [for off-ch]
    Lower TSF of start time (3 octets)
    PHY format (~4 bits)
    PLCP header contents sans tail and FCS (17 + 34 bits)
    Total transmit power (6 bits)
    RA (6 octets)
    (Max) Retry number (4 bits)
    Success (6 bits, for AMPDU)
    AC (2 bits)
    ECW (4 bits) and random backoff (10 bits)
    Frozen slots during backoff (10 bits)
    Log8(BufferedOctets/16) (8 bits)
    …24 octets + 1 reserved per transmission; say 100 octets
  4 most recent good-PLCP receptions:
    Primary channel (1 octet) [for off-ch]
    Lower TSF of start time (3 octets)
    PHY format (~4 bits)
    PLCP header contents sans tail and FCS (17 + 34 bits)
    RSSI (6-8 bits)
    Good FCS (1 bit)
    TA (if available) (6 octets)
    Retry bit (if available) (1 bit)
    …17 octets + 1 reserved per transmission; say 72 octets

## Slide 9: Sample Contents within 250 octet Budget (2/2)
  8 most recent non-or bad-PLCP CCA Events:
    Primary channel (1 octet) [for off-ch]
    Lower TSF of start time (4 octets)
    Duration (2 octets)
    RSSI (1 octet)
    …8 octets per event + 1 reserved; say 72 octets
  Summary
  100+72+72 = 244 octets in all (plus overheads from A-MDPU subframe and MAC header/footer)
  More or fewer events can be transmitted according to the PHY rate, while keeping the overhead of MAC state reporting at well below the PLCP overhead
  MAC state reporting can be enabled/disabled

## Slide 10: Knobs that May Be Controlled More Optimally / More Dynamically
  Existing
    Channel assignment
    Bandwidth assignment
    Transmit power
    EDCA parameters
  Interesting
    CCA levels (new; but there would be enough information to do this robustly)
    Minimum MCSs for Beacon / Probe Request/Response frames
  Out of band
    Information provided to vendor of badly behaved clients; for driver update