## Slide 1: Quantitative QoE Requirements for HEW
Date: 2013-07-15
Authors:

## Slide 2: Motivation
In the previous 802.11 HEW meeting, Some members discussed the requirements for HEW [1-18]
In this presentation, we share our views on QoE requirements for HEW

## Slide 3: QoE is One of the Key Requirements for HEW
Whether HEW successful or not eventually decided by QoE satisfaction from users
Compared to cellular, the main concern from customers for Wi-Fi in high density area [1,4,7,11,12, 14, etc.]:
  No QoE can be maintained
With mobile video becoming the major traffic type, QoE provision is very important for HEW in consideration
  Mobile video >50% for the first time in 2011 among various traffic types
  Forecasted >70% by 2016
  More uplink video traffic will be generated
Source: The Cisco® Visual Networking Index (VNI) Global Mobile Data Traffic Forecast Update

## Slide 4: Challenge of Evaluating QoE
QoE is very subjective due to user’s perceptive feelings
  Literatures didn’t give measurable parameters clearly
In HEW, we need to define basic quantitative QoE parameters
  [4,5,11] recommended several parameters such as
    Minimum required average (or CDF) throughput per STA
    Maximum medium access delay
    Average area throughput
  [9] lists QoS parameters for various applications
    Rate, Packet error rate, delay, jitter, etc.

## Slide 5: Our Consideration for QoE
Strict QoS guarantee for any user and any application may not be realistic for Wi-Fi
  e.g. difficult to guarantee <20ms delay for any video packet
However, some basic QoE requirement needs to be satisfied particularly for AV applications
  e.g., a user will be disappointed if the screen freezes for several seconds during watch a youtube video clip
Some quantitative QoE parameters need to be defined
    Minimum average data rate for each traffic type requested by a user
    Maximum connection setup delay
    Maximum packet transmission delay
    Maximum information unit transmission delay, etc.

## Slide 6: Minimum average data rate for each traffic type
Need to have a minimum average data provision from Wi-Fi for smooth AV playback
  This parameter can be easily set with popular AV compression standards such as H.264
    Video itself can be adaptive in some range too
  One exception is truly lossless compression, but it is rarely used for HEW
For other traffic types such as web browsing or e-mail, will be difficult to define
  However, these applications are more delay tolerant
  From [9], 20kbps is the minimum data rate requirements for all traffic types
  If user/application cannot decide minimum data rate, use 20kbps may not be a bad idea
    Current Wi-Fi seems difficult to guarantee this rate in some worst cases

## Slide 7: Maximum connection setup delay
Definition of Connection setup delay:
  The duration between a user or application requests to use Wi-Fi for transmission and the first real data packet starts to be transmitted
Discussion
  Delay caused by Association, authentication and etc. should be included if haven’t been done
  Channel access delay requested by service discovery and other control messages also need to be included
Remarks
  Most likely a user will lose patience if this procedure takes longer than 20 seconds
  802.11ai helps to solve this issue partially
    But delay caused by some application/traffic specific control messages may still not be resolved

## Slide 8: Maximum packet transmission delay
This parameter also depends on traffic types
From [9] the maximum delay requirement is 400ms for all traffic types
  This value may be too big for some traffic types such as video gaming
  However, current Wi-Fi cannot guarantee this number as observed in some high-density Wi-Fi environment

## Slide 9: Maximum information unit transmission delay
This parameter also depends on applications
  An information unit is a data unit meaningful for end-users
  e.g., An information unit can be a web page for web browsing, a video frame for video streaming, etc.
Value of this parameter
  Seems 10 seconds is most users’ upper limit of tolerance
    Video streaming may be Ok with this value due to pre-buffering
  Interactive real-time video has more strict requirement like 100ms
Packet
Packet
Packet
Packet
.
.
.
.
.
.
One Information Unit

## Slide 10: Summary
Some minimum QoE performance need to be supported by HEW
It is important to define QoE requirements in a quantitative way
  With clear QoE metrics, the evaluation of the HEW technologies can be done fairly.
Some example QoE parameters are discussed
  Minimum average data rate for each traffic type
  Maximum connection setup delay
  Maximum packet transmission delay
  Maximum information unit transmission delay, etc.
Further discussions and comments are welcome on this topic
  e.g., how to map the application requirements to MAC/PHY parameters

## Slide 11: References
https://mentor.ieee.org/802.11/dcn/13/11-13-0113-00-0wng-applications-and-requirements-for-next-generation-wlan.pptx
https://mentor.ieee.org/802.11/dcn/13/11-13-0313-00-0wng-usage-models-for-next-generation-wi-fi.pptx
https://mentor.ieee.org/802.11/dcn/13/11-13-0486-01-0hew-hew-metrics-targets.pptx
https://mentor.ieee.org/802.11/dcn/13/11-13-0503-00-0hew-discussion-on-basic-technical-aspects-for-hew.pptx
https://mentor.ieee.org/802.11/dcn/13/11-13-0505-00-0hew-mac-efficiecy-analysis-for-hew-sg.pptx
https://mentor.ieee.org/802.11/dcn/13/11-13-0520-01-0hew-hew-scenarios-and-evaluation-metrics.pptx
https://mentor.ieee.org/802.11/dcn/13/11-13-0523-02-0hew-understanding-current-situation-of-public-wifi-usage.pptx
https://mentor.ieee.org/802.11/dcn/13/11-13-0524-02-0hew-discussions-on-functional-requirements.pptx
https://mentor.ieee.org/802.11/dcn/13/11-13-0527-02-0hew-usage-models-for-next-generation-wlan.pptx
https://mentor.ieee.org/802.11/dcn/13/11-13-0534-01-0hew-direction-and-use-cases-for-hew.pptx
https://mentor.ieee.org/802.11/dcn/13/11-13-0538-02-0hew-dense-apartment-building-use-case-for-hew.ppt
https://mentor.ieee.org/802.11/dcn/13/11-13-0545-01-0hew-wlan-qoe-end-user-perspective-opportunities-to-improve.ppt
https://mentor.ieee.org/802.11/dcn/13/11-13-0549-00-0hew-a-perspective-on-what-any-high-efficiency-wireless-tg-should-and-should-not-do.pptx
https://mentor.ieee.org/802.11/dcn/13/11-13-0555-02-0hew-considerations-on-functional-requirements-for-hew.ppt
https://mentor.ieee.org/802.11/dcn/13/11-13-0567-00-0hew-proposed-hew-usage-models.pptx
https://mentor.ieee.org/802.11/dcn/13/11-13-0626-01-0wng-a-mechanism-to-provide-qos-in-ieee-802-11e-mac.pptx
https://mentor.ieee.org/802.11/dcn/13/11-13-0632-00-0hew-ultra-high-density-wlan.pptx
https://mentor.ieee.org/802.11/dcn/13/11-13-0657-02-0hew-hew-sg-usage-models-and-requirements-liaison-with-wfa.ppt

## Slide 12
Thank you!