## Slide 1: Potential approach to improve WLAN BSS edge performance
Date: 2013-07-16
Authors:

## Slide 2: Abstract
This presentation presents potential solution to improve BSS edge performance in low and medium SNR condition
  High level scheme
  Simulation results
  Discussion.
Notes: doc.: IEEE 802.11-yy/xxxxr0

## Slide 3: Motivation
In previous presentations have discussed targets for HEW work
  Fairness between BSS center and BSS edge users.
  Improved BSS edge performance.
Additionally document 11-13-545-01 presented significant issues with current standard and implementations based on real network measurements:
  Link adaptation not able to follow channel conditions
  Extremely high number of re-transmissions
Additionally to be able to increase density of the networks it is essential to be able to work effectively at low SNR regions.
  For frequency re-use one networks, operation at zero SNR level is needed.

## Slide 4: Current ARQ protocol
Currently no separation in ARQ protocol between:
  CRC Decoding error due to too low SNR level to decode transmitted packet correctly.
  CRC decoding error due to collision.
  Assumes always that collision occurred and increases the backoff.
  TXOP can support fast packet retransmission with Block ACK, but different transmissions of same data packet are fully independent.
When link is suffering from high system load
  Collisions affect the achieved BLER and link adaptation drives down used MCS to maintain BLER target.
  Effect can be somewhat compensated but it will reduce link adaptation capability to follow channel dynamics.

## Slide 5: PHY Header Robustness
Detection of PHY header can be done at low SNR
  Several dB difference to small packet
  Longer packets would suffer even more.

## Slide 6: HARQ to IEEE802.11
To get HARQ operating receivers need to know which packets
  Are indented for it
  Which packets should be combined together.
Introducing necessary address fields to a new HARQ header part together with MCS indication and control field CRC
  Other fields can be included depending on HARQ scheme.
Transmitted as part of PHY-header with robust manner
  We can actually re-use existing PHY header SIG fields for Control header
Actual data part transmitted with higher MCS decided by the link adaptation protected with MAC packet FCS
  Control header defines who is the transmitter and intended receiver and how to receive data part.
Legacy PHY header part
HARQ
header
CRC
MAC SDU
FCS
MAC header
Example packet format

## Slide 7: HARQ Receiver Operation
Intended Receiver of the packet
  Send ACK frame when both control part CRC and data part FCS decoded correctly
    ACK can re-use current ACK frame
  Send NACK frame when control part CRC received correctly but data part CRC fails
    NACK frame can re-use current ACK frame with minor modifications
    Transmitter retransmits the packet without collision avoidance – Looks like packet segmentation procedure for other STAs
  Send nothing when control part CRC fails – fall backs to normal ARQ operation with collision avoidance
    No increase of residual HARQ BLER due to control part failures
  Combine soft bits of different transmissions before decoding
Other receivers can filter the packet from PHY header.

## Slide 8: HARQ Re-transmission
After receiving NACK Frame
  Retransmission after SIFS, as NACK can keep channel reserved.
  Reduced latency with fast re-transmission.
  Reduced buffering in receiver.
Coding chain between transmissions and re-transmission can be very similar
  Sifting data in frequency domain is a simple way to provide frequency diversity.
  Used in following simulation results.
Different options could be considered
  Data part could be kept self-decodable.
  Different parity bits could be transmitted to provide extra coding gain.

## Slide 9: TXOP with HARQ
Previous slides presented HARQ operation in case of single frame,
  Utilized by all unicast management, control and individual data frames.
In case of TXOP
  Multiple data frames would be transmitted before Block ACK.
  Block Ack frame has capability indicate missing frames which could be re-transmitted in HARQ manner.
  Additionally block ack request, Block ack could benefit from HARQ re-transmissions introducing extra robustness to TXOP.
  Re-transmission can happen inside same TXOP, next TXOP or existing TXOP could be extended.

## Slide 10: Simulation Results Single link, single packet of 2048bytes, CW = 32, No collisions
Chart: Throughput at SNR 3dB
| B | D | F
Baseline | 5.1494 | 6.0486 | 6.6405
HARQ | 7.4823 | 8.2465 | 8.3855
Basline - short CP | 5.5523 | 6.6864 | 6.5318
HARQ - short CP | 8.0283 | 9.1407 | 8.8489
Chart: Throughput at SNR 6dB
| B | D | F
Baseline | 11.0407 | 11.8692 | 12.2482
HARQ | 11.8369 | 12.4113 | 12.7597
Baseline - Short CP | 11.9984 | 13.0119 | 12.8384
HARQ - Short CP | 12.9249 | 13.591 | 13.4269

## Slide 11: Average Gain Single link, single packet of 2048bytes, CW = 32, no collisions
Significant gain at 3dB area.
  Higher gain for short CP in difficult channel.
At 6dB area link adaptation works better and reduces the gain around 5%
  Only 10% of packets being re-transmitted
Our simulations show high gain when larger CW values are used
  Penalty of contention becomes larger.
In real system the channel would be many times reserved at re-transmission
  Baseline throughput would be lower.
  Higher relative HARQ.
Chart: Relative Gain
| B | D | F
3 dB | 0.45304 | 0.36337 | 0.26278
3 dB - Short CP | 0.44594 | 0.36706 | 0.35474
6 dB | 0.072115 | 0.045673 | 0.041761
6 dB - short CP | 0.077219 | 0.044505 | 0.045839

## Slide 12: Conclusion
Hybrid ARQ can provide significant gains in throughput in low SNR conditions resulting improved BSS edge data rates:
  PHY header detection will become limiting factor.
  Decoding error due to low SNR is not penalized
Reduced latency:
  Higher average data rate seen by higher protocol layers
  Fast retransmission without contention
In higher SNR scenarios the throughput gain is less significant,
  Improved robustness to time-varying interference
  Fast recovery from link adaptation error.
  Wider utilization of short CP.
  Receiver may decide to decode re-transmission independently and not use combining.
Next steps:
  Verify system level gains in HEW simulation scenarios
  Consider as one technical option for future HEW work.

## Slide 13: Annex: Simulation parameters
Parameter | Value
Channel Model | B/D/F
Carrier Frequency | 2.4GHz
Channel bandwidth | 40 MHz
Channel estimation | LMMSE
Equalization (SIMO) | MRC
Equalization (MIMO) | LMMSE
Channel code | Convolutional code, number of codecs can vary
Tx modes | STBC
Phase noise | 802.11n spec. [2]
Timing offset | Estimated based on STF,LTF and VHT-LTF (integer number of samples)
Frequency offset | Estimated based on STF and pilot carriers (Uniform +- 20ppm)
Power amplifier | 802.11n spec (Rapp, p=3)
IBO | 8 dB (very close to 8 dB OBO)
Mobile speed | 0 km/h (environment “velocity” 0.089 km/h)
Antenna array | ULA with distance between antennas is λ/2
AGC | Assumes L-STF location known. Similar performance probably achievable with simple STF correlator for low SNR and power ramp detector for high SNR.
Noise variance | Estimated based on null carriers (except DC) of non-VHT portion

## Slide 14: Annex: Simulation parameters
Bandwidth 40MHz
AP/STA have 2 antenna's
SU-MIMO 1 stream (STBC)
For each SNR point 100 fast-fade-drops (FFD) generated, with 100 MSDU transmission per FFD
  100 MSDUs correspond roughly to 1.6 Mb data burst
Simulation per FFD terminated if 100 MSDUs successfully transmitted OR 10 MSDU transmission failures per FFD detected
  We have used maximum number of 7 retransmissions for AP ARQ OR less if 80ms time delay exceeded
MSDU size 2048 Bytes
Non-idealities as in IEEE reference comparison set