## Slide 1: Video Data Rate for HEW
Date: 2013-07-18
Authors:
Name | Affiliations | Address | Phone | email
Huai-Rong Shao | Samsung | 75 West Plumeria Dr., San Jose, CA 95134, USA |  | hr.shao@samsung.com
Chiu Ngo | Samsung | 75 West Plumeria Dr., San Jose, CA 95134, USA |  | chiu.ngo@samsung.com
Sehee Han | Samsung | 416, Maetan-3 Dong, Yeongtong-gu, Suwon-city, Gyeonggi-do, South Korea |  | sehee7.han@samsung.com
SangHyun Chang | Samsung | 416, Maetan-3 Dong, Yeongtong-gu, Suwon-city, Gyeonggi-do, South Korea |  | s29.chang@samsung.com
Hyunjeong Kang | Samsung | 416, Maetan-3 Dong, Yeongtong-gu, Suwon-city, Gyeonggi-do, South Korea |  | hyunjeong.kang@samsung.com
David Xun Yang | Huawei | F1-17, Bantian, Longgang District, Shenzhen 518129, P.R.China |  | david.yangxun@huawei.com
Chaochun Wang | MediaTek | 2860 Junction Ave, San Jose, CA 95134, USA |  | Chaochun.wang@mediatek.com

## Slide 2: Motivation
This presentation explains
  How to calculate the data rate of uncompressed video
  How to estimate the data rate of compressed video

## Slide 3: Data Rate of Uncompressed Video
(Uncompressed video data rate) =
(Video frame Width)*(Video frame Height)*(Bits per pixel)*(Video frames per second)
(Bits per pixel) depends on the (Bit depth per each color element) and video format (4:4:4, 4:2:2 or 4:2:0)
Color depth per each element | Bits per pixel for 4:4:4 format | Bits per pixel for 4:2:2 format | Bits per pixel for 4:2:0 format
8 | 24 | 16 | 12
10 | 30 | 20 | 15
12 | 36 | 24 | 18
16 | 48 | 32 | 24
Note: Traditionally commercial video uses 4:2:0 format, but now 4:4:4 and 4:2:2 video formats are mandated by video interface standards

## Slide 4: Data Rate of Uncompressed Video
Data rate examples
Video name | Width | Height | Bits per pixel | frame rate (Hz) | Video data rate (Gbps)
1080p or Full HD | 1920 | 1080 | 12 | 60 | 1.5
 |  |  | 24 |  | 3
 |  |  | 36 |  | 4.5
 |  |  | 48 |  | 6
 |  |  | 12 | 120 | 3
 |  |  | 24 |  | 6
 |  |  | 36 |  | 9
 |  |  | 48 |  | 12
UHD 4K video | 3840 | 2160 | 12 | 60 | 6
 |  |  | 24 |  | 12
 |  |  | 36 |  | 18
 |  |  | 48 |  | 24
 |  |  | 12 | 120 | 12
 |  |  | 24 |  | 24
 |  |  | 36 |  | 36
 |  |  | 48 |  | 48
UHD 8K video | 7680 | 4320 | 12 | 60 | 24
 |  |  | 24 |  | 48
 |  |  | 36 |  | 72
 |  |  | 48 |  | 96
 |  |  | 12 | 120 | 48
 |  |  | 24 |  | 96
 |  |  | 36 |  | 144
 |  |  | 48 |  | 192
Note: Huawei’s contribution 11-13-0527r2 has a similar table on 4k and 8k video

## Slide 5: Data Rate of Compressed Video
Data rate of compressed video depends on the compression ratio
Two major video application areas
  Pre-stored video such as TV broadcasting and Blue-ray movies
    High compression ratio: can go up to several hundreds (MPEG, H.264 and now HEVC)
    Long latency: Both intra-frame and inter-frame video processing, also multi-frame reference schemes
  Real-time video such as 60GHz display extension
    Low compression ratio: usually at the order of 10
    Low-latency: Mainly intra-frame video processing
Note: currently a lot of Internet video applications like youtube usually use videos with low resolution and low rate

## Slide 6
Thank you!