## Slide 1: Ack Policy for Short MAC Header
Date: 2013-07-13
Authors:

## Slide 4: Response Indication
Response Indication field in the SIG field of the PPDU is used to indicate third party receivers the response frame duration [1]
In current STD, the intended receiver determines its ACK policy based on
  The ACK policy subfield in the QoS Control field of the normal MAC header
  For short MAC Header, currently there is no ACK policy field or indication
In the following we discuss how to indicate ACK policy for frames with short MAC header
  Propose to add an ACK policy bit in the Frame Control field of the short MAC header
* Renamed ACK Indication field as Response Indication to be consistent with Response Indication Deferral mechanism
Response Indication* | Response Type
0 | No Response
1 | NDP Response
2 | Normal Response
3 | Long Response
SIG
MH
Data
FCS

## Slide 5: Ack Policy field
Use one bit of the FC field of the Short MAC Header to indicate ACK policy bit
  Reduce Type field by one bit
A single bit for ACK policy indicates
  Ack and No Ack policy for single (VHT) MPDUs
  Block Ack and Implicit BAR for A-MPDUs*
* A-MPDUs without a Block Ack agreement (such as group addressed frames) indicate No ACK if the ACK policy bit is set to 0
 | B0 B1 | B2 B54 |  | B5 | B6 |  | B7 | B8 | B9 | B10 | B11 | B12 B14 | B15
 | Protocol Version |  | Type | From DS | More Fragments | Power Management |  | More Data | Protected Frame | End of Service Period | Relayed Frame | TID | Ack Policy
Bits: | 2 | 43 |  | 1 | 1 |  | 1 | 1 | 1 | 1 | 1 | 3 | 1
ACK Policy in FC | PPDU type | Ack Policy
0 | MPDU (VHT Single MPDU) | No Ack
1 | MPDU (VHT Single MPDU) | Ack
0 | A-MPDU | Block Ack*
1 | A-MPDU | Implicit BAR

## Slide 6: Straw Poll 1
Do you support to add one Ack Policy bit in the Frame control field for Short MAC header as in slide 5?