## Slide 1: Stacking Tags In LLC Media
Date: 2013-08-12
Authors:

## Slide 2: Abstract
Work now in progress on P802.1Qbz and P802.11ak has shown that the method currently defined in IEEE 802.1Q for adding and removing tags (e.g., the VLAN tag) to frames on LLC media, as opposed to Length/Type media, is untenable. In a proposed new scheme, only the first tag (or the original MSDU, if there is no tag) is encapsulated via LLC. Every following tag, and the original MSDU (if tagged), is Length/Type encoded. As each tag is added or removed, the encapsulation of the next-inner tag or original MSDU is changed.

## Slide 3: Current tagging situation

## Slide 4: Back to basics: The 802.11 Data Frame
IEEE Std 802.11-2011
802.1 mac_service_data_unit (MSDU)

## Slide 5: Back to basics: The 802.3 Data Frame
IEEE Std 802.3-2008
802.1 mac_service_data_unit (MSDU)
PREAMBLE
SFD
DA
LENGTH
/ TYPE
FCS
EXTENSION
SA
MAC CLIENT DATA
Octets
7 1 6 6 2 46-1982 4 var.

## Slide 6: Back to basics: 802.11 Length/Type MSDU
EtherType data (e.g. IP packet):
LLC data (e.g. Bridge Protocol Data Unit [BPDU]):
SNAP:
LENGTH / TYPE
MAC CLIENT DATA
. 2 3 N–3
N
42-42-03
BPDU
LENGTH < 05-DD
LLC, LL ≠ AA-AA
data
LENGTH / TYPE
MAC CLIENT DATA
. 2 3 3 2 N–8
N
AA-AA-03
00-00-00
LENGTH < 05-DD
LLC, LL = AA-AA
OUI or 0
08-00
EtherType or subtype
IP header
data
IP data
TYPE > 05-FF
MAC CLIENT DATA
08-00
IP header
IP data
LENGTH / TYPE
MAC CLIENT DATA
. 2 M

## Slide 7: Back to basics: 802.2 LLC MSDU
EtherType data (e.g. IP packet):
LLC data (e.g. Bridge Protocol Data Unit [BPDU]):
Other SNAP:
MSDU
3 M
42-42-03
BPDU
LLC, LL ≠ AA-AA
data
MSDU
3 3 2 M
AA-AA-03
PQ-RS-TU
LLC, LL = AA-AA
OUI
WX-YZ
subtype
proprietary protocol
data
MSDU
3 3 2 M
AA-AA-03
00-00-00
LLC, LL = AA-AA
0
08-00
EtherType
IP header
data
IP data

## Slide 8: Old tagging process IEEE Std 802.1Q-2011
Length/Type no tag:
Length/Type tagged:
LLC no tag:
LLC tagged:
MAC CLIENT DATA
MSDU
. 2 N–2
LENGTH / TYPE
MSDU
3 M–3
LLC
data
EtherType
MAC CLIENT DATA
81-00
MSDU
. 2 L 2 N–2
LENGTH / TYPE
Tag value
02-44
MSDU
. 6 2 L 3 M–3
LLC
data
EtherType
81-00
Tag value
02-44
SNAP
AA-AA-03-00-00-00
Simply add or remove tag; MSDU is unchanged.
Simply add or remove tag; MSDU is unchanged.

## Slide 9: Old tagging process IEEE Std 802.1Q-2011
On LLC media, the first 3 bytes following every tag are LLC.
On Length/Type media, the first 2 bytes following every tag are a Length/Type.
You know how to decode the whole frame, because you know whether the medium is LLC or Length/Type.

## Slide 10: Why that is a problem

## Slide 11: The end-to-end tag stacking problem
B5
B4
B3
B2
E1
E2
data
Q
CA
data
Q
S
CA
B2
data
Q
S
CA
BA
I
data
Q
S
CA
BA
I
data
Q
S
CA
BA
I
data
Q
S
CA
data
CA
LLC tags
Length/Type tags
Notes: Decoder ring: BA = Backbone Addresses, I = I-tag, CA = Customer Addresses, S = Service VLAN tags, Q = Customer VLAN tags.

## Slide 12: The end-to-end tag solution
Tagging near the edges of the network must be in the format expected by the medium in that area.
  Otherwise, they cannot decode the tag stack.
  We cannot, ex post facto, require every bridge and tag-aware end station to start translating between encapsulations.
We could ask the bridge that connects to two media types to convert all tags and the original MSDU.
  That is difficult to do in high speed in ASICs.
  It makes it impossible to deploy new tags at the edge, because the core devices will not know how how long those tags are.
  It is a fundamental violation of the principles of layering.

## Slide 13: New proposal for tagging

## Slide 14: New tagging process P802.1Qbz Draft 1.2
Length/Type no tag:
Length/Type tagged:
LLC no tag:
LLC tagged:
MAC CLIENT DATA
MSDU
. 2 N–2
LENGTH / TYPE
MSDU
3 M–3
LLC
data
EtherType
MAC CLIENT DATA
81-00
MSDU
. 2 L 2 N–2
LENGTH / TYPE
Tag value
02-44
MSDU
. 6 2 L 2 N–2
EtherType
81-00
Tag value
02-44
SNAP
AA-AA-03-00-00-00
Simply add or remove tag; MSDU is unchanged.
Change MSDU when adding or removing a tag.
MAC CLIENT DATA
LENGTH / TYPE

## Slide 15: LLC tagging process P802.1Qbz Draft 1.2
0
Add/remove tag on SNAP frame
Add: Convert old outer item LLC  L/T, add LLC tag.
Remove: Delete LLC tag, convert new outer item L/TLLC.
OR: Add/remove tag between LLC-SNAP and MSDU.
Untagged MSDU
3 3 2 M
AA-AA-03
00-00-00
LLC, LL = AA-AA
0
08-00
EtherType
IP header
data
IP data
Untagged MSDU
3 3 2 L 2 M
AA-AA-03
00-00-00
LLC, LL = AA-AA
0
08-00
EtherType
IP header
data
IP data
EtherType
81-00
Tag value
02-44
TAG
Tagged MSDU

## Slide 16: LLC tagging process P802.1Qbz Draft 1.2
Add/remove tag on LLC frame
Add or remove both the LLC tag and the Length field.
3 3 2 2 2 3 M
AA-AA-03
00-00-00
LLC, LL = AA-AA
0
EtherType
88-A8
Tag value
02-44
TAG
Tagged MSGU
Untagged MSDU
3 M
42-42-03
BPDU
LLC, LL ≠ AA-AA
data
Untagged MSDU
42-42-03
BPDU
LLC, LL ≠ AA-AA
data
Length
M+3

## Slide 17: The net effect
Multiple tags on Length/Type (802.3) frame:
Multiple tags on LLC (802.11) frame:
Only the first item is LLC-encoded on an LLC medium; all other items are Length/Type-encoded.
(An untagged MSDU is LLC or Length/Type, by medium.)
Length/Type MSDU
Length/Type Tag 3
Length/Type Tag 2
Length/Type Tag 1
Length/Type MSDU
Length/Type Tag 3
Length/Type Tag 2
LLC SNAP Tag 1

## Slide 18: The end-to-end tag solution
We keep the whole stack, except for the outermost item, in Length/Type format.
Every device knows how to encode/decode frames.
Only one item is converted per tag added or removed.
The outermost item still follows the rules for the medium in question.
We could equally well have used the LLC format in all except the outermost item, except that 802.3 devices already use multiple tags and (as far as this author knows) 802.11 devices do not use LLC-stacked tags.

## Slide 19: A plea
If any actual use of the LLC-stacked tag format is known, please let TGak know about it, because we propose to make this format “illegal”.
If there is such a use, then we have to re-examine our options.
Slide 19
Norman Finn, Cisco Systems
. 6 2 L 6 2 M
EtherType
81-00
Tag value
02-44
SNAP
AA-AA-03-00-00-00
08-00
EtherType
IP header
data
IP data
SNAP
AA-AA-03-00-00-00