## Slide 1: Payload Format / Tag Stacking Change
Date: 2013-09-17
Authors:

## Slide 2: Abstract
This presentation discusses payload encoding and the conversion thereof in relation to P802.11ak.

## Slide 3: Background
802.11 and the rest of the world use different frame payload encodings. 802.11 uses LLC (LSAP-LSAP-Control format) encoding while the rest of the world uses Length/Type format encoding.
This is not a problem for simple payloads as usually occur at the edge of the network. But, in the general case of a payload with multiple tags (VLAN, congestion, security, proprietary, etc.), including future tags yet to be defined, it is not possible to convert from one to the other which might be required on entry to or exit from an 802.11ak link.
To fix this requires a frame format change, at least under some circumstances.

## Slide 4: The Question:
The diagram below is from 802.11-2012 Table P-3.
Does anyone use this format? Or any other cases of stacked SNAP/LLC encoding? If so, please tell TGak.
Some proposed solutions to the problem on the previous slide prohibit the use of this encoding.
Two SNAPs
No Length/Type
Slide 4
Norman Finn, Cisco Systems
. 6 2 L 6 2 M
EtherType
81-00
Tag value
87-65
SNAP
AA-AA-03-00-00-00
08-06
EtherType
IP ARP packet
data
SNAP
AA-AA-03-00-00-00

## Slide 5: References
For further discussion of this topic, come to the TGak session tomorrow, Thursday, AM1.
More detailed discussion of some aspects of these issues is in document 11-13/0952r2.
The current text of P802.1Qbz Draft 1.3 contains a new tag stacking scheme. P802.1Qbz has passed Task Group Ballot with no “Disapprove” votes.