## Slide 1: EDCA Enhancements for HEW
Date: 2013-09-15
Authors:
Name | Affiliations | Address | Phone | Email
Hui Zhao | BUPT |  |  | hzhao@bupt.edu.cn
Juwo Yang | BUPT |  |  | yangjuwo@163.com
Giuxia Kang | BUPT |  |  | gxkang@bupt.edu.cn
Weixia Zou | BUPT |  |  | zwx0218@bupt.edu.cn
Guanglong Du | BUPT |  |  | guanglong108@sina.com

## Slide 2: Abstract
With the development of throughput in WLAN, many new kinds of data packets will flow through WLAN networks.
This presentation discusses the enhancement of EDCA and propose an auxiliary parameter and a hierarchical scheduling model to deal with new situations.

## Slide 3: Background(1/2)
HEW address “improving real world performance”
  Parameterized and guaranteed QoE may be a solution
Today only the IEEE 802.11e std. is available
  HCCA for parameterized QoS
  EDCA for differentiated QoS
IEEE 802.11e EDCA defines traffic classes to classify packets of 4 Access Categories.
  AC_BK is the lowest priority for background data
  AC_BE is the next priority for best-effort data
  AC_VI is the priority for video applications
  AC_VO is the priority for voice applications
The packets for the same AC are enqueued in FCFS queue with drop tail technique (EDCAF).
Notes: HCCA

## Slide 4: Background(2/2)
In the HEW system data traffic, except bulky data, there are still many short packets. They may be minor part of total data volume, but major amount of data packets[1]
  While 4K&8K/Ultra-HD supported, there are also many 360P/480P video.
  Some users are BitTorrent downloading, others may check their e-mail or Facebook.
The original EDCA do not differentiate detail property of the data packets in the same AC. So it may be unfair for the short packets.

## Slide 5: Hierarchical Scheduler
We propose to add an auxiliary parameter AAC (auxiliary access categories) to each packet after the AC parameter, to make the EDCA more flexible in dealing with diversity of packets.
  The AACs are depending on the detail properties of the packet, like length, delay, type of service etc.
And in each AC, an extra scheduler is added for different AACs, to make each AAC flow has a appropriate throughput.
  Detail scheduler algorithm TBD.

## Slide 6: Hierarchical Scheduler Procedure(1/2)
The eligible packet must pass through hierarchical scheduling levels:
  Step 1: H-EDCA receives the packets from the upper layer, then classifies the packets into 4 classes as defined in EDCA specifications.
Former EDCA Reference Implementation Model
IP Network Layer Interface
8 Priorities Classified in 4 Access Categories
AC3
AC2
Original Scheduler(level two)
AC1
n Flows Divided by AAC
Qn
Q0
……
Added Scheduler(level one)
AC0
Attempt to transmit and access channel
……
……
……

## Slide 7: Hierarchical Scheduler Procedure(2/2)
  STEP 2: In each AC, it divides the packets into n flows depending on AAC of each packet. Define one queue for each flow.
  STEP 3: For dequeueing, an added scheduler (level one) will serve the packet queued at the head of queue of each AAC.
  STEP 4: These eligible packet at each AC wait their backoff and AIFS, depending on there AC, depending on their AC priority (level two).
Then the node attempts to transmit the eligible packet
IP Network Layer Interface
8 Priorities Classified in 4 Access Categories
AC3
AC2
Original Scheduler(level two)
AC1
n Flows Divided by AAC
Qn
Q0
……
Added Scheduler(level one)
AC0
Attempt to transmit and access channel
……
……
……

## Slide 8: Simulation(1/2)
We assume that in a given AC, there are 4 kinds of packets for example.
  ACC 0 for packets below 100 bytes
  ACC 1 for packets between 100 to 2000 bytes
  ACC 2 for packets between 2000 to 10000 bytes
  ACC 3 for packets above 10000 bytes
The packets are transmitted by original EDCA and Hierarchical Scheduler respectively, during 1ms with the total transmission rate of 1Gbps (1Mbits=1Gbps*1ms).
In original EDCA, FCFS is used.
Original EDCA
1Mbits

## Slide 9: Simulation(2/2)
In the Hierarchical Scheduler, WFQ (Weighted Fair Queuing) is used for example.
Hierarchical Scheduler
Compared with original EDCA, the Hierarchical Scheduler can do better with the bursty short packets.
The Hierarchical Scheduler may be more flexible according to the ACC setting
1Mbits

## Slide 10: Suggestion
Suggestion 1: The Auxiliary Access Categories and Hierarchical Scheduler model might be considered in HEW, due to the diversity of packets.
  The detail parameter setting and scheduler algorithm may be studied in the future.
Suggestion 2: The enhancement of EDCA needs to be considered in future discuss to deal with new traffic models in HEW.

## Slide 11: References
[1] 11-13-0728-01-0hew-network-optimization-for-expected-traffic-patterns
[2] Abuzanat, H. ; Trouillet, B. ; Toguyeni, A. “FQ-EDCA: An extension of EDCA to improve fairness in ad-hoc wireless network”. Computers & Industrial Engineering, 2009. CIE 2009. pp.1617-1622