## Slide 1: HEW SG Simulation Scenarios
Date: 2013-09-15
Authors:

## Slide 2: Abstract
This presentation gives a supplement to the existing simulation scenarios, and proposes a modified set of unified simulation scenarios for further evaluation.

## Slide 3: Summary of Existing Proposals
Contribution [1] summarizes all existing proposals related to simulation scenarios, and proposes a mapping between usage models and typical scenarios
  A unified set of simulation scenarios was proposed
    Three scenario categories: Residential, Enterprise/hotspot, Large BSS
  The mapping between usage models and simulation scenarios was defined

## Slide 4: Mapping (1)
Contributions [1-3] propose to map directly various usage models to simulation scenarios. This is similar to the method in TGn [4]
  TGn uses many-to-many and one-to-one mappings between usage models and simulation scenarios
    Mandatory/ Residential IBSS/ Large Enterprise/ Conference Room/ Hot Spot/ Mix-Mode BSS/ Co-channel Legacy BSS

## Slide 5: Mapping (2)
Following the mapping in our previous proposal [3], we propose to have four scenario categories:
  Enterprise
  Residential
  Indoor Hotspot
  Outdoor Hotspot

## Slide 6: Mapping (3)
Based on the contribution [1], the relationship between usage model and our proposed scenario categories is shown as follows:
Usage Model |  |  |  | Mapping
1 | high density of APs and high density of STAs per AP | a | Stadium | Indoor Hotspot
 |  | b | airport/train stations | Indoor Hotspot
 |  | c | exhibition hall | Indoor Hotspot
 |  | d | shopping malls | Indoor Hotspot
 |  | e | E-Education | Enterprise
 |  | f | Multi-media Mesh backhaul | Enterprise/Indoor hotspot
2 | high density of STAs – Indoor | a | dense wireless office | Enterprise
 |  | b | public transportation | Indoor Hotspot
 |  | c | lecture hall | Enterprise
 |  | d | Manufacturing Floor Automation | Enterprise
3 | high density of APs (low/medium density of STAs per AP) – Indoor | a | dense apartment building | Residential
 |  | b | Community Wi-Fi | Indoor Hotspot
4 | high density of APs and high density of STAs per AP – Outdoor | a | Super dense urban Street | Outdoor Hotspot
 |  | b | Pico-cell street deployment | Outdoor Hotspot
 |  | c | Macro-cell street deployment | Outdoor Hotspot

## Slide 7: Mapping (4)
When compared with the scenario categories proposed in [1], we consider “Large BSS” to be a subset of Outdoor Hotspot (dense deployment in street)

## Slide 8: Outdoor Hotspot
Dense deployment in streets model has relevance to Outdoor Hotspot
The scenario of dense deployment in streets follows the result discussed in 3GPP TR36.872 for deployment of micro-cells
  AP deployment depends on the topology, especially for hotspot in streets
  It is hard to say what type of regular distribution of AP is most typical
  The difference of random location and regular location of APs is minor
We propose the scenario of outdoor hotspot to follow the settings in 3GPP TR36.872 where APs are randomly distributed in each cluster

## Slide 9: Our Proposal
We propose to use the following 4 categories and typical scenarios:
  Note: All the scenarios except residential should be manageable.
Scenario Category | Typical Scenario | Environment | AP Deployment | User Distribution
Enterprise | Dense Wireless office | Indoor | Planned | Clusters with random distribution inside
Residential | Dense apartment building | Indoor | Unplanned | Random inside the cluster (each apartment is a cluster)
Indoor hotspot | Airport/train stations | Indoor | Planned | Uniformly distributed
Outdoor hotspot | Dense deployment in streets | Outdoor | Unplanned | Uniformly distributed in each BSS

## Slide 10: Summary
This presentation proposes 4 scenario categories, discusses on the recommendation of the settings of AP and STA deployment of Outdoor Hotspot, and proposes a mapping between usage models and simulation scenarios

## Slide 11: Straw Poll
Do you agree with the table of the simulation scenarios in slide 9?
  Y
  N
  Abs

## Slide 12: References
[1] 11-13/1000r0 Simulation Scenarios
[2] 11-13/0723r1 HEW SG Evaluation Methodology Overview
[3] 11-13/0786r0 HEW SLS Methodology
[4] 11-03/0802r23 Usage Models