## Slide 1: HEW SG Progress Review
Date: 2013-09-15
Authors:

## Slide 2: Abstract
This submission summarizes HEW SG progress up-to-date.

## Slide 3: Overview
HEW SG was approved by the IEEE 802 EC in March 2013 and had its first meeting in May 2013.
Reaction to the newly formed SG has been overwhelming.
  Over 60 submissions presented and discussed during the first two meetings (May and July 2013).
    Covering usage models, functional requirements, technologies, evaluation methodologies and simulation models.
  Compared to ~12 submissions during the VHT first two meetings (May and July 2007)
... However

## Slide 4: SG Main Task
The normal function of a SG is to draft a complete PAR and five criteria (see rules5) and to gain approval for them from the 802.11 WG – (11-13/0001r2).
  Agree on a project scope.
  Demonstrate feasibility (technologies exist to achieve the scope) – 5C
Not too many submissions addressing what the problem we are trying to solve is.
  Need to be more specific on the problem space.
  Need to solicit more submissions that assist in drafting the PAR.
  How do we see the work in HEW progressing toward a TG?

## Slide 5: Example PAR Scopes
TGac PAR:
  This amendment defines standardized modifications to both the 802.11 physical layers (PHY) and the 802.11 Medium Access Control Layer (MAC) that enable modes of operation capable of supporting: o A maximum multi-station (STA) throughput (measured at the MAC data service access point), of at least 1 Gbps and a maximum single link throughput (measured at the MAC data service access point), of at least 500 Mbps. o Below 6 GHz carrier frequency operation excluding 2.4 GHz operation while ensuring backward compatibility and coexistence with legacy IEEE802.11 devices in the 5 GHz unlicensed band.
TGah PAR
  This amendment defines an Orthogonal Frequency Division Multiplexing (OFDM) Physical layer (PHY) operating in the license-exempt bands below 1 GHz, e.g., 868-868.6 MHz (Europe), 950 MHz -958 MHz (Japan), 314-316 MHz, 430-434 MHz, 470-510 MHz, and 779-787 MHz (China), 917 - 923.5 MHz (Korea) and 902-928 MHz (USA), and enhancements to the IEEE 802.11 Medium Access Control (MAC) to support this PHY, and provides mechanisms that enable coexistence with other systems in the bands including IEEE 802.15.4 and IEEE P802.15.4g. The data rates defined in this amendment optimize the rate vs range performance of the specific channelization in a given band. This amendment also adds support for: -transmission range up to 1 km -data rates > 100 kbit/s
PAR scope should be clear in defining the problem we are trying to solve and its boundaries.

## Slide 6: Possible PAR Topics
Band: 2.4/5 GHz, others
Layer: MAC and PHY enhancements
Technology
Goal(s): spectrum efficiency (rate), area throughput, etc.
Targets:
Constraints: what is the problem space?
Etc.

## Slide 7: Topics Covered
Usage Models.
  The SG has already concluded its Usage Models discussion and waiting for WFA feedback
Measurements and deployment experience
Evaluation Methodologies and Simulation Models
  Significant amount of the SG effort is spent on this topic.
  Is there the intention to use these models during SG discussion?
  How much will we be able to achieve in the SG, given the timeline?
Functional Requirements
  Helpful
PHY/MAC technologies
  Necessary to demonstrate feasibility

## Slide 8: Evaluation Methodologies and Simulation Models
The need for system simulations.
  In addition to PHY link simulations
Simulation models should be related to usage cases.
Make use of 802.11n and 802.11ac with appropriate modifications.
Traffic models definition.
PHY and MAC parameters.
Indoor and Outdoor models
Channel models.
Average and 5%CDF performance measures. Area throughput, STA throughput, QoE measures, etc.

## Slide 9: PHY/MAC Technologies
Use of beamforming to enhance cell edge performance
Full-Duplex technology
HIPERLAN channel access mechanism
Small BSS deployments
HARQ
OFDMA

## Slide 10: Timeline
May 2013
  Initial meeting
July 2013
  Presentations
  SG Extension
Sept 2013
  Presentations
Nov 2013
  Presentations
  Initial PAR and 5C
  SG Extension
Jan 2014
  Presentations
  Final version of PAR and 5C
  WG Approval
March 2014
  Presentations
  EC Approval
May-June 2014
  Nescom approval
July 2014
  TG starts

## Slide 11: References