## Slide 1: Report on LB198 on TGai Draft 1.0
Date: 2013-09-15
Authors:

## Slide 2: Abstract
Report on WG LB198 on TGai D1.0

## Slide 3: Official Outcome of LB198 on TGai Draft 1.0
Votes:
  334 eligible people are in this ballot group.
    147 affirmative votes
    51 negative votes
    6 negative vote without comments
    22 abstention votes
    ===
    226 votes received = 67.7% valid returns = 9.7% valid abstentions
  This ballot has met the 50% returned ballot requirement
  This ballot has met the less than 30% abstention requirement
  APPROVAL RATE:
    146 affirmative votes = 74.2 % affirmative
    51 valid negative votes = 25.8 % negative
    The 75% affirmation requirement has not been met,
    Motion Fails.
Comments: 1389total
  68 General
  696 Technical
  625 Editorial

## Slide 4: Received Comments: Excerpt
Disclaimer:
  The cited comments are chosen as it was believed that they represent ‘major technical issues’ and dissent from concepts and ideas included in TGai draft.
  Addressing those comments is likely to involve some major effort.
  Other comments address very important issues as well but do not indicate dissent from the actual intend / technical idea. Resolving those comments may require tremendous work as well.
  The excerpt shall not be taken as a representative representation of the received comments nor as a judgment on the importance or validity of any comment.

## Slide 5: General
Inconsistent Conformance Language - Section 1.4 of IEEE 802.11-2012 describes the word usage for specific terms, namely "shall", "should", "may" and "can". Many sections of this proposed amendment do not use any of these terms, so it's impossible to determine which are normative requirements and which are not. there are far too many to list in individual comments. This conformance language is necessary in order for a manufacturer or conformance test organization to write a test plan and verify conformance of a product to the specification. This is necessary to ensure interoperability amongst various implementations and products.  Define the specific requirements for conforming to this specification by use of "shall", "should", "may" or "can" in all sections where a specific requirement is needed.
An editorial note says "changes made by 802.11ad and other preceding amendments will be reflected in later drafts". I have no objection to this note per se; I object to submitting 802.11ai to sponsor ballot without including the effects of changes in 802.11ad.
Editor note that the draft is not in compliance tells the TG that it should have waited to start the LB until it had incorporated all the preceding ammendments. I understand the need to make progress, but the initial draft should have been based on all the preceding amendments to ensure changes noted in D1 do not have unintended consequences to text that may have been changed by other amendments
The draft is based on P802.11ad-2012 (among others) but fails to account for .11ad changes. Specifically, scanning procedures in 10.1.4.3.2 and 10.1.4.3.3 make no mention of directional multi-gigabit (DMG) devices. Presumably, it is not the intention of the amendment to preclude DMG STAs from performing active scanning.
This draft ignores changes made by previous amendments to the 802.11 text. For example, all the changes made by 11ad in 10.1.4 are not captured.
11ai follows 11ac, it should take into account changes that will be made to the standard by the time it passes sponsor ballot [ref. To Cls 11.11.2.5]  Reflect your baseline and show all changes from prior amendments.  Either incorporate the changes .11ad made to active scanning subclauses into the proprosed ai amendment, or carve out the DMG STA active scanning procedures into a separate subclause.  Clarify if the mechanism of 11ai are relavent to .11ad devices and how.  Properly reflect content from your baseline.  Update the draft to include all the current amendments that are ahead of this amendment.The recirculation ballot should be delayed until it is confirmed to have included the preceding amendments.
Missing merge of text from Tgai (Cls. 8.4.2.176)

## Slide 6: General (2)
This amendment sometimes uses the same name for a value and for an element that contains that value. Therefore the identity of the object behind each name must be stated explicitly  Insert "element" after "Parameters" on line 12, after "Time" on line 15 and after "Count" on line 17.
This is a huge frame to be transmitted in the beacon !! What is the maximum size of this element? It breaks the whole GAS/ANQP model, which was designed to provide information to the STA prior to association, so that beacon bloat could be avoided. Please use the ANQP-element Neighbor Report element instead.  Use the ANQP-element neighbor report instead. Alternative create an ANQP-element reduced neighbor report.
How will multiple higher layer packets fit into a single Element? [note not part of the comment: this seems to mean to abandon the piggy backing concept]
In the 802.1 architecture, "higher layer packets" are MSDUs and encapsulated in Data frames. There is no text is this amendment that describes when, how or why MSDUs would be encapsulated in a FILS Higher Layer Encapsulation frame. It also makes absolutely no sense to encapsulate MSDUs in management frames.  Remove all FILS Secure Container TLVs except KEY RSC and GTK. Send the higher-layer data in normal data frames after association  Remove subclause 8.5.24.1
ILS synchronization subfield does not serve any practical purpose, as there are no peak assocation times observed in the field. See submission 13/906r0 for analysis of real world data.  Adopt submission 13/907r2

## Slide 7: General (2)
I don't believe the mandatory requirements placed on FILS non-AP STAs are resonable given the minimal reduction in management traffic this procedure can expect to achieve. I am particularly concerned that if I wish to implement "FILS authentication" in my product that I will also need to implement this completely unrelated feature. Note that I would be required to implement this in my FILS non-AP STA device even if no APs out there that supported the feature. [ref. To Cls 10.44.6.2]  Create a new class of device for which this procedure is required. The shall requirements can then be placed on that class of device instead of all FILS devices. Alternatively, remove the feature from the spec.
FILS should be able to function at the concurrently with Fast BSS-Transition. An FT-capable device should be able to use FILS between ESS's and FT between BSS's.  Add the protocol elements and derivations necessary to allow FILS to work with Fast BSS-Transition.
Lack of MIB modification in Annex C.
Annex C is a disaster zone. The following work needs to be done: 1. Assign these definitions to objects - e.g. choose between smt, mac or phy 2. Insert <ANA> flags for managed namespaces 3. Correct the syntax for the definition of thse objects (part of step 1.) 4. Create a group for FILS objects 5. Add dot11FILSActivated to dot11SMTbase and up-rev it. Update the dot 11 compliance statement to use the new rev. 6. Create a compliance statement for FILS and cite the FILS group as mandatory in this compliance statement. 7. (probably later, but certainly before MDR completes) compile the MIB and fix any compilation errors.

## Slide 8: Security
Within the definition of certificate authority what does 'etc.' refer to?  Definitions should not use 'etc.' as this implies unknown examples where the definition may apply. These examples are in the author's mind and not within the reader's.
Definition of TTP is too vague and lacks context. Does the security associaion with the two need to be maintained at the same time?
What does this new exception entail? This could break the existing security association state machine, as the 802.1X Controlled Port could be left open. At some point in this amendment a modified controlled port state machine figure is required.  Add a note explaining what is and is not 'applicable'. In other words, a short explanation of the new circumstances under which the 802.1X Controlled Port is not closed. Add a new Figure showing the state machine of the controlled port, with an additional state showing when the Controlled Port is not closed and how the state transitions to 'closed port'.
What does trusted mean? Where does the 3rd party exist within the IEEE 802.11 architecture. Is it within the BSS or the ESS?  Add some text (or a new definition) to explain the term trusted. Add new text or a Figure, showing the typical architecture of where the trusted third party resides within the BSS or ESS.
"Exchange of messages (method, procedure, format and content) between AP/Authenticator and the trusted third party is out of scope of this specification" is inconsistent with the statement on P99L42: "When a trusted third party is used for FILS authentication, then EAP-RP as defined in [IETF RFC 5295/6696] shall be used"  Either remove the out of scope statement or remove the requirements for EAP-RP.

## Slide 9: Security (2)
When TTP authentication is used, how does the STA know that both it and the AP share the same TTP? So there are really three identities involved: the non-AP STA, the AP and the TTP. In order to protect its identity, it is necessary for the STA to know that it shares a TTP with the AP before shares its identity otherwise it would be sharing identity with a device it may not trust. Also, what happens in the case where a STA (and AP) have multiple TTPs? Do they each try all possible identity combinations in the hope that one validates?  Define the mechanism by which the the STA determines that both it and the AP share the same TTP.
Fixed nonces, mistake.  Adopt AEAD scheme in 11-13/0806r2
The relationship between "FILS authentication" and EAP-RP is as clear as mud. How does the EAP-RP protocol fit with the FILS authentication handshake? It seems that the spec is trying to do three things: 1. Define reduced overhead handshake for simple PSK that has nothing to do with EAP-RP, 2. define a reduced overhead handshake for re-authentication using EAP-RP following full EAP-RP authentication using 802.1X messaging 3. Trusted 3rd party certificate-based authentication that has nothing to do with EAP-RP. It seems that different parts of the spec have been written with different assumptions regarding the security model. All are lumped under "FILS authentication". What exactly is FILS authentication? Is it the security model or the reduced handshake? The security minds in this task group need to meld and come up with language that makes all this clear. My suggestion woud be to place the three autheticaiton methods either in separate sections or in existing clauses. For example, 4.10.3.3 (AKM operations with Password or PSK) could describe two handhakes: the exiting 4-way handshake and the new FILS handshake.

## Slide 10: References
11-13-1076-00-00ai-TGai-LB198-comments-for-Draft-1-0
Mail official result LB198 (From: Bruce Kraemer <bkraemer@MARVELL.COM> Subject: [STDS-802-11] Results of WG LB#198 regarding 802.11ai D1.0Date: 15 September 2013 14:13:48 GMT+08:00To: STDS-802-11@LISTSERV.IEEE.ORG)