## Slide 1: Discussion on HEW Functional Requirements
Date: 2013-09-15
Authors:

## Slide 2: Introduction
In the previous meeting, several contributions from [1] to [4] discussed about functional requirements considering
  AP and STA density
  Indoor and outdoor channel environment
  And more requirement like backward compatibility
Functional requirements can be categorized as two aspects
  System-perspective requirements
  User-perspective requirements
This contribution discusses about functional requirements focusing on “User-perspective”

## Slide 3: System-perspective requirements
System-perspective requirements are categorized as follows:
  Throughput averaged over unit area
    bps/Hz/unit area or bps/unit area
    called as ‘area throughput’, ‘aggregated BSS throughput per area’, or etc
  Throughput averaged over BSS
    bps/Hz/BSS or bps/BSS
    called as ‘average throughput per BSS’, or etc
One candidate baseline: area throughput [5]
  One of unique metrics to identify HEW
  Captures well most of use cases in high dense environment [6]

## Slide 4: Motivation on user-perspective requirements
As Wi-Fi usage in CE devices is increasing, quality of experience (QoE) of each user becomes dominant
  70% of mobile users use Wi-Fi for data traffic [7]
An end user is interested in not system-perspective performance, but user-perspective performance
  Even though system performance is good, there might be users feeling ‘bad’, e.g.
  Some fixed users with continuous bad-channel/interference condition
  Some users moving back and force across small BSSs
  If they don’t feel good at Wi-Fi, they usually complain to device vendors
System-wise feather alone can not fully reflect user fairness and throughput distribution
  e.g. (Total transmitted bits to MAC SAP at all APs/STAs) / time / m2

## Slide 5: Proposed metrics for user-perspective requirements
From the perspective of user throughput
  Minimum throughput per STA
    How can we guarantee it in contention-based Wi-Fi?
  Suggested metric: Average 5th percentile user throughput
    Observed by 5th percentile point of throughput CDF
    Counts for BSS edge-user performance as well as performance in bad channel conditions
    Usually used in cellular network and considerable in high-dense Wi-Fi
  Suggested metric: Average throughput per STA
    Directly derived by dividing average throughput per BSS or areal throughput by the number of STAs in a given condition
From the perspective of delay/latency
  Minimum delay/jitter, average access delay, number of active real-time service users, etc
    One of important terms for QoE
    But, need to discuss more how to define and quantize

## Slide 6: Conclusion
Main goal of HEW changes from legacy standards
  More interest in ‘average’ system-perspective performance in ‘real’ world than ‘maximum’ performance in ‘ideal’ world
In addition, there is increasing needs to enhance quality of experience (QoE) from user-perspective
HEW should capture both system-perspective and user-perspective requirements, and candidate metrics are:
  Area throughput
  Average 5th percentile user throughput
  Average throughput per STA

## Slide 7: Reference
[1]13/0787 “Followup on Functional Requirements”, Wu Tianyu (Huawei)
[2]13/0850 “Quantitative QoE Requirements for HEW”, Huai-Rong Shao (Samsung Electronics)
[3]13/0840 “HEW functional requirements follow-up”, Minho Cheong (ETRI)
[4]13/0798 “Functional requirements in HEW”, Jinsoo Choi (LG Electronics)
[5] 13/1097 “Functional requirements for the HEW PAR”, Minho Cheong (ETRI)
[6] 13/0657r6 “Usage models for IEEE 802.11 High Efficiency WLAN study group (HEW SG) – Liaison with WFA”, Laurent Cariou (Orange)
[7] “Understanding today’s smartphone user: Demystifying data usage trends on cellular & Wi-Fi networks,” Mobidia, Feb. 27, 2012”

## Slide 8: Appendix: Discussed functional requirements & metrics from [1] to [4]
 | [1] | [2] | [3] | [4]
Quality of user experience | - Delay, packet loss | Minimum average data rate Maximum connection setup delay Maximum packet transmission delay Maximum information unit transmission delay | Agreed on this metric | - Minimum per device throughput Average access delay Average round trip delay X number of active real-time service users
Area throughput | Agreed on this metric |  | - Aggregated BSS throughput per area | Agreed on this metric
Spectrum efficiency | (suggest to replace it by below requirements) |  | Maximum single/multi-STA spectral efficiency (spectrum widening aspect) | - Maximum single/multi-STA throughput
Others | - MAC efficiency - Throughput of AP |  | - Backward compatibility /coexistence - Maintaining 802.11 user experience | - Performance reliability in outdoor